## Slide 1: SUBELEMENT T2 [3 Exam Questions - 3 Groups]
Operating Procedures
Notes: <number>
2010 Technician Class (Element 2) Master syllabus
Released 1 February, 2010
396 questions in 35 sections
These slides are free to use and are available from http://www.microhams.com. Changes are allowed if Microhams branding is left in place (feel free to ad your own). Any content additions should be forwarded to the author, Scott N7SS at N7SS@arrl.net so they can be rolled into future versions and available for everyone.

## Slide 2: T2 – Operating Procedures
<number>
Microhams 2010 Technician
T2A - Station operation; choosing an operating frequency, calling another station, test transmissions, use of minimum power, frequency use, band plans
T2B - VHF/UHF operating practices; SSB phone, FM repeater, simplex, frequency offsets, splits and shifts, CTCSS, DTMF, tone squelch, carrier squelch, phonetics
T2C -Public service; emergency and non-emergency operations, message traffic handling

## Slide 3: Common Abbreviations
Operating Practices
<number>
CQ Call Any Station
RST Readability, Signal Strength, Tone
DX Distance, foreign country
73 Best Regards
DE From, this is
PTT Push To Talk
VOX Voice Activated Switch

## Slide 4: ITU Phonetic Alphabet
Operating Practices
<number>
Agreed upon words to represent the letters of the “roman alphabet”.
The boldfaced syllables are emphasized. The pronunciations shown in this table were designed for those who speak any of the international languages.
The pronunciations given for “Oscar”, “Papa” and “Victor” may seem awkward to English-speaking people in the US.
A Alfa AL FAH
B Bravo BRAH VOH
C Charlie CHAR LEE
D Delta DELL TAH
E Echo ECK OH
F Foxtrot FOKS TROT
G Golf GOLF
H Hotel HOH TELL
I India IN DEE AH
J Juliet JEW LEE ETT
K Kilo KEY LOH
L Lima LEE MAH
M Mike MIKE
N November NO VEM BER
O Oscar OSS CAH
P Papa PAH PAH
Q Quebec KEH BECK
R Romeo ROW ME OH
S Sierra SEE AIR RAH
T Tango TANG GO
U Uniform YOU NEE FORM
V Victor VIK TAH
W Whiskey WISS KEY
X X-Ray ECKS RAY
Y Yankee YANG KEY
Z Zulu ZOO LOO

## Slide 5: Repeater Operation
Station Setup and Operation
<number>
60+ miles
Output Freq
145.21 MHz
Input Freq
144.61 MHz
Offset
- 600 kHz

## Slide 6: Repeater Input/Output Offsets
Station Setup and Operation
<number>
Band Offset
6 meters 1 MHz
2 meters 600 kHz
1.25 meters 1.6 MHz
70 cm 5 MHz
33 cm 12 MHz
23 cm 20 MHz
Notes: <number>
This is the national band plan. Note that Western Washington uses a different split on 6 meters.

## Slide 7: T2A01 What is the most common repeater frequency offset in the 2 meter band?
<number>
Microhams 2010 Technician
  A. plus 500 kHz
  B. plus or minus 600 kHz
  C. minus 500 kHz
  D. Only plus 600 kHz

## Slide 8: T2A01 What is the most common repeater frequency offset in the 2 meter band?
<number>
Microhams 2010 Technician
  A. plus 500 kHz
B. plus or minus 600 kHz
  C. minus 500 kHz
  D. Only plus 600 kHz

## Slide 9: T2A02 What is the national calling frequency for FM simplex operations in the 70 cm band?
<number>
Microhams 2010 Technician
  A. 146.520 MHz
  B. 145.000 MHz
  C. 432.100 MHz
  D. 446.000 MHz

## Slide 10: T2A02 What is the national calling frequency for FM simplex operations in the 70 cm band?
<number>
Microhams 2010 Technician
  A. 146.520 MHz
  B. 145.000 MHz
  C. 432.100 MHz
D. 446.000 MHz

## Slide 11: T2A03 What is a common repeater frequency offset in the 70 cm band?
<number>
Microhams 2010 Technician
  A. Plus or minus 5 MHz
  B. Plus or minus 600 kHz
  C. Minus 600 kHz
  D. Plus 600 kHz

## Slide 12: T2A03 What is a common repeater frequency offset in the 70 cm band?
<number>
Microhams 2010 Technician
A. Plus or minus 5 MHz
  B. Plus or minus 600 kHz
  C. Minus 600 kHz
  D. Plus 600 kHz

## Slide 13: T2A04 What is an appropriate way to call another station on a repeater if you know the other station's call sign?
<number>
Microhams 2010 Technician
  A. Say "break, break" then say the station's call sign
  B. Say the station's call sign then identify with your call sign
  C. Say "CQ" three times then the other station's call sign
  D. Wait for the station to call "CQ" then answer it

## Slide 14: T2A04 What is an appropriate way to call another station on a repeater if you know the other station's call sign?
<number>
Microhams 2010 Technician
  A. Say "break, break" then say the station's call sign
B. Say the station's call sign then identify with your call sign
  C. Say "CQ" three times then the other station's call sign
  D. Wait for the station to call "CQ" then answer it

## Slide 15: T2A05 What should you transmit when responding to a call of CQ?
<number>
Microhams 2010 Technician
  A. CQ followed by the other station's call sign
  B. Your call sign followed by the other station's call sign
  C. The other station's call sign followed by your call sign
  D. A signal report followed by your call sign

## Slide 16: T2A05 What should you transmit when responding to a call of CQ?
<number>
Microhams 2010 Technician
  A. CQ followed by the other station's call sign
  B. Your call sign followed by the other station's call sign
C. The other station's call sign followed by your call sign
  D. A signal report followed by your call sign

## Slide 17: T2A06 What must an amateur operator do when making on-air transmissions to test equipment or antennas?
<number>
Microhams 2010 Technician
  A. Properly identify the transmitting station
  B. Make test transmissions only after 10:00 p.m. local time
  C. Notify the FCC of the test transmission
  D. State the purpose of the test during the test procedure

## Slide 18: T2A06 What must an amateur operator do when making on-air transmissions to test equipment or antennas?
<number>
Microhams 2010 Technician
A. Properly identify the transmitting station
  B. Make test transmissions only after 10:00 p.m. local time
  C. Notify the FCC of the test transmission
  D. State the purpose of the test during the test procedure

## Slide 19: T2A07 Which of the following is true when making a test transmission?
<number>
Microhams 2010 Technician
  A. Station identification is not required if the transmission is less than 15 seconds
  B. Station identification is not required if the transmission is less than 1 watt
  C. Station identification is required only if your station can be heard
  D. Station identification is required at least every ten minutes during the test and at the end

## Slide 20: T2A07 Which of the following is true when making a test transmission?
<number>
Microhams 2010 Technician
  A. Station identification is not required if the transmission is less than 15 seconds
  B. Station identification is not required if the transmission is less than 1 watt
  C. Station identification is required only if your station can be heard
D. Station identification is required at least every ten minutes during the test and at the end

## Slide 21: T2A08 What is the meaning of the procedural signal "CQ"?
<number>
Microhams 2010 Technician
  A. Call on the quarter hour
  B. A new antenna is being tested (no station should answer)
  C. Only the called station should transmit
  D. Calling any station

## Slide 22: T2A08 What is the meaning of the procedural signal "CQ"?
<number>
Microhams 2010 Technician
  A. Call on the quarter hour
  B. A new antenna is being tested (no station should answer)
  C. Only the called station should transmit
D. Calling any station

## Slide 23: T2A09 What brief statement is often used in place of "CQ" to indicate that you are listening on a repeater?
<number>
Microhams 2010 Technician
  A. Say "Hello test" followed by your call sign
  B. Say your call sign
  C. Say the repeater call sign followed by your call sign
  D. Say the letters "QSY" followed by your call sign

## Slide 24: T2A09 What brief statement is often used in place of "CQ" to indicate that you are listening on a repeater?
<number>
Microhams 2010 Technician
  A. Say "Hello test" followed by your call sign
B. Say your call sign
  C. Say the repeater call sign followed by your call sign
  D. Say the letters "QSY" followed by your call sign

## Slide 25: T2A10 What is a band plan, beyond the privileges established by the FCC?
<number>
Microhams 2010 Technician
  A. A voluntary guideline for using different modes or activities within an amateur band
  B. A mandated list of operating schedules
  C. A list of scheduled net frequencies
  D. A plan devised by a club to use a frequency band during a contest

## Slide 26
Operating Practices
<number>
23cm
33cm
70cm
1.25m
2m
6m
2300 2310 2390 2450
1240 1300
902 928
420 430 435 438 450
Not Available North of Line A |  | Satellite | 
219 220 222 225
144 144.1 148
CW | 
50 50.1 54
 No Code Technicians Have All Privileges On The Above Bands 
13cm
Point to Point Digital Links |  | 
CW | 
70cm - 5 MHz repeater frequency separation (Split)
2m - 600 kHz repeater frequency separation (Split)
Notes: <number>
The FCC has mandated the areas colored (other than blue) to specific purposes. The remaining areas are divided by the amateur community into a band plan to insure most effective use of the spectrum and minimize interference. This band plan is not law but voluntary. If the FCC does get involved in a dispute, they will use the local band plan as a means to resolve the dispute.

## Slide 27: T2A10 What is a band plan, beyond the privileges established by the FCC?
<number>
Microhams 2010 Technician
A. A voluntary guideline for using different modes or activities within an amateur band
  B. A mandated list of operating schedules
  C. A list of scheduled net frequencies
  D. A plan devised by a club to use a frequency band during a contest

## Slide 28: T2A11 What are the FCC rules regarding power levels used in the amateur bands?
<number>
Microhams 2010 Technician
  A. Always use the maximum power allowed to ensure that you complete the contact
  B. An amateur may use no more than 200 watts PEP to make an amateur contact
  C. An amateur may use up to 1500 watts PEP on any amateur frequency
  D. An amateur must use the minimum transmitter power necessary to carry out the desired communication

## Slide 29: T2A11 What are the FCC rules regarding power levels used in the amateur bands?
<number>
Microhams 2010 Technician
  A. Always use the maximum power allowed to ensure that you complete the contact
  B. An amateur may use no more than 200 watts PEP to make an amateur contact
  C. An amateur may use up to 1500 watts PEP on any amateur frequency
D. An amateur must use the minimum transmitter power necessary to carry out the desired communication

## Slide 30: T2B01 What is the term used to describe an amateur station that is transmitting and receiving on the same frequency?
<number>
Microhams 2010 Technician
  A. Full duplex communication
  B. Diplex communication
  C. Simplex communication
  D. Half duplex communication

## Slide 31: T2B01 What is the term used to describe an amateur station that is transmitting and receiving on the same frequency?
<number>
Microhams 2010 Technician
  A. Full duplex communication
  B. Diplex communication
C. Simplex communication
  D. Half duplex communication

## Slide 32: T2B02 What is the term used to describe the use of a sub-audible tone transmitted with normal voice audio to open the squelch of a receiver?
<number>
Microhams 2010 Technician
  A. Carrier squelch
  B. Tone burst
  C. DTMF
  D. CTCSS

## Slide 33: T2B02 What is the term used to describe the use of a sub-audible tone transmitted with normal voice audio to open the squelch of a receiver?
<number>
Microhams 2010 Technician
  A. Carrier squelch
  B. Tone burst
  C. DTMF
D. CTCSS

## Slide 34: T2B03 Which of the following describes the muting of receiver audio controlled solely by the presence or absence of an RF signal?
<number>
Microhams 2010 Technician
  A. Tone squelch
  B. Carrier squelch
  C. CTCSS
  D. Modulated carrier

## Slide 35: T2B03 Which of the following describes the muting of receiver audio controlled solely by the presence or absence of an RF signal?
<number>
Microhams 2010 Technician
  A. Tone squelch
B. Carrier squelch
  C. CTCSS
  D. Modulated carrier

## Slide 36: T2B04 Which of the following common problems might cause you to be able to hear but not access a repeater even when transmitting with the proper offset?
<number>
Microhams 2010 Technician
  A. The repeater receiver requires audio tone burst for access
  B. The repeater receiver requires a CTCSS tone for access
  C. The repeater receiver may require a DCS tone sequence for access
  D. All of these choices are correct

## Slide 37: T2B04 Which of the following common problems might cause you to be able to hear but not access a repeater even when transmitting with the proper offset?
<number>
Microhams 2010 Technician
  A. The repeater receiver requires audio tone burst for access
  B. The repeater receiver requires a CTCSS tone for access
  C. The repeater receiver may require a DCS tone sequence for access
D. All of these choices are correct

## Slide 38: T2B05 What determines the amount of deviation of an FM signal?
<number>
Microhams 2010 Technician
  A. Both the frequency and amplitude of the modulating signal
  B. The frequency of the modulating signal
  C. The amplitude of the modulating signal
  D. The relative phase of the modulating signal and the carrier

## Slide 39: T2B05 What determines the amount of deviation of an FM signal?
<number>
Microhams 2010 Technician
  A. Both the frequency and amplitude of the modulating signal
  B. The frequency of the modulating signal
C. The amplitude of the modulating signal
  D. The relative phase of the modulating signal and the carrier

## Slide 40: T2B06 What happens when the deviation of an FM transmitter is increased?
<number>
Microhams 2010 Technician
  A. Its signal occupies more bandwidth
  B. Its output power increases
  C. Its output power and bandwidth increases
  D. Asymmetric modulation occurs

## Slide 41: T2B06 What happens when the deviation of an FM transmitter is increased?
<number>
Microhams 2010 Technician
A. Its signal occupies more bandwidth
  B. Its output power increases
  C. Its output power and bandwidth increases
  D. Asymmetric modulation occurs

## Slide 42: T2B07 What should you do if you receive a report that your station's transmissions are causing splatter or interference on nearby frequencies?
<number>
Microhams 2010 Technician
  A. Increase transmit power
  B. Change mode of transmission
  C. Report the interference to the equipment manufacturer
  D. Check your transmitter for off-frequency operation or spurious emissions

## Slide 43: T2B07 What should you do if you receive a report that your station's transmissions are causing splatter or interference on nearby frequencies?
<number>
Microhams 2010 Technician
  A. Increase transmit power
  B. Change mode of transmission
  C. Report the interference to the equipment manufacturer
D. Check your transmitter for off-frequency operation or spurious emissions

## Slide 44: T2B08 What is the proper course of action if your station's transmission unintentionally interferes with another station?
<number>
Microhams 2010 Technician
  A. Rotate your antenna slightly
  B. Properly identify your transmission and move to a different frequency
  C. Increase power
  D. Change antenna polarization

## Slide 45: T2B08 What is the proper course of action if your station's transmission unintentionally interferes with another station?
<number>
Microhams 2010 Technician
  A. Rotate your antenna slightly
B. Properly identify your transmission and move to a different frequency
  C. Increase power
  D. Change antenna polarization

## Slide 46: T2B09 Which of the following methods is encouraged by the FCC when identifying your station when using phone?
<number>
Microhams 2010 Technician
  A. Use of a phonetic alphabet
  B. Send your call sign in CW as well as voice
  C. Repeat your call sign three times
  D. Increase your signal to full power when identifying

## Slide 47: T2B09 Which of the following methods is encouraged by the FCC when identifying your station when using phone?
<number>
Microhams 2010 Technician
A. Use of a phonetic alphabet
  B. Send your call sign in CW as well as voice
  C. Repeat your call sign three times
  D. Increase your signal to full power when identifying

## Slide 48: T2B10 What is the "Q" signal used to indicate that you are receiving interference from other stations?
<number>
Microhams 2010 Technician
  A. QRM
  B. QRN
  C. QTH
  D. QSB

## Slide 49: T2B10 What is the "Q" signal used to indicate that you are receiving interference from other stations?
<number>
Microhams 2010 Technician
A. QRM
  B. QRN
  C. QTH
  D. QSB

## Slide 50: T2B11 What is the "Q" signal used to indicate that you are changing frequency?
<number>
Microhams 2010 Technician
  A. QRU
  B. QSY
  C. QSL
  D. QRZ

## Slide 51: T2B11 What is the "Q" signal used to indicate that you are changing frequency?
<number>
Microhams 2010 Technician
  A. QRU
B. QSY
  C. QSL
  D. QRZ

## Slide 52: T2C01 What set of rules applies to proper operation of your station when using amateur radio at the request of public service officials?
<number>
Microhams 2010 Technician
  A. RACES Rules
  B. ARES Rules
  C. FCC Rules
  D. FEMA Rules

## Slide 53: T2C01 What set of rules applies to proper operation of your station when using amateur radio at the request of public service officials?
<number>
Microhams 2010 Technician
  A. RACES Rules
  B. ARES Rules
C. FCC Rules
  D. FEMA Rules

## Slide 54: T2C02 Who must submit the request for a temporary waiver of Part 97.113 to allow amateur radio operators to provide communications on behalf of their employers during a government sponsored disaster drill?
<number>
Microhams 2010 Technician
  A. Each amateur participating in the drill
  B. Any employer participating in the drill
  C. The local American Red Cross Chapter
  D. The government agency sponsoring the event

## Slide 55: T2C02 Who must submit the request for a temporary waiver of Part 97.113 to allow amateur radio operators to provide communications on behalf of their employers during a government sponsored disaster drill?
<number>
Microhams 2010 Technician
  A. Each amateur participating in the drill
  B. Any employer participating in the drill
  C. The local American Red Cross Chapter
D. The government agency sponsoring the event

## Slide 56: T2C03 When is it legal for an amateur licensee to provide communications on behalf of their employer during a government sponsored disaster drill or exercise?
<number>
Microhams 2010 Technician
  A. Whenever the employer is a not-for-profit organization
  B. Whenever there is a temporary need for the employer's business continuity plan
  C. Only when the FCC has granted a government-requested waiver
  D. Only when the amateur is not receiving compensation from his employer for the activity

## Slide 57: T2C03 When is it legal for an amateur licensee to provide communications on behalf of their employer during a government sponsored disaster drill or exercise?
<number>
Microhams 2010 Technician
  A. Whenever the employer is a not-for-profit organization
  B. Whenever there is a temporary need for the employer's business continuity plan
C. Only when the FCC has granted a government-requested waiver
  D. Only when the amateur is not receiving compensation from his employer for the activity

## Slide 58: RACES / ARES
Operating Practices
<number>
RACES – Radio Amateur Civil Emergency Service
  Work with local, state and federal government only
  When activated, you work for the government (Restricted)
  When activated, mission participants are covered by government insurance
ARES - Amateur Radio Emergency Service
  Health and welfare
  Work with government and NGO (Red Cross, Salvation Army) and support services
  When activated, you still are a civilian
Note – both groups do good work, and many hams belong to both groups,
also both groups are often combined.

## Slide 59: T2C04 What do RACES and ARES have in common?
<number>
Microhams 2010 Technician
  A. They represent the two largest ham clubs in the United States
  B. Both organizations broadcast road and weather traffic information
  C. Neither may handle emergency traffic supporting public service agencies
  D. Both organizations may provide communications during emergencies

## Slide 60: T2C04 What do RACES and ARES have in common?
<number>
Microhams 2010 Technician
  A. They represent the two largest ham clubs in the United States
  B. Both organizations broadcast road and weather traffic information
  C. Neither may handle emergency traffic supporting public service agencies
D. Both organizations may provide communications during emergencies

## Slide 61: T2C05 What is the Radio Amateur Civil Emergency Service?
<number>
Microhams 2010 Technician
  A. An emergency radio service organized by amateur operators
  B. A radio service using amateur stations for emergency management or civil defense communications
  C. A radio service organized to provide communications at civic events
  D. A radio service organized by amateur operators to assist non-military persons

## Slide 62: T2C05 What is the Radio Amateur Civil Emergency Service?
<number>
Microhams 2010 Technician
  A. An emergency radio service organized by amateur operators
B. A radio service using amateur stations for emergency management or civil defense communications
  C. A radio service organized to provide communications at civic events
  D. A radio service organized by amateur operators to assist non-military persons

## Slide 63: T2C06 Which of the following is common practice during net operations to get the immediate attention of the net control station when reporting an emergency?
<number>
Microhams 2010 Technician
  A. Repeat the words SOS three times followed by the call sign of the reporting station
  B. Press the push-to-talk button three times
  C. Begin your transmission with "Priority" or "Emergency" followed by your call sign
  D. Play a pre-recorded emergency alert tone followed by your call sign

## Slide 64: T2C06 Which of the following is common practice during net operations to get the immediate attention of the net control station when reporting an emergency?
<number>
Microhams 2010 Technician
  A. Repeat the words SOS three times followed by the call sign of the reporting station
  B. Press the push-to-talk button three times
C. Begin your transmission with "Priority" or "Emergency" followed by your call sign
  D. Play a pre-recorded emergency alert tone followed by your call sign

## Slide 65: T2C07 What should you do to minimize disruptions to an emergency traffic net once you have checked in?
<number>
Microhams 2010 Technician
  A. Whenever the net frequency is quiet, announce your call sign and location
  B. Move 5 kHz away from the net's frequency and use high power to ask other hams to keep clear of the net frequency
  C. Do not transmit on the net frequency until asked to do so by the net control station
  D. Wait until the net frequency is quiet, then ask for any emergency traffic for your area

## Slide 66: T2C07 What should you do to minimize disruptions to an emergency traffic net once you have checked in?
<number>
Microhams 2010 Technician
  A. Whenever the net frequency is quiet, announce your call sign and location
  B. Move 5 kHz away from the net's frequency and use high power to ask other hams to keep clear of the net frequency
C. Do not transmit on the net frequency until asked to do so by the net control station
  D. Wait until the net frequency is quiet, then ask for any emergency traffic for your area

## Slide 67: T2C08 What is usually considered to be the most important job of an amateur operator when handling emergency traffic messages?
<number>
Microhams 2010 Technician
  A. Passing messages exactly as written, spoken or as received
  B. Estimating the number of people affected by the disaster
  C. Communicating messages to the news media for broadcast outside the disaster area
  D. Broadcasting emergency information to the general public

## Slide 68: T2C08 What is usually considered to be the most important job of an amateur operator when handling emergency traffic messages?
<number>
Microhams 2010 Technician
A. Passing messages exactly as written, spoken or as received
  B. Estimating the number of people affected by the disaster
  C. Communicating messages to the news media for broadcast outside the disaster area
  D. Broadcasting emergency information to the general public

## Slide 69: T2C09 When may an amateur station use any means of radio communications at its disposal for essential communications in connection with immediate safety of human life and protection of property?
<number>
Microhams 2010 Technician
  A. Only when FEMA authorizes it by declaring an emergency
  B. When normal communications systems are not available
  C. Only when RACES authorizes it by declaring an emergency
  D. Only when authorized by the local MARS program director

## Slide 70: T2C09 When may an amateur station use any means of radio communications at its disposal for essential communications in connection with immediate safety of human life and protection of property?
<number>
Microhams 2010 Technician
  A. Only when FEMA authorizes it by declaring an emergency
B. When normal communications systems are not available
  C. Only when RACES authorizes it by declaring an emergency
  D. Only when authorized by the local MARS program director

## Slide 71: T2C10 What is the preamble in a formal traffic message?
<number>
Microhams 2010 Technician
  A. The first paragraph of the message text
  B. The message number
  C. The priority handling indicator for the message
  D. The information needed to track the message as it passes through the amateur radio traffic handling system

## Slide 72: T2C10 What is the preamble in a formal traffic message?
<number>
Microhams 2010 Technician
  A. The first paragraph of the message text
  B. The message number
  C. The priority handling indicator for the message
D. The information needed to track the message as it passes through the amateur radio traffic handling system

## Slide 73: T2C11 What is meant by the term "check" in reference to a formal traffic message?
<number>
Microhams 2010 Technician
  A. The check is a count of the number of words or word equivalents in the text portion of the message
  B. The check is the value of a money order attached to the message
  C. The check is a list of stations that have relayed the message
  D. The check is a box on the message form that tells you the message was received

## Slide 74: T2C11 What is meant by the term "check" in reference to a formal traffic message?
<number>
Microhams 2010 Technician
A. The check is a count of the number of words or word equivalents in the text portion of the message
  B. The check is the value of a money order attached to the message
  C. The check is a list of stations that have relayed the message
  D. The check is a box on the message form that tells you the message was received

## Slide 75: SUBELEMENT T2 [3 exam questions – 3 groups]
<number>
Microhams 2010 Technician
Notes: <number>
http://www.microhams.com
Created by Scott N7SS