## Slide 1: SUBELEMENT T4 [2 Exam Questions - 2 Groups]
Amateur radio practices and station setup
Notes: <number>
2010 Technician Class (Element 2) Master syllabus
Released 1 February, 2010
396 questions in 35 sections
These slides are free to use and are available from http://www.microhams.com. Changes are allowed if Microhams branding is left in place (feel free to ad your own). Any content additions should be forwarded to the author, Scott N7SS at N7SS@arrl.net so they can be rolled into future versions and available for everyone.

## Slide 2: T4 – Amateur Practices
<number>
Microhams 2010 Technician
T4A - Station setup; microphone, speaker, headphones, filters, power source, connecting a computer, RF grounding
T4B - Operating controls; tuning, use of filters, squelch, AGC, repeater offset, memory channels

## Slide 3: T4A01 Which of the following is true concerning the microphone connectors on amateur transceivers?
<number>
Microhams 2010 Technician
  A. All transceivers use the same microphone connector type
  B. Some connectors include push-to-talk and voltages for powering the microphone
  C. All transceivers using the same connector type are wired identically
  D. Un-keyed connectors allow any microphone to be connected

## Slide 4: T4A01 Which of the following is true concerning the microphone connectors on amateur transceivers?
<number>
Microhams 2010 Technician
  A. All transceivers use the same microphone connector type
B. Some connectors include push-to-talk and voltages for powering the microphone
  C. All transceivers using the same connector type are wired identically
  D. Un-keyed connectors allow any microphone to be connected

## Slide 5: T4A02 What could be used in place of a regular speaker to help you copy signals in a noisy area?
<number>
Microhams 2010 Technician
  A. A video display
  B. A low pass filter
  C. A set of headphones
  D. A boom microphone

## Slide 6: Communications Headset
Station Setup and Operation
<number>
Notes: <number>
Good communications headphones are not the same as HiFi headphones. HiFi headphones are designed to cover the entire range of human hearing (20-20,000Hz) equally well. Communications headphones are only designed to reproduce the 300-3000Hz voice frequencies which helps reduce non-voice noise that might come out of the receiver. This model includes a boom microphone that minimizes background noise and insures consistent voice quality. Push-to-Talk (PTT) is via a foot switch on the floor to leave the operators hands free.

## Slide 7: T4A02 What could be used in place of a regular speaker to help you copy signals in a noisy area?
<number>
Microhams 2010 Technician
  A. A video display
  B. A low pass filter
C. A set of headphones
  D. A boom microphone

## Slide 8: T4A03 Which is a good reason to use a regulated power supply for communications equipment?
<number>
Microhams 2010 Technician
  A. It prevents voltage fluctuations from reaching sensitive circuits
  B. A regulated power supply has FCC approval
  C. A fuse or circuit breaker regulates the power
  D. Power consumption is independent of load

## Slide 9: T4A03 Which is a good reason to use a regulated power supply for communications equipment?
<number>
Microhams 2010 Technician
A. It prevents voltage fluctuations from reaching sensitive circuits
  B. A regulated power supply has FCC approval
  C. A fuse or circuit breaker regulates the power
  D. Power consumption is independent of load

## Slide 10: Power Supply
Radio and Electronic Fundamentals
<number>
This Daiwa power supply has a meter that can display voltage and current
Notes: <number>
If your power supply has volt and ammeters, it can be used to calculate power consumption of your rig at various power levels. This will help determine proper fuse sizing, appropriate wire gauge, anticipated battery life, etc.

## Slide 11: T4A04 Where must a filter be installed to reduce harmonic emissions?
<number>
Microhams 2010 Technician
  A. Between the transmitter and the antenna
  B. Between the receiver and the transmitter
  C. At the station power supply
  D. At the microphone

## Slide 12: T4A04 Where must a filter be installed to reduce harmonic emissions?
<number>
Microhams 2010 Technician
A. Between the transmitter and the antenna
  B. Between the receiver and the transmitter
  C. At the station power supply
  D. At the microphone

## Slide 13: T4A05 What type of filter should be connected to a TV receiver as the first step in trying to prevent RF overload from a nearby 2 meter transmitter?
<number>
Microhams 2010 Technician
  A. Low-pass filter
  B. High-pass filter
  C. Band-pass filter
  D. Band-reject filter

## Slide 14: T4A05 What type of filter should be connected to a TV receiver as the first step in trying to prevent RF overload from a nearby 2 meter transmitter?
<number>
Microhams 2010 Technician
  A. Low-pass filter
  B. High-pass filter
  C. Band-pass filter
D. Band-reject filter

## Slide 15: Notch (Band Stop) Filter
Station Setup and Operation
<number>
Stop Band
High Frequency
Low Frequency
40 dB
0 dB
fc
fc
-3 dB
Pass Band
Pass Band
There are notch filters built to notch out the powerful pager transmitters located just above the 2m band.
Very effective notch filters can be made with a 1/2 wavelength piece of coax shorted on one end connected to a coaxial “T” connector on the other. These are often called “stubs”.
Repeaters use cavity notch filters that have very sharp skirts to keep the transmitter from interfering with the receiver, since they’re both active at the same time on very close frequencies.

## Slide 16: T4A06 Which of the following would be connected between a transceiver and computer in a packet radio station?
<number>
Microhams 2010 Technician
  A. Transmatch
  B. Mixer
  C. Terminal node controller
  D. Antenna

## Slide 17: T4A06 Which of the following would be connected between a transceiver and computer in a packet radio station?
<number>
Microhams 2010 Technician
  A. Transmatch
  B. Mixer
C. Terminal node controller
  D. Antenna

## Slide 18: Terminal Node Controllers (TNC) (Radio Modems)
Station Setup and Operation
<number>

## Slide 19: T4A07 How is the computer's sound card used when conducting digital communications using a computer?
<number>
Microhams 2010 Technician
  A. The sound card communicates between the computer CPU and the video display
  B. The sound card records the audio frequency for video display
  C. The sound card provides audio to the microphone input and converts received audio to digital form
  D. All of these choices are correct

## Slide 20: T4A07 How is the computer's sound card used when conducting digital communications using a computer?
<number>
Microhams 2010 Technician
  A. The sound card communicates between the computer CPU and the video display
  B. The sound card records the audio frequency for video display
C. The sound card provides audio to the microphone input and converts received audio to digital form
  D. All of these choices are correct

## Slide 21: T4A08 Which type of conductor is best to use for RF grounding?
<number>
Microhams 2010 Technician
  A. Round stranded wire
  B. Round copper-clad steel wire
  C. Twisted-pair cable
  D. Flat strap

## Slide 22: T4A08 Which type of conductor is best to use for RF grounding?
<number>
Microhams 2010 Technician
  A. Round stranded wire
  B. Round copper-clad steel wire
  C. Twisted-pair cable
D. Flat strap

## Slide 23: T4A09 Which would you use to reduce RF current flowing on the shield of an audio cable?
<number>
Microhams 2010 Technician
  A. Band-pass filter
  B. Low-pass filter
  C. Preamplifier
  D. Ferrite choke

## Slide 24: T4A09 Which would you use to reduce RF current flowing on the shield of an audio cable?
<number>
Microhams 2010 Technician
  A. Band-pass filter
  B. Low-pass filter
  C. Preamplifier
D. Ferrite choke

## Slide 25: T4A10 What is the source of a high-pitched whine that varies with engine speed in a mobile transceiver's receive audio?
<number>
Microhams 2010 Technician
  A. The ignition system
  B. The alternator
  C. The electric fuel pump
  D. Anti-lock braking system controllers

## Slide 26: T4A10 What is the source of a high-pitched whine that varies with engine speed in a mobile transceiver's receive audio?
<number>
Microhams 2010 Technician
  A. The ignition system
B. The alternator
  C. The electric fuel pump
  D. Anti-lock braking system controllers

## Slide 27: T4A11 Where should a mobile transceiver's power negative connection be made?
<number>
Microhams 2010 Technician
  A. At the battery or engine block ground strap
  B. At the antenna mount
  C. To any metal part of the vehicle
  D. Through the transceiver's mounting bracket

## Slide 28: T4A11 Where should a mobile transceiver's power negative connection be made?
<number>
Microhams 2010 Technician
A. At the battery or engine block ground strap
  B. At the antenna mount
  C. To any metal part of the vehicle
  D. Through the transceiver's mounting bracket

## Slide 29: T4B01 What may happen if a transmitter is operated with the microphone gain set too high?
<number>
Microhams 2010 Technician
  A. The output power might be too high
  B. The output signal might become distorted
  C. The frequency might vary
  D. The SWR might increase

## Slide 30: T4B01 What may happen if a transmitter is operated with the microphone gain set too high?
<number>
Microhams 2010 Technician
  A. The output power might be too high
B. The output signal might become distorted
  C. The frequency might vary
  D. The SWR might increase

## Slide 31: Icom IC-7000 Multimode Transceiver
Keypad for band changes and frequency entry
Volume/Squelch Control
VFO or Tuning Knob
Noise Blanker
Up/Down Buttons
RIT
Tune Step (TS)

## Slide 32: T4B02 Which of the following can be used to enter the operating frequency on a modern transceiver?
<number>
Microhams 2010 Technician
  A. The keypad or VFO knob
  B. The CTCSS or DTMF encoder
  C. The Automatic Frequency Control
  D. All of these choices are correct

## Slide 33: T4B02 Which of the following can be used to enter the operating frequency on a modern transceiver?
<number>
Microhams 2010 Technician
A. The keypad or VFO knob
  B. The CTCSS or DTMF encoder
  C. The Automatic Frequency Control
  D. All of these choices are correct

## Slide 34: T4B03 What is the purpose of the squelch control on a transceiver?
<number>
Microhams 2010 Technician
  A. To set the highest level of volume desired
  B. To set the transmitter power level
  C. To adjust the automatic gain control
  D. To mute receiver output noise when no signal is being received

## Slide 35: T4B03 What is the purpose of the squelch control on a transceiver?
<number>
Microhams 2010 Technician
  A. To set the highest level of volume desired
  B. To set the transmitter power level
  C. To adjust the automatic gain control
D. To mute receiver output noise when no signal is being received

## Slide 36: T4B04 What is a way to enable quick access to a favorite frequency on your transceiver?
<number>
Microhams 2010 Technician
  A. Enable the CTCSS tones
  B. Store the frequency in a memory channel
  C. Disable the CTCSS tones
  D. Use the scan mode to select the desired frequency

## Slide 37: T4B04 What is a way to enable quick access to a favorite frequency on your transceiver?
<number>
Microhams 2010 Technician
  A. Enable the CTCSS tones
B. Store the frequency in a memory channel
  C. Disable the CTCSS tones
  D. Use the scan mode to select the desired frequency

## Slide 38: T4B05 Which of the following would reduce ignition interference to a receiver?
<number>
Microhams 2010 Technician
  A. Change frequency slightly
  B. Decrease the squelch setting
  C. Turn on the noise blanker
  D. Use the RIT control

## Slide 39: T4B05 Which of the following would reduce ignition interference to a receiver?
<number>
Microhams 2010 Technician
  A. Change frequency slightly
  B. Decrease the squelch setting
C. Turn on the noise blanker
  D. Use the RIT control

## Slide 40: T4B06 Which of the following controls could be used if the voice pitch of a single-sideband signal seems too high or low?
<number>
Microhams 2010 Technician
  A. The AGC or limiter
  B. The bandwidth selection
  C. The tone squelch
  D. The receiver RIT or clarifier

## Slide 41: T4B06 Which of the following controls could be used if the voice pitch of a single-sideband signal seems too high or low?
<number>
Microhams 2010 Technician
  A. The AGC or limiter
  B. The bandwidth selection
  C. The tone squelch
D. The receiver RIT or clarifier

## Slide 42: T4B07 What does the term "RIT" mean?
<number>
Microhams 2010 Technician
  A. Receiver Input Tone
  B. Receiver Incremental Tuning
  C. Rectifier Inverter Test
  D. Remote Input Transmitter

## Slide 43: T4B07 What does the term "RIT" mean?
<number>
Microhams 2010 Technician
  A. Receiver Input Tone
B. Receiver Incremental Tuning
  C. Rectifier Inverter Test
  D. Remote Input Transmitter

## Slide 44: T4B08 What is the advantage of having multiple receive bandwidth choices on a multimode transceiver?
<number>
Microhams 2010 Technician
  A. Permits monitoring several modes at once
  B. Permits noise or interference reduction by selecting a bandwidth matching the mode
  C. Increases the number of frequencies that can be stored in memory
  D. Increases the amount of offset between receive and transmit frequencies

## Slide 45: T4B08 What is the advantage of having multiple receive bandwidth choices on a multimode transceiver?
<number>
Microhams 2010 Technician
  A. Permits monitoring several modes at once
B. Permits noise or interference reduction by selecting a bandwidth matching the mode
  C. Increases the number of frequencies that can be stored in memory
  D. Increases the amount of offset between receive and transmit frequencies

## Slide 46: T4B09 Which of the following is an appropriate receive filter to select in order to minimize noise and interference for SSB reception?
<number>
Microhams 2010 Technician
  A. 500 Hz
  B. 1000 Hz
  C. 2400 Hz
  D. 5000 Hz

## Slide 47: T4B09 Which of the following is an appropriate receive filter to select in order to minimize noise and interference for SSB reception?
<number>
Microhams 2010 Technician
  A. 500 Hz
  B. 1000 Hz
C. 2400 Hz
  D. 5000 Hz

## Slide 48: T4B10 Which of the following is an appropriate receive filter to select in order to minimize noise and interference for CW reception?
<number>
Microhams 2010 Technician
  A. 500 Hz
  B. 1000 Hz
  C. 2400 Hz
  D. 5000 Hz

## Slide 49: T4B10 Which of the following is an appropriate receive filter to select in order to minimize noise and interference for CW reception?
<number>
Microhams 2010 Technician
A. 500 Hz
  B. 1000 Hz
  C. 2400 Hz
  D. 5000 Hz

## Slide 50: T4B11 Which of the following describes the common meaning of the term "repeater offset"?
<number>
Microhams 2010 Technician
  A. The distance between the repeater's transmit and receive antennas
  B. The time delay before the repeater timer resets
  C. The difference between the repeater's transmit and receive frequencies
  D. The maximum frequency deviation permitted on the repeater's input signal

## Slide 51: T4B11 Which of the following describes the common meaning of the term "repeater offset"?
<number>
Microhams 2010 Technician
  A. The distance between the repeater's transmit and receive antennas
  B. The time delay before the repeater timer resets
C. The difference between the repeater's transmit and receive frequencies
  D. The maximum frequency deviation permitted on the repeater's input signal

## Slide 52: Repeater Operation
Station Setup and Operation
<number>
60+ miles
Output Freq
145.21 MHz
Input Freq
144.61 MHz
Offset
- 600 kHz

## Slide 53: Repeater Input/Output Offsets
Station Setup and Operation
<number>
Band Offset
6 meters 1 MHz
2 meters 600 kHz
1.25 meters 1.6 MHz
70 cm 5 MHz
33 cm 12 MHz
23 cm 20 MHz
Notes: <number>
This is the national band plan. Note that Western Washington uses a different split on 6 meters.

## Slide 54: SUBELEMENT T4 [2 exam questions – 2 groups]
<number>
Microhams 2010 Technician
Notes: <number>
http://www.microhams.com
Created by Scott N7SS