## Slide 1: SUBELEMENT T5 [4 Exam Questions - 4 Groups]
Electrical Principles, Electronic Principles, Math for Electronics
Notes: <number>
2010 Technician Class (Element 2) Master syllabus
Released 1 February, 2010
396 questions in 35 sections
These slides are free to use and are available from http://www.microhams.com. Changes are allowed if Microhams branding is left in place (feel free to ad your own). Any content additions should be forwarded to the author, Scott N7SS at N7SS@arrl.net so they can be rolled into future versions and available for everyone.

## Slide 2: T5 – Electrical and Electronic Principles, Math for Electronics
<number>
Microhams 2010 Technician
T5A – Electrical Principles, current and voltage, conductors and insulators, alternating and direct current.
T5B – Math for electronics, decibels, electronic unites and the metric system.
T5C – Electronic principles, capacitance, inductance, current flow in circuits, alternating current, definition of RF, power calculations.
T5D - Ohm’s Law

## Slide 3: Units of Measure
Radio and Electronic Fundamentals
<number>
Power | Watt
Resistance | Ohm
Voltage | Volt
Current | Ampere
Frequency | Hertz

## Slide 4
Radio and Electronic Fundamentals
<number>
109 106 103 102 101 100 10-1 10-2 10-3 10-6 10-9
G M k h da d c m µ n
giga mega kilo hecto deca deci centi milli micro nano
Metric Units of Measure
Gigahertz | 1,000,000,000
Megahertz | 1,000,000
Kilohertz | 1,000
Hertz | 1
Ampere | 1
Milliampere | 0.001
Microampere | 0.000001
Nanoampere | 0.000000001
Billions
Millions
Thousands
Hundreds
Tens
Tenths
Thousandths
Hundredths
Millionths
Billionths
Notes: <number>
Note the shift in decimal places. This is standard metric notation. 1 Gigahertz is 1 Billion Hertz and a Nanoampere is 1 Billionth of an Ampere.

## Slide 5: Voltage, Current, Resistance
Radio and Electronic Fundamentals
<number>
+
-
Voltage
Current
Resistance (Load)
You need a circuit for electricity to flow
Components of a circuit: Source, Conductors, Load, Sink (Ground)
Notes: <number>
Voltage is also called Electromotive Force and is an electrical “pressure”. Current is a measure of the flow of electrons (volume) from the negative to positive poles. The load presents resistance to the flow of electrons. Voltage is measured across the positive and negative poles (in parallel) to measure the difference in “pressure”. To measure the electron flow, the meter must be placed in-line (in series) with the flow.
Direct Current (DC) is a constant voltage source that causes current to flow in only one direction and has a positive and negative pole – like a battery. Alternating Current is what is available in the wall and the constantly changing polarity causes current to alternate directions.

## Slide 6: T5A01 Electrical current is measured in which of the following units?
  A. Volts
  B. Watts
  C. Ohms
  D. Amperes

## Slide 7: T5A01 Electrical current is measured in which of the following units?
  A. Volts
  B. Watts
  C. Ohms
D. Amperes

## Slide 8: T5A02 Electrical power is measured in which of the following units?
  A. Volts
  B. Watts
  C. Ohms
  D. Amperes

## Slide 9: T5A02 Electrical power is measured in which of the following units?
  A. Volts
B. Watts
  C. Ohms
  D. Amperes

## Slide 10: T5A03 What is the name for the flow of electrons in an electric circuit?
  A. Voltage
  B. Resistance
  C. Capacitance
  D. Current

## Slide 11: T5A03 What is the name for the flow of electrons in an electric circuit?
  A. Voltage
  B. Resistance
  C. Capacitance
D. Current

## Slide 12: Direct Current Alternating Current
Radio and Electronic Fundamentals
<number>
DC
Current flows in one direction only
  Examples:
    Battery Operated Devices
    Cars
AC
Current flows in both directions, voltage and current very with time
  Example: House Wiring

## Slide 13: T5A04 What is the name for a current that flows only in one direction?
  A. Alternating current
  B. Direct current
  C. Normal current
  D. Smooth current

## Slide 14: T5A04 What is the name for a current that flows only in one direction?
  A. Alternating current
B. Direct current
  C. Normal current
  D. Smooth current

## Slide 15: T5A05 What is the electrical term for the electromotive force (EMF) that causes electron flow?
  A. Voltage
  B. Ampere-hours
  C. Capacitance
  D. Inductance

## Slide 16: T5A05 What is the electrical term for the electromotive force (EMF) that causes electron flow?
A. Voltage
  B. Ampere-hours
  C. Capacitance
  D. Inductance

## Slide 17: T5A06 How much voltage does a mobile transceiver usually require?
  A. About 12 volts
  B. About 30 volts
  C. About 120 volts
  D. About 240 volts

## Slide 18: T5A06 How much voltage does a mobile transceiver usually require?
A. About 12 volts
  B. About 30 volts
  C. About 120 volts
  D. About 240 volts

## Slide 19: Conductors and Insulators
Radio and Electronic Fundamentals
<number>
In a conductor, electric current can flow freely, in an insulator it cannot. Simply stated, most metals are good electrical conductors, most nonmetals are not. Metals are also generally good heat conductors while nonmetals are not.
Conductors – Copper, Silver, Gold, Aluminum, Platinum, Steel, …
Insulators – Glass, Wood, Rubber, Air, Plastic …
Note: Salt water is a
conductor, and so are you!
Cu
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
Neighboring electrons are repulsed by the motion of electrons, creating a chain reaction that propagates through the material at nearly the speed of light.
Cross- section of copper wire
Copper’s valence electrons move freely throughout the solid copper metal
Copper and other metals have a weak hold on their outer or “valence” electrons. Atoms of insulating materials have a tight grip on their outer electrons.

## Slide 20: T5A07 Which of the following is a good electrical conductor?
  A. Glass
  B. Wood
  C. Copper
  D. Rubber

## Slide 21: T5A07 Which of the following is a good electrical conductor?
  A. Glass
  B. Wood
C. Copper
  D. Rubber

## Slide 22: T5A08 Which of the following is a good electrical insulator?
  A. Copper
  B. Glass
  C. Aluminum
  D. Mercury

## Slide 23: T5A08 Which of the following is a good electrical insulator?
  A. Copper
B. Glass
  C. Aluminum
  D. Mercury

## Slide 24: T5A09 What is the name for a current that reverses direction on a regular basis?
  A. Alternating current
  B. Direct current
  C. Circular current
  D. Vertical current

## Slide 25: T5A09 What is the name for a current that reverses direction on a regular basis?
A. Alternating current
  B. Direct current
  C. Circular current
  D. Vertical current

## Slide 26: T5A10 Which term describes the rate at which electrical energy is used?
  A. Resistance
  B. Current
  C. Power
  D. Voltage

## Slide 27: T5A10 Which term describes the rate at which electrical energy is used?
  A. Resistance
  B. Current
C. Power
  D. Voltage

## Slide 28: T5A11 What is the basic unit of electromotive force?
  A. The volt
  B. The watt
  C. The ampere
  D. The ohm

## Slide 29: T5A11 What is the basic unit of electromotive force?
A. The volt
  B. The watt
  C. The ampere
  D. The ohm

## Slide 30: T5B01 How many milliamperes is 1.5 amperes?
  A. 15 milliamperes
  B. 150 milliamperes
  C. 1,500 milliamperes
  D. 15,000 milliamperes

## Slide 31: T5B01 How many milliamperes is 1.5 amperes?
  A. 15 milliamperes
  B. 150 milliamperes
C. 1,500 milliamperes
  D. 15,000 milliamperes

## Slide 32: T5B02 What is another way to specify a radio signal frequency of 1,500,000 hertz?
  A. 1500 kHz
  B. 1500 MHz
  C. 15 GHz
  D. 150 kHz

## Slide 33: T5B02 What is another way to specify a radio signal frequency of 1,500,000 hertz?
A. 1500 kHz
  B. 1500 MHz
  C. 15 GHz
  D. 150 kHz

## Slide 34: T5B03 How many volts are equal to one kilovolt?
  A. One one-thousandth of a volt
  B. One hundred volts
  C. One thousand volts
  D. One million volts

## Slide 35: T5B03 How many volts are equal to one kilovolt?
  A. One one-thousandth of a volt
  B. One hundred volts
C. One thousand volts
  D. One million volts

## Slide 36: T5B04 How many volts are equal to one microvolt?
  A. One one-millionth of a volt
  B. One million volts
  C. One thousand kilovolts
  D. One one-thousandth of a volt

## Slide 37: T5B04 How many volts are equal to one microvolt?
A. One one-millionth of a volt
  B. One million volts
  C. One thousand kilovolts
  D. One one-thousandth of a volt

## Slide 38: T5B05 Which of the following is equivalent to 500 milliwatts?
  A. 0.02 watts
  B. 0.5 watts
  C. 5 watts
  D. 50 watts

## Slide 39: T5B05 Which of the following is equivalent to 500 milliwatts?
  A. 0.02 watts
B. 0.5 watts
  C. 5 watts
  D. 50 watts

## Slide 40: T5B06 If an ammeter calibrated in amperes is used to measure a 3000-milliampere current, what reading would it show?
  A. 0.003 amperes
  B. 0.3 amperes
  C. 3 amperes
  D. 3,000,000 amperes

## Slide 41: T5B06 If an ammeter calibrated in amperes is used to measure a 3000-milliampere current, what reading would it show?
  A. 0.003 amperes
  B. 0.3 amperes
C. 3 amperes
  D. 3,000,000 amperes

## Slide 42: T5B07 If a frequency readout calibrated in megahertz shows a reading of 3.525 MHz, what would it show if it were calibrated in kilohertz?
  A. 0.003525 kHz
  B. 35.25 kHz
  C. 3525 kHz
  D. 3,525,000 kHz

## Slide 43: T5B07 If a frequency readout calibrated in megahertz shows a reading of 3.525 MHz, what would it show if it were calibrated in kilohertz?
  A. 0.003525 kHz
  B. 35.25 kHz
C. 3525 kHz
  D. 3,525,000 kHz

## Slide 44: T5B08 How many microfarads are 1,000,000 picofarads?
  A. 0.001 microfarads
  B. 1 microfarad
  C. 1000 microfarads
  D. 1,000,000,000 microfarads

## Slide 45: T5B08 How many microfarads are 1,000,000 picofarads?
  A. 0.001 microfarads
B. 1 microfarad
  C. 1000 microfarads
  D. 1,000,000,000 microfarads

## Slide 46: T5B09 What is the approximate amount of change, measured in decibels (dB), of a power increase from 5 watts to 10 watts?
  A. 2 dB
  B. 3 dB
  C. 5 dB
  D. 10 dB

## Slide 47: T5B09 What is the approximate amount of change, measured in decibels (dB), of a power increase from 5 watts to 10 watts?
  A. 2 dB
B. 3 dB
  C. 5 dB
  D. 10 dB

## Slide 48: T5B10 What is the approximate amount of change, measured in decibels (dB), of a power decrease from 12 watts to 3 watts?
  A. 1 dB
  B. 3 dB
  C. 6 dB
  D. 9 dB

## Slide 49: T5B10 What is the approximate amount of change, measured in decibels (dB), of a power decrease from 12 watts to 3 watts?
  A. 1 dB
  B. 3 dB
C. 6 dB
  D. 9 dB

## Slide 50: T5B11 What is the approximate amount of change, measured in decibels (dB), of a power increase from 20 watts to 200 watts?
  A. 10 dB
  B. 12 dB
  C. 18 dB
  D. 28 dB

## Slide 51: T5B11 What is the approximate amount of change, measured in decibels (dB), of a power increase from 20 watts to 200 watts?
A. 10 dB
  B. 12 dB
  C. 18 dB
  D. 28 dB

## Slide 52: T5C01 What is the ability to store energy in an electric field called?
  A. Inductance
  B. Resistance
  C. Tolerance
  D. Capacitance

## Slide 53: T5C01 What is the ability to store energy in an electric field called?
  A. Inductance
  B. Resistance
  C. Tolerance
D. Capacitance

## Slide 54: T5C02 What is the basic unit of capacitance?
  A. The farad
  B. The ohm
  C. The volt
  D. The henry

## Slide 55: T5C02 What is the basic unit of capacitance?
A. The farad
  B. The ohm
  C. The volt
  D. The henry

## Slide 56: T5C03 What is the ability to store energy in a magnetic field called?
  A. Admittance
  B. Capacitance
  C. Resistance
  D. Inductance

## Slide 57: T5C03 What is the ability to store energy in a magnetic field called?
  A. Admittance
  B. Capacitance
  C. Resistance
D. Inductance

## Slide 58: T5C04 What is the basic unit of inductance?
  A. The coulomb
  B. The farad
  C. The henry
  D. The ohm

## Slide 59: T5C04 What is the basic unit of inductance?
  A. The coulomb
  B. The farad
C. The henry
  D. The ohm

## Slide 60: T5C05 What is the unit of frequency?
  A. Hertz
  B. Henry
  C. Farad
  D. Tesla

## Slide 61: T5C05 What is the unit of frequency?
A. Hertz
  B. Henry
  C. Farad
  D. Tesla

## Slide 62: T5C06 What is the abbreviation that refers to radio frequency signals of all types?
  A. AF
  B. HF
  C. RF
  D. VHF

## Slide 63: T5C06 What is the abbreviation that refers to radio frequency signals of all types?
  A. AF
  B. HF
C. RF
  D. VHF

## Slide 64: T5C07 What is a usual name for electromagnetic waves that travel through space?
  A. Gravity waves
  B. Sound waves
  C. Radio waves
  D. Pressure waves

## Slide 65: T5C07 What is a usual name for electromagnetic waves that travel through space?
  A. Gravity waves
  B. Sound waves
C. Radio waves
  D. Pressure waves

## Slide 66: T5C08 What is the formula used to calculate electrical power in a DC circuit?
  A. Power (P) equals voltage (E) multiplied by current (I)
  B. Power (P) equals voltage (E) divided by current (I)
  C. Power (P) equals voltage (E) minus current (I)
  D. Power (P) equals voltage (E) plus current (I)

## Slide 67: Voltage, Current and Power
Radio and Electronic Fundamentals
<number>
Potential – Electromotive Force
  Electromotive Force (E)
  Units – Volts
  Unit Symbol V – 10V
  Measured across (parallel to load)
Current – Electron flow
  Current (I)
  Unites – Amps, Amperes
  Unit Symbol A – 0.1A
  Measured through (inline with load)
Power (P)
  Watts
  Units – Watts
  Unit Symbol W – 60W
P
I
E
P = I x E
Notes: <number>
Potential – Voltage or Electromotive force
Units are Volts named after Count Alessandro Giuseppe Antonio Anastasio Volta (Italian Inventor), invented the baterry.
Flow – Current, measured in amps, named after André-Marie Ampère (French) scientist and mathematician. I is used as the abbreviation because it referred to the Intensity of the current.
Power – Measured in Watts, named after James Watt (Scottish/British) inventor

## Slide 68: T5C08 What is the formula used to calculate electrical power in a DC circuit?
A. Power (P) equals voltage (E) multiplied by current (I)
  B. Power (P) equals voltage (E) divided by current (I)
  C. Power (P) equals voltage (E) minus current (I)
  D. Power (P) equals voltage (E) plus current (I)

## Slide 69: T5C09 How much power is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
  A. 138 watts
  B. 0.7 watts
  C. 23.8 watts
  D. 3.8 watts

## Slide 70: T5C09 How much power is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
Radio and Electronic Fundamentals
<number>
P
I
E
P = I x E
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 71: T5C09 How much power is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
Radio and Electronic Fundamentals
<number>
P
I
E
P = I * E
P = 10A x 13.8V = 138W
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 72: T5C09 How much power is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
A. 138 watts
  B. 0.7 watts
  C. 23.8 watts
  D. 3.8 watts

## Slide 73: T5C10 How much power is being used in a circuit when the applied voltage is 12 volts DC and the current is 2.5 amperes?
  A. 4.8 watts
  B. 30 watts
  C. 14.5 watts
  D. 0.208 watts

## Slide 74: T5C10 How much power is being used in a circuit when the applied voltage is 12 volts DC and the current is 2.5 amperes?
Radio and Electronic Fundamentals
<number>
P
I
E
P = I * E
P = 2.5 A x 12 V = 30 W
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 75: T5C10 How much power is being used in a circuit when the applied voltage is 12 volts DC and the current is 2.5 amperes?
  A. 4.8 watts
B. 30 watts
  C. 14.5 watts
  D. 0.208 watts

## Slide 76: T5C11 How many amperes are flowing in a circuit when the applied voltage is 12 volts DC and the load is 120 watts?
  A. 0.1 amperes
  B. 10 amperes
  C. 12 amperes
  D. 132 amperes

## Slide 77: T5C11 How many amperes are flowing in a circuit when the applied voltage is 12 volts DC and the load is 120 watts?
Radio and Electronic Fundamentals
<number>
P
I
E
I = P / E
I = 120 W  12 VDC = 10A
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 78: T5C11 How many amperes are flowing in a circuit when the applied voltage is 12 volts DC and the load is 120 watts?
  A. 0.1 amperes
B. 10 amperes
  C. 12 amperes
  D. 132 amperes

## Slide 79: T5D01 What formula is used to calculate current in a circuit?
  A. Current (I) equals voltage (E) multiplied by resistance (R)
  B. Current (I) equals voltage (E) divided by resistance (R)
  C. Current (I) equals voltage (E) added to resistance (R)
  D. Current (I) equals voltage (E) minus resistance (R)

## Slide 80: Ohm’s Law and Power Calculations
Radio and Electronic Fundamentals
<number>
E
I
R
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
P=Power (Watts)
To solve for a value, cover it with your finger and solve the remaining formula
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 81: T5D01 What formula is used to calculate current in a circuit?
  A. Current (I) equals voltage (E) multiplied by resistance (R)
B. Current (I) equals voltage (E) divided by resistance (R)
  C. Current (I) equals voltage (E) added to resistance (R)
  D. Current (I) equals voltage (E) minus resistance (R)

## Slide 82: T5D02 What formula is used to calculate voltage in a circuit?
  A. Voltage (E) equals current (I) multiplied by resistance (R)
  B. Voltage (E) equals current (I) divided by resistance (R)
  C. Voltage (E) equals current (I) added to resistance (R)
  D. Voltage (E) equals current (I) minus resistance (R)

## Slide 83: Ohm’s Law and Power Calculations
Radio and Electronic Fundamentals
<number>
E
I
R
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
P=Power (Watts)
To solve for a value, cover it with your finger and solve the remaining formula
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 84: T5D02 What formula is used to calculate voltage in a circuit?
A. Voltage (E) equals current (I) multiplied by resistance (R)
  B. Voltage (E) equals current (I) divided by resistance (R)
  C. Voltage (E) equals current (I) added to resistance (R)
  D. Voltage (E) equals current (I) minus resistance (R)

## Slide 85: T5D03 What formula is used to calculate resistance in a circuit?
  A. Resistance (R) equals voltage (E) multiplied by current (I)
  B. Resistance (R) equals voltage (E) divided by current (I)
  C. Resistance (R) equals voltage (E) added to current (I)
  D. Resistance (R) equals voltage (E) minus current (I)

## Slide 86: Ohm’s Law and Power Calculations
Radio and Electronic Fundamentals
<number>
E
I
R
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
P=Power (Watts)
To solve for a value, cover it with your finger and solve the remaining formula
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 87: T5D03 What formula is used to calculate resistance in a circuit?
  A. Resistance (R) equals voltage (E) multiplied by current (I)
B. Resistance (R) equals voltage (E) divided by current (I)
  C. Resistance (R) equals voltage (E) added to current (I)
  D. Resistance (R) equals voltage (E) minus current (I)

## Slide 88: T5D04 What is the resistance of a circuit in which a current of 3 amperes flows through a resistor connected to 90 volts?
  A. 3 ohms
  B. 30 ohms
  C. 93 ohms
  D. 270 ohms

## Slide 89: T5D04 What is the resistance of a circuit in which a current of 3 amperes flows through a resistor connected to 90 volts?
Radio and Electronic Fundamentals
<number>
E
I
R
R = E / I
R = 90 V  3 A = 30Ω
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 90: T5D04 What is the resistance of a circuit in which a current of 3 amperes flows through a resistor connected to 90 volts?
  A. 3 ohms
B. 30 ohms
  C. 93 ohms
  D. 270 ohms

## Slide 91: T5D05 What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
  A. 18 ohms
  B. 0.125 ohms
  C. 8 ohms
  D. 13.5 ohms

## Slide 92: T5D05 What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
Radio and Electronic Fundamentals
<number>
E
I
R
R = E / I
R = 12 V  1.5 A = 8 Ω
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 93: T5D05 What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
  A. 18 ohms
  B. 0.125 ohms
C. 8 ohms
  D. 13.5 ohms

## Slide 94: T5D06 What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
  A. 3 ohms
  B. 16 ohms
  C. 48 ohms
  D. 8 Ohms

## Slide 95: T5D06 What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
Radio and Electronic Fundamentals
<number>
E
I
R
R = E / I
R = 12 V  4 A = 3 Ω
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 96: T5D06 What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
A. 3 ohms
  B. 16 ohms
  C. 48 ohms
  D. 8 Ohms

## Slide 97: T5D07 What is the current flow in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
  A. 9600 amperes
  B. 200 amperes
  C. 0.667 amperes
  D. 1.5 amperes

## Slide 98: T5D07 What is the current flow in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
Radio and Electronic Fundamentals
<number>
E
I
R
I = E / R
I = 120V  80Ω = 1.5A
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 99: T5D07 What is the current flow in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
  A. 9600 amperes
  B. 200 amperes
  C. 0.667 amperes
D. 1.5 amperes

## Slide 100: T5D08 What is the current flowing through a 100-ohm resistor connected across 200 volts?
  A. 20,000 amperes
  B. 0.5 amperes
  C. 2 amperes
  D. 100 amperes

## Slide 101: T5D08 What is the current flowing through a 100-ohm resistor connected across 200 volts?
Radio and Electronic Fundamentals
<number>
E
I
R
I = E / R
I = 200V  100Ω = 2 A
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 102: T5D08 What is the current flowing through a 100-ohm resistor connected across 200 volts?
  A. 20,000 amperes
  B. 0.5 amperes
C. 2 amperes
  D. 100 amperes

## Slide 103: T5D09 What is the current flowing through a 24-ohm resistor connected across 240 volts?
  A. 24,000 amperes
  B. 0.1 amperes
  C. 10 amperes
  D. 216 amperes

## Slide 104: T5D09 What is the current flowing through a 24-ohm resistor connected across 240 volts?
Radio and Electronic Fundamentals
<number>
E
I
R
I = E / R
I = 240V  24Ω = 10 A
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 105: T5D09 What is the current flowing through a 24-ohm resistor connected across 240 volts?
  A. 24,000 amperes
  B. 0.1 amperes
C. 10 amperes
  D. 216 amperes

## Slide 106: T5D10 What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
  A. 1 volt
  B. 0.25 volts
  C. 2.5 volts
  D. 1.5 volts

## Slide 107: T5D10 What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
Radio and Electronic Fundamentals
<number>
E
I
R
E = I * R
E = 0.5A x 2Ω = 1V
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 108: T5D10 What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
A. 1 volt
  B. 0.25 volts
  C. 2.5 volts
  D. 1.5 volts

## Slide 109: T5D11 What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
  A. 1 volt
  B. 10 volts
  C. 11 volts
  D. 9 volts

## Slide 110: T5D11 What is the voltage across a 10-ohm resistor if a current of 1 amperes flows through it?
Radio and Electronic Fundamentals
<number>
E
I
R
E = I * R
E = 1 A x 10Ω = 10V
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 111: T5D11 What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
  A. 1 volt
B. 10 volts
  C. 11 volts
  D. 9 volts

## Slide 112: T5D12 What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
  A. 8 volts
  B. 0.2 volts
  C. 12 volts
  D. 20 volts

## Slide 113: T5D12 What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
Radio and Electronic Fundamentals
<number>
E
I
R
E = I * R
E = 2 A x 10Ω = 20V
Notes: <number>
There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 114: T5D12 What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
  A. 8 volts
  B. 0.2 volts
  C. 12 volts
D. 20 volts

## Slide 115: T5 – Electrical Principles, Electronic Principles, Math for Electronics 4 exam questions – 4 groups
Radio and Electronic Fundamentals
<number>
Notes: <number>
http://www.microhams.com
Created by Scott N7SS