## Slide 1: SUBELEMENT T7 [4 Exam Questions - 4 Groups]
Station equipment, common transmitter and receiver problems, antenna measurements and troubleshooting, basic repair and testing.
Notes: <number>
2010 Technician Class (Element 2) Master syllabus
Released 1 February, 2010
396 questions in 35 sections
These slides are free to use and are available from http://www.microhams.com. Changes are allowed if Microhams branding is left in place (feel free to ad your own). Any content additions should be forwarded to the author, Scott N7SS at N7SS@arrl.net so they can be rolled into future versions and available for everyone.

## Slide 2: T7 – Station Equipment and Troubleshooting
<number>
Microhams 2010 Technician
T7A – Station radios; receivers, transmitters, transceivers
T7B – Common transmitter and receiver problems; symptoms of overload and overdrive, distortion, interference, over and under modulation, RF feedback, off frequency signals; fading and noise; problems with digital communications interfaces
T7C – Antenna measurements and troubleshooting; measuring SWR, dummy loads, feed line failure modes
T7D – Basic repair and testing; soldering, use of a voltmeter, ammeter, and ohmmeter

## Slide 3: T7A01 What is the function of a product detector?
  A. Detect phase modulated signals
  B. Demodulate FM signals
  C. Detect CW and SSB signals
  D. Combine speech and RF signals

## Slide 4: T7A01 What is the function of a product detector?
  A. Detect phase modulated signals
  B. Demodulate FM signals
C. Detect CW and SSB signals
  D. Combine speech and RF signals

## Slide 5: T7A02 What type of receiver is shown in Figure T6?
  A. Direct conversion
  B. Super-regenerative
  C. Single-conversion superheterodyne
  D. Dual-conversion superheterodyne

## Slide 6: T7A02 What type of receiver is shown in Figure T6?
  A. Direct conversion
  B. Super-regenerative
C. Single-conversion superheterodyne
  D. Dual-conversion superheterodyne

## Slide 7: T7A03 What is the function of a mixer in a superheterodyne receiver?
  A. To reject signals outside of the desired passband
  B. To combine signals from several stations together
  C. To shift the incoming signal to an intermediate frequency
  D. To connect the receiver with an auxiliary device, such as a TNC

## Slide 8: T7A03 What is the function of a mixer in a superheterodyne receiver?
  A. To reject signals outside of the desired passband
  B. To combine signals from several stations together
C. To shift the incoming signal to an intermediate frequency
  D. To connect the receiver with an auxiliary device, such as a TNC

## Slide 9: T7A04 What circuit is pictured in Figure T7, if block 1 is a frequency discriminator?
  A. A double-conversion receiver
  B. A regenerative receiver
  C. A superheterodyne receiver
  D. An FM receiver

## Slide 10: T7A04 What circuit is pictured in Figure T7, if block 1 is a frequency discriminator?
  A. A double-conversion receiver
  B. A regenerative receiver
  C. A superheterodyne receiver
D. An FM receiver

## Slide 11: T7A05 What is the function of block 1 if figure T4 is a simple CW transmitter?
  A. Reactance modulator
  B. Product detector
  C. Low-pass filter
  D. Oscillator

## Slide 12: T7A05 What is the function of block 1 if figure T4 is a simple CW transmitter?
  A. Reactance modulator
  B. Product detector
  C. Low-pass filter
D. Oscillator

## Slide 13: T7A06 What device takes the output of a low-powered 28 MHz SSB exciter and produces a 222 MHz output signal?
  A. High-pass filter
  B. Low-pass filter
  C. Transverter
  D. Phase converter

## Slide 14: T7A06 What device takes the output of a low-powered 28 MHz SSB exciter and produces a 222 MHz output signal?
  A. High-pass filter
  B. Low-pass filter
C. Transverter
  D. Phase converter

## Slide 15: T7A07 If figure T5 represents a transceiver in which block 1 is the transmitter portion and block 3 is the receiver portion, what is the function of block 2?
  A. A balanced modulator
  B. A transmit-receive switch
  C. A power amplifier
  D. A high-pass filter

## Slide 16: T7A07 If figure T5 represents a transceiver in which block 1 is the transmitter portion and block 3 is the receiver portion, what is the function of block 2?
  A. A balanced modulator
B. A transmit-receive switch
  C. A power amplifier
  D. A high-pass filter

## Slide 17: T7A08 Which of the following circuits combines a speech signal and an RF carrier?
  A. Beat frequency oscillator
  B. Discriminator
  C. Modulator
  D. Noise blanker

## Slide 18: T7A08 Which of the following circuits combines a speech signal and an RF carrier?
  A. Beat frequency oscillator
  B. Discriminator
C. Modulator
  D. Noise blanker

## Slide 19: T7A09 Which of the following devices is most useful for VHF weak-signal communication?
  A. A quarter-wave vertical antenna
  B. A multi-mode VHF transceiver
  C. An omni-directional antenna
  D. A mobile VHF FM transceiver

## Slide 20: T7A09 Which of the following devices is most useful for VHF weak-signal communication?
  A. A quarter-wave vertical antenna
B. A multi-mode VHF transceiver
  C. An omni-directional antenna
  D. A mobile VHF FM transceiver

## Slide 21: T7A10 What device increases the low-power output from a handheld transceiver?
  A. A voltage divider
  B. An RF power amplifier
  C. An impedance network
  D. A voltage regulator

## Slide 22: T7A10 What device increases the low-power output from a handheld transceiver?
  A. A voltage divider
B. An RF power amplifier
  C. An impedance network
  D. A voltage regulator

## Slide 23: T7A11 Which of the following circuits demodulates FM signals?
  A. Limiter
  B. Discriminator
  C. Product detector
  D. Phase inverter

## Slide 24: T7A11 Which of the following circuits demodulates FM signals?
  A. Limiter
B. Discriminator
  C. Product detector
  D. Phase inverter

## Slide 25: T7A12 Which term describes the ability of a receiver to discriminate between multiple signals?
  A. Tuning rate
  B. Sensitivity
  C. Selectivity
  D. Noise floor

## Slide 26: T7A12 Which term describes the ability of a receiver to discriminate between multiple signals?
  A. Tuning rate
  B. Sensitivity
C. Selectivity
  D. Noise floor

## Slide 27: T7A13 Where is an RF preamplifier installed?
  A. Between the antenna and receiver
  B. At the output of the transmitter's power amplifier
  C. Between a transmitter and antenna tuner
  D. At the receiver's audio output

## Slide 28: T7A13 Where is an RF preamplifier installed?
A. Between the antenna and receiver
  B. At the output of the transmitter's power amplifier
  C. Between a transmitter and antenna tuner
  D. At the receiver's audio output

## Slide 29: T7B01 What can you do if you are told your FM handheld or mobile transceiver is over deviating?
  A. Talk louder into the microphone
  B. Let the transceiver cool off
  C. Change to a higher power level
  D. Talk farther away from the microphone

## Slide 30: T7B01 What can you do if you are told your FM handheld or mobile transceiver is over deviating?
  A. Talk louder into the microphone
  B. Let the transceiver cool off
  C. Change to a higher power level
D. Talk farther away from the microphone

## Slide 31: T7B02 What is meant by fundamental overload in reference to a receiver?
  A. Too much voltage from the power supply
  B. Too much current from the power supply
  C. Interference caused by very strong signals
  D. Interference caused by turning the volume up too high

## Slide 32: T7B02 What is meant by fundamental overload in reference to a receiver?
  A. Too much voltage from the power supply
  B. Too much current from the power supply
C. Interference caused by very strong signals
  D. Interference caused by turning the volume up too high

## Slide 33: T7B03 Which of the following may be a cause of radio frequency interference?
  A. Fundamental overload
  B. Harmonics
  C. Spurious emissions
  D. All of these choices are correct

## Slide 34: T7B03 Which of the following may be a cause of radio frequency interference?
  A. Fundamental overload
  B. Harmonics
  C. Spurious emissions
D. All of these choices are correct

## Slide 35: T7B04 What is the most likely cause of interference to a non-cordless telephone from a nearby transmitter?
  A. Harmonics from the transmitter
  B. The telephone is inadvertently acting as a radio receiver
  C. Poor station grounding
  D. Improper transmitter adjustment

## Slide 36: T7B04 What is the most likely cause of interference to a non-cordless telephone from a nearby transmitter?
  A. Harmonics from the transmitter
B. The telephone is inadvertently acting as a radio receiver
  C. Poor station grounding
  D. Improper transmitter adjustment

## Slide 37: T7B05 What is a logical first step when attempting to cure a radio frequency interference problem in a nearby telephone?
  A. Install a low-pass filter at the transmitter
  B. Install a high-pass filter at the transmitter
  C. Install an RF filter at the telephone
  D. Improve station grounding

## Slide 38: T7B05 What is a logical first step when attempting to cure a radio frequency interference problem in a nearby telephone?
  A. Install a low-pass filter at the transmitter
  B. Install a high-pass filter at the transmitter
C. Install an RF filter at the telephone
  D. Improve station grounding

## Slide 39: T7B06 What should you do first if someone tells you that your station's transmissions are interfering with their radio or TV reception?
  A. Make sure that your station is functioning properly and that it does not cause interference to your own television
  B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
  C. Tell them that your license gives you the right to transmit and nothing can be done to reduce the interference
  D. Continue operating normally because your equipment cannot possibly cause any interference

## Slide 40: T7B06 What should you do first if someone tells you that your station's transmissions are interfering with their radio or TV reception?
A. Make sure that your station is functioning properly and that it does not cause interference to your own television
  B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
  C. Tell them that your license gives you the right to transmit and nothing can be done to reduce the interference
  D. Continue operating normally because your equipment cannot possibly cause any interference

## Slide 41: T7B07 Which of the following may be useful in correcting a radio frequency interference problem?
  A. Snap-on ferrite chokes
  B. Low-pass and high-pass filters
  C. Band-reject and band-pass filters
  D. All of these choices are correct

## Slide 42: T7B07 Which of the following may be useful in correcting a radio frequency interference problem?
  A. Snap-on ferrite chokes
  B. Low-pass and high-pass filters
  C. Band-reject and band-pass filters
D. All of these choices are correct

## Slide 43: T7B08 What should you do if a "Part 15" device in your neighbor's home is causing harmful interference to your amateur station?
  A. Work with your neighbor to identify the offending device
  B. Politely inform your neighbor about the rules that require him to stop using the device if it causes interference
  C. Check your station and make sure it meets the standards of good amateur practice
  D. All of these choices are correct

## Slide 44: T7B08 What should you do if a "Part 15" device in your neighbor's home is causing harmful interference to your amateur station?
  A. Work with your neighbor to identify the offending device
  B. Politely inform your neighbor about the rules that require him to stop using the device if it causes interference
  C. Check your station and make sure it meets the standards of good amateur practice
D. All of these choices are correct

## Slide 45: T7B09 What could be happening if another operator reports a variable high-pitched whine on the audio from your mobile transmitter?
  A. Your microphone is picking up noise from an open window
  B. You have the volume on your receiver set too high
  C. You need to adjust your squelch control
  D. Noise on the vehicle's electrical system is being transmitted along with your speech audio

## Slide 46: T7B09 What could be happening if another operator reports a variable high-pitched whine on the audio from your mobile transmitter?
  A. Your microphone is picking up noise from an open window
  B. You have the volume on your receiver set too high
  C. You need to adjust your squelch control
D. Noise on the vehicle's electrical system is being transmitted along with your speech audio

## Slide 47: T7B10 What might be the problem if you receive a report that your audio signal through the repeater is distorted or unintelligible?
  A. Your transmitter may be slightly off frequency
  B. Your batteries may be running low
  C. You could be in a bad location
  D. All of these choices are correct

## Slide 48: T7B10 What might be the problem if you receive a report that your audio signal through the repeater is distorted or unintelligible?
  A. Your transmitter may be slightly off frequency
  B. Your batteries may be running low
  C. You could be in a bad location
D. All of these choices are correct

## Slide 49: T7B11 What is a symptom of RF feedback in a transmitter or transceiver?
  A. Excessive SWR at the antenna connection
  B. The transmitter will not stay on the desired frequency
  C. Reports of garbled, distorted, or unintelligible transmissions
  D. Frequent blowing of power supply fuses

## Slide 50: T7B11 What is a symptom of RF feedback in a transmitter or transceiver?
  A. Excessive SWR at the antenna connection
  B. The transmitter will not stay on the desired frequency
C. Reports of garbled, distorted, or unintelligible transmissions
  D. Frequent blowing of power supply fuses

## Slide 51: T7B12 What does the acronym "BER" mean when applied to digital communications systems?
  A. Baud Enhancement Recovery
  B. Baud Error Removal
  C. Bit Error Rate
  D. Bit Exponent Resource

## Slide 52: T7B12 What does the acronym "BER" mean when applied to digital communications systems?
  A. Baud Enhancement Recovery
  B. Baud Error Removal
C. Bit Error Rate
  D. Bit Exponent Resource

## Slide 53: T7C01 What is the primary purpose of a dummy load?
  A. To prevent the radiation of signals when making tests
  B. To prevent over-modulation of your transmitter
  C. To improve the radiation from your antenna
  D. To improve the signal to noise ratio of your receiver

## Slide 54: T7C01 What is the primary purpose of a dummy load?
A. To prevent the radiation of signals when making tests
  B. To prevent over-modulation of your transmitter
  C. To improve the radiation from your antenna
  D. To improve the signal to noise ratio of your receiver

## Slide 55: T7C02 Which of the following instruments can be used to determine if an antenna is resonant at the desired operating frequency?
  A. A VTVM
  B. An antenna analyzer
  C. A "Q" meter
  D. A frequency counter

## Slide 56: T7C02 Which of the following instruments can be used to determine if an antenna is resonant at the desired operating frequency?
  A. A VTVM
B. An antenna analyzer
  C. A "Q" meter
  D. A frequency counter

## Slide 57: T7C03 What, in general terms, is standing wave ratio (SWR)?
  A. A measure of how well a load is matched to a transmission line
  B. The ratio of high to low impedance in a feedline
  C. The transmitter efficiency ratio
  D. An indication of the quality of your station's ground connection

## Slide 58: T7C03 What, in general terms, is standing wave ratio (SWR)?
A. A measure of how well a load is matched to a transmission line
  B. The ratio of high to low impedance in a feedline
  C. The transmitter efficiency ratio
  D. An indication of the quality of your station's ground connection

## Slide 59: T7C04 What reading on an SWR meter indicates a perfect impedance match between the antenna and the feedline?
  A. 2 to 1
  B. 1 to 3
  C. 1 to 1
  D. 10 to 1

## Slide 60: T7C04 What reading on an SWR meter indicates a perfect impedance match between the antenna and the feedline?
  A. 2 to 1
  B. 1 to 3
C. 1 to 1
  D. 10 to 1

## Slide 61: T7C05 What is the approximate SWR value above which the protection circuits in most solid-state transmitters begin to reduce transmitter power?
  A. 2 to 1
  B. 1 to 2
  C. 6 to 1
  D. 10 to 1

## Slide 62: T7C05 What is the approximate SWR value above which the protection circuits in most solid-state transmitters begin to reduce transmitter power?
A. 2 to 1
  B. 1 to 2
  C. 6 to 1
  D. 10 to 1

## Slide 63: T7C06 What does an SWR reading of 4:1 mean?
  A. An antenna loss of 4 dB
  B. A good impedance match
  C. An antenna gain of 4
  D. An impedance mismatch

## Slide 64: T7C06 What does an SWR reading of 4:1 mean?
  A. An antenna loss of 4 dB
  B. A good impedance match
  C. An antenna gain of 4
D. An impedance mismatch

## Slide 65: T7C07 What happens to power lost in a feedline?
  A. It increases the SWR
  B. It comes back into your transmitter and could cause damage
  C. It is converted into heat
  D. It can cause distortion of your signal

## Slide 66: T7C07 What happens to power lost in a feedline?
  A. It increases the SWR
  B. It comes back into your transmitter and could cause damage
C. It is converted into heat
  D. It can cause distortion of your signal

## Slide 67: T7C08 What instrument other than an SWR meter could you use to determine if a feedline and antenna are properly matched?
  A. Voltmeter
  B. Ohmmeter
  C. Iambic pentameter
  D. Directional wattmeter

## Slide 68: T7C08 What instrument other than an SWR meter could you use to determine if a feedline and antenna are properly matched?
  A. Voltmeter
  B. Ohmmeter
  C. Iambic pentameter
D. Directional wattmeter

## Slide 69: T7C09 Which of the following is the most common cause for failure of coaxial cables?
  A. Moisture contamination
  B. Gamma rays
  C. The velocity factor exceeds 1.0
  D. Overloading

## Slide 70: T7C09 Which of the following is the most common cause for failure of coaxial cables?
A. Moisture contamination
  B. Gamma rays
  C. The velocity factor exceeds 1.0
  D. Overloading

## Slide 71: T7C10 Why should the outer jacket of coaxial cable be resistant to ultraviolet light?
  A. Ultraviolet resistant jackets prevent harmonic radiation
  B. Ultraviolet light can increase losses in the cable's jacket
  C. Ultraviolet and RF signals can mix together, causing interference
  D. Ultraviolet light can damage the jacket and allow water to enter the cable

## Slide 72: T7C10 Why should the outer jacket of coaxial cable be resistant to ultraviolet light?
  A. Ultraviolet resistant jackets prevent harmonic radiation
  B. Ultraviolet light can increase losses in the cable's jacket
  C. Ultraviolet and RF signals can mix together, causing interference
D. Ultraviolet light can damage the jacket and allow water to enter the cable

## Slide 73: T7C11 What is a disadvantage of "air core" coaxial cable when compared to foam or solid dielectric types?
  A. It has more loss per foot
  B. It cannot be used for VHF or UHF antennas
  C. It requires special techniques to prevent water absorption
  D. It cannot be used at below freezing temperatures

## Slide 74: T7C11 What is a disadvantage of "air core" coaxial cable when compared to foam or solid dielectric types?
  A. It has more loss per foot
  B. It cannot be used for VHF or UHF antennas
C. It requires special techniques to prevent water absorption
  D. It cannot be used at below freezing temperatures

## Slide 75: T7D01 Which instrument would you use to measure electric potential or electromotive force?
  A. An ammeter
  B. A voltmeter
  C. A wavemeter
  D. An ohmmeter

## Slide 76: T7D01 Which instrument would you use to measure electric potential or electromotive force?
  A. An ammeter
B. A voltmeter
  C. A wavemeter
  D. An ohmmeter

## Slide 77: T7D02 What is the correct way to connect a voltmeter to a circuit?
  A. In series with the circuit
  B. In parallel with the circuit
  C. In quadrature with the circuit
  D. In phase with the circuit

## Slide 78: T7D02 What is the correct way to connect a voltmeter to a circuit?
  A. In series with the circuit
B. In parallel with the circuit
  C. In quadrature with the circuit
  D. In phase with the circuit

## Slide 79: T7D03 How is an ammeter usually connected to a circuit?
  A. In series with the circuit
  B. In parallel with the circuit
  C. In quadrature with the circuit
  D. In phase with the circuit

## Slide 80: T7D03 How is an ammeter usually connected to a circuit?
A. In series with the circuit
  B. In parallel with the circuit
  C. In quadrature with the circuit
  D. In phase with the circuit

## Slide 81: T7D04 Which instrument is used to measure electric current?
  A. An ohmmeter
  B. A wavemeter
  C. A voltmeter
  D. An ammeter

## Slide 82: T7D04 Which instrument is used to measure electric current?
  A. An ohmmeter
  B. A wavemeter
  C. A voltmeter
D. An ammeter

## Slide 83: T7D05 What instrument is used to measure resistance?
  A. An oscilloscope
  B. A spectrum analyzer
  C. A noise bridge
  D. An ohmmeter

## Slide 84: T7D05 What instrument is used to measure resistance?
  A. An oscilloscope
  B. A spectrum analyzer
  C. A noise bridge
D. An ohmmeter

## Slide 85: T7D06 Which of the following might damage a multimeter?
  A. Measuring a voltage too small for the chosen scale
  B. Leaving the meter in the milliamps position overnight
  C. Attempting to measure voltage when using the resistance setting
  D. Not allowing it to warm up properly

## Slide 86: T7D06 Which of the following might damage a multimeter?
  A. Measuring a voltage too small for the chosen scale
  B. Leaving the meter in the milliamps position overnight
C. Attempting to measure voltage when using the resistance setting
  D. Not allowing it to warm up properly

## Slide 87: T7D07 Which of the following measurements are commonly made using a multimeter?
  A. SWR and RF power
  B. Signal strength and noise
  C. Impedance and reactance
  D. Voltage and resistance

## Slide 88: T7D07 Which of the following measurements are commonly made using a multimeter?
  A. SWR and RF power
  B. Signal strength and noise
  C. Impedance and reactance
D. Voltage and resistance

## Slide 89: T7D08 Which of the following types of solder is best for radio and electronic use?
  A. Acid-core solder
  B. Silver solder
  C. Rosin-core solder
  D. Aluminum solder

## Slide 90: T7D08 Which of the following types of solder is best for radio and electronic use?
  A. Acid-core solder
  B. Silver solder
C. Rosin-core solder
  D. Aluminum solder

## Slide 91: T7D09 What is the characteristic appearance of a "cold" solder joint?
  A. Dark black spots
  B. A bright or shiny surface
  C. A grainy or dull surface
  D. A greenish tint

## Slide 92: T7D09 What is the characteristic appearance of a "cold" solder joint?
  A. Dark black spots
  B. A bright or shiny surface
C. A grainy or dull surface
  D. A greenish tint

## Slide 93: T7D10 What is probably happening when an ohmmeter, connected across a circuit, initially indicates a low resistance and then shows increasing resistance with time?
  A. The ohmmeter is defective
  B. The circuit contains a large capacitor
  C. The circuit contains a large inductor
  D. The circuit is a relaxation oscillator

## Slide 94: T7D10 What is probably happening when an ohmmeter, connected across a circuit, initially indicates a low resistance and then shows increasing resistance with time?
  A. The ohmmeter is defective
B. The circuit contains a large capacitor
  C. The circuit contains a large inductor
  D. The circuit is a relaxation oscillator

## Slide 95: T7D11 Which of the following precautions should be taken when measuring circuit resistance with an ohmmeter?
  A. Ensure that the applied voltages are correct
  B. Ensure that the circuit is not powered
  C. Ensure that the circuit is grounded
  D. Ensure that the circuit is operating at the correct frequency

## Slide 96: T7D11 Which of the following precautions should be taken when measuring circuit resistance with an ohmmeter?
  A. Ensure that the applied voltages are correct
B. Ensure that the circuit is not powered
  C. Ensure that the circuit is grounded
  D. Ensure that the circuit is operating at the correct frequency

## Slide 97: SUBELEMENT T7 [4 exam questions – 4 groups]
<number>
Microhams 2010 Technician
Notes: <number>
http://www.microhams.com
Created by Scott N7SS