## Slide 1: SUBELEMENT T8 [4 Exam Questions – 4 Groups]
Modulation modes; amateur satellite operation, operating activities, non-voice communications
Notes: <number>
2010 Technician Class (Element 2) Master syllabus
Released 1 February, 2010
396 questions in 35 sections
These slides are free to use and are available from http://www.microhams.com. Changes are allowed if Microhams branding is left in place (feel free to ad your own). Any content additions should be forwarded to the author, Scott N7SS at N7SS@arrl.net so they can be rolled into future versions and available for everyone.

## Slide 2: T8 - Modulation modes, amateur satellite operation, operating activities
<number>
Microhams 2010 Technician
T8A - Modulation modes; bandwidth of various signals
T8B - Amateur satellite operation; Doppler shift, basic orbits, operating protocols
T8C - Operating activities; radio direction finding, radio control, contests, special event stations, basic linking over Internet
T8D - Non-voice communications; image data, digital modes, CW, packet, PSK31

## Slide 3: Sample Emission Modes
Communications Modes and Methods
<number>
Mode | Type | Bandwidth | Content
CW | Telegraphy | 10 Hz | Text Data
SSB | Telephony | 2800 Hz | Voice
AM | Telephony | 6 kHz | Voice
FM | Telephony | 5-15 kHz | Voice
SSTV / Fax | Image | 2800 Hz | Image
ATV | Image | 6 MHz | Image
PSK31 | Data | 31 Hz | Text Data
RTTY | Data | 250 Hz | Text Data
Pactor (I, II, III) | Data | 500-2800 Hz | Binary Data
AX.25 Packet | Data | 10-20 kHz | Binary Data

## Slide 4: Amplitude Modulation
Communications Modes and Methods
<number>
An unmodulated RF
carrier wave
A carrier wave amplitude
modulated (AM) with a simple audio tone
Notes: <number>
Note the identical sidebands. They peak and dip together.

## Slide 5: Amplitude Modulation
Communications Modes and Methods
<number>
An unmodulated RF
carrier requires narrow
bandwidth
Modulation of the carrier
creates sidebands. This
requires more bandwidth.
Transmitter power is spread across this bandwidth

## Slide 6: AM and SSB
Communications Modes and Methods
<number>
The carrier contains no
audio information.
The sidebands contain
duplicate audio information
By filtering out the carrier and one sideband,
we save spectrum and concentrate our RF
energy into a narrower bandwidth. SSB is
therefore more efficient.

## Slide 7: Frequency Modulation
Communications Modes and Methods
<number>
Unmodulated carrier, full power at all times
Waveform of modulating signal
Modulated carrier with frequency deviation and constant amplitude
“Over modulation” called “over deviation” on FM, causes the signal to become wider and potentially cause adjacent channel interference

## Slide 8: Common required Bandwidth
Communications Modes and Methods
<number>
CW – 5-10Hz
Phone / Voice
  SSB - 2-3 kHz
  AM – 4-6 kHz
  FM – 5-15 kHz
Digital
  PSK31 – 31 Hz
  RTTY – 250 Hz
Slow Scan TV – 3KHz
Fast Scan TV – 6Mhz

## Slide 9: Amateur Television Signal
Communications Modes and Methods
<number>
A 6 MHz ATV video channel with the video carrier 1.25 MHz up from the lower edge. The color subcarrier is at 3.58 MHz and the sound subcarrier at 4.5 MHz above the video carrier.
The Luminance, Chrominance and Audio carriers are visible in the spectrum plot at left

## Slide 10: T8A01 Which of the following is a form of amplitude modulation?
  A. Spread-spectrum
  B. Packet radio
  C. Single sideband
  D. Phase shift keying

## Slide 11: T8A01 Which of the following is a form of amplitude modulation?
  A. Spread-spectrum
  B. Packet radio
C. Single sideband
  D. Phase shift keying

## Slide 12: T8A02 What type of modulation is most commonly used for VHF packet radio transmissions?
  A. FM
  B. SSB
  C. AM
  D. Spread Spectrum

## Slide 13: T8A02 What type of modulation is most commonly used for VHF packet radio transmissions?
A. FM
  B. SSB
  C. AM
  D. Spread Spectrum

## Slide 14: T8A03 Which type of voice modulation is most often used for long-distance or weak signal contacts on the VHF and UHF bands?
  A. FM
  B. AM
  C. SSB
  D. PM

## Slide 15: T8A03 Which type of voice modulation is most often used for long-distance or weak signal contacts on the VHF and UHF bands?
  A. FM
  B. AM
C. SSB
  D. PM

## Slide 16: T8A04 Which type of modulation is most commonly used for VHF and UHF voice repeaters?
  A. AM
  B. SSB
  C. PSK
  D. FM

## Slide 17: T8A04 Which type of modulation is most commonly used for VHF and UHF voice repeaters?
  A. AM
  B. SSB
  C. PSK
D. FM

## Slide 18: T8A05 Which of the following types of emission has the narrowest bandwidth?
  A. FM voice
  B. SSB voice
  C. CW
  D. Slow-scan TV

## Slide 19: T8A05 Which of the following types of emission has the narrowest bandwidth?
  A. FM voice
  B. SSB voice
C. CW
  D. Slow-scan TV

## Slide 20: T8A06 Which sideband is normally used for 10 meter HF, VHF and UHF single-sideband communications?
  A. Upper sideband
  B. Lower sideband
  C. Suppressed sideband
  D. Inverted sideband

## Slide 21: T8A06 Which sideband is normally used for 10 meter HF, VHF and UHF single-sideband communications?
A. Upper sideband
  B. Lower sideband
  C. Suppressed sideband
  D. Inverted sideband

## Slide 22: T8A07 What is the primary advantage of single sideband over FM for voice transmissions?
  A. SSB signals are easier to tune
  B. SSB signals are less susceptible to interference
  C. SSB signals have narrower bandwidth
  D. All of these choices are correct

## Slide 23: T8A07 What is the primary advantage of single sideband over FM for voice transmissions?
  A. SSB signals are easier to tune
  B. SSB signals are less susceptible to interference
C. SSB signals have narrower bandwidth
  D. All of these choices are correct

## Slide 24: T8A08 What is the approximate bandwidth of a single sideband voice signal?
  A. 1 kHz
  B. 3 kHz
  C. 6 kHz
  D. 15 kHz

## Slide 25: T8A08 What is the approximate bandwidth of a single sideband voice signal?
  A. 1 kHz
B. 3 kHz
  C. 6 kHz
  D. 15 kHz

## Slide 26: T8A09 What is the approximate bandwidth of a VHF repeater FM phone signal?
  A. Less than 500 Hz
  B. About 150 kHz
  C. Between 5 and 15 kHz
  D. Between 50 and 125 kHz

## Slide 27: T8A09 What is the approximate bandwidth of a VHF repeater FM phone signal?
  A. Less than 500 Hz
  B. About 150 kHz
C. Between 5 and 15 kHz
  D. Between 50 and 125 kHz

## Slide 28: T8A10 What is the typical bandwidth of analog fast-scan TV transmissions on the 70 cm band?
  A. More than 10 MHz
  B. About 6 MHz
  C. About 3 MHz
  D. About 1 MHz

## Slide 29: T8A10 What is the typical bandwidth of analog fast-scan TV transmissions on the 70 cm band?
  A. More than 10 MHz
B. About 6 MHz
  C. About 3 MHz
  D. About 1 MHz

## Slide 30: T8A11 What is the approximate maximum bandwidth required to transmit a CW signal?
  A. 2.4 kHz
  B. 150 Hz
  C. 1000 Hz
  D. 15 kHz

## Slide 31: T8A11 What is the approximate maximum bandwidth required to transmit a CW signal?
  A. 2.4 kHz
B. 150 Hz
  C. 1000 Hz
  D. 15 kHz

## Slide 32: Susan J. Helms, KC7NHZ Flight Engineer - ISS
Special Operation
<number>
Notes: <number>
Most astronauts are licensed hams. Most often they get their Technician licenses so they are allowed to operate the ISS radio station.
Photo from NASA

## Slide 33: Doppler Shift
Special Operation
<number>
Doppler shift is a change in frequency as an object moves. The wave in front of the object is compressed and expanded behind.
To a fixed observer, the shortened wavelength in front causes the frequency to increase. As the object passes, the longer wavelength behind will cause the frequency to shift down.

## Slide 34: T8B01 Who may be the control operator of a station communicating through an amateur satellite or space station?
  A. Only an Amateur Extra Class operator
  B. A General Class licensee or higher licensee who has a satellite operator certification
  C. Only an Amateur Extra Class operator who is also an AMSAT member
  D. Any amateur whose license privileges allow them to transmit on the satellite uplink frequency

## Slide 35: T8B01 Who may be the control operator of a station communicating through an amateur satellite or space station?
  A. Only an Amateur Extra Class operator
  B. A General Class licensee or higher licensee who has a satellite operator certification
  C. Only an Amateur Extra Class operator who is also an AMSAT member
D. Any amateur whose license privileges allow them to transmit on the satellite uplink frequency

## Slide 36: T8B02 How much transmitter power should be used on the uplink frequency of an amateur satellite or space station?
  A. The maximum power of your transmitter
  B. The minimum amount of power needed to complete the contact
  C. No more than half the rating of your linear amplifier
  D. Never more than 1 watt

## Slide 37: T8B02 How much transmitter power should be used on the uplink frequency of an amateur satellite or space station?
  A. The maximum power of your transmitter
B. The minimum amount of power needed to complete the contact
  C. No more than half the rating of your linear amplifier
  D. Never more than 1 watt

## Slide 38: T8B03 Which of the following can be done using an amateur radio satellite?
  A. Talk to amateur radio operators in other countries
  B. Get global positioning information
  C. Make telephone calls
  D. All of these choices are correct

## Slide 39: T8B03 Which of the following can be done using an amateur radio satellite?
A. Talk to amateur radio operators in other countries
  B. Get global positioning information
  C. Make telephone calls
  D. All of these choices are correct

## Slide 40: T8B04 Which amateur stations may make contact with an amateur station on the International Space Station using 2 meter and 70 cm band amateur radio frequencies?
  A. Only members of amateur radio clubs at NASA facilities
  B. Any amateur holding a Technician or higher class license
  C. Only the astronaut's family members who are hams
  D. You cannot talk to the ISS on amateur radio frequencies

## Slide 41: T8B04 Which amateur stations may make contact with an amateur station on the International Space Station using 2 meter and 70 cm band amateur radio frequencies?
  A. Only members of amateur radio clubs at NASA facilities
B. Any amateur holding a Technician or higher class license
  C. Only the astronaut's family members who are hams
  D. You cannot talk to the ISS on amateur radio frequencies

## Slide 42: T8B05 What is a satellite beacon?
  A. The primary transmit antenna on the satellite
  B. An indicator light that that shows where to point your antenna
  C. A reflective surface on the satellite
  D. A transmission from a space station that contains information about a satellite

## Slide 43: T8B05 What is a satellite beacon?
  A. The primary transmit antenna on the satellite
  B. An indicator light that that shows where to point your antenna
  C. A reflective surface on the satellite
D. A transmission from a space station that contains information about a satellite

## Slide 44: T8B06 What can be used to determine the time period during which an amateur satellite or space station can be accessed?
  A. A GPS receiver
  B. A field strength meter
  C. A telescope
  D. A satellite tracking program

## Slide 45: T8B06 What can be used to determine the time period during which an amateur satellite or space station can be accessed?
  A. A GPS receiver
  B. A field strength meter
  C. A telescope
D. A satellite tracking program

## Slide 46: T8B07 With regard to satellite communications, what is Doppler shift?
  A. A change in the satellite orbit
  B. A mode where the satellite receives signals on one band and transmits on another
  C. An observed change in signal frequency caused by relative motion between the satellite and the earth station
  D. A special digital communications mode for some satellites

## Slide 47: T8B07 With regard to satellite communications, what is Doppler shift?
  A. A change in the satellite orbit
  B. A mode where the satellite receives signals on one band and transmits on another
C. An observed change in signal frequency caused by relative motion between the satellite and the earth station
  D. A special digital communications mode for some satellites

## Slide 48: T8B08 What is meant by the statement that a satellite is operating in "mode U/V"?
  A. The satellite uplink is in the 15 meter band and the downlink is in the 10 meter band
  B. The satellite uplink is in the 70 cm band and the downlink is in the 2 meter band
  C. The satellite operates using ultraviolet frequencies
  D. The satellite frequencies are usually variable

## Slide 49: T8B08 What is meant by the statement that a satellite is operating in "mode U/V"?
  A. The satellite uplink is in the 15 meter band and the downlink is in the 10 meter band
B. The satellite uplink is in the 70 cm band and the downlink is in the 2 meter band
  C. The satellite operates using ultraviolet frequencies
  D. The satellite frequencies are usually variable

## Slide 50: T8B09 What causes "spin fading" when referring to satellite signals?
  A. Circular polarized noise interference radiated from the sun
  B. Rotation of the satellite and its antennas
  C. Doppler shift of the received signal
  D. Interfering signals within the satellite uplink band

## Slide 51: T8B09 What causes "spin fading" when referring to satellite signals?
  A. Circular polarized noise interference radiated from the sun
B. Rotation of the satellite and its antennas
  C. Doppler shift of the received signal
  D. Interfering signals within the satellite uplink band

## Slide 52: T8B10 What do the initials LEO tell you about an amateur satellite?
  A. The satellite battery is in Low Energy Operation mode
  B. The satellite is performing a Lunar Ejection Orbit maneuver
  C. The satellite is in a Low Earth Orbit
  D. The satellite uses Light Emitting Optics

## Slide 53: T8B10 What do the initials LEO tell you about an amateur satellite?
  A. The satellite battery is in Low Energy Operation mode
  B. The satellite is performing a Lunar Ejection Orbit maneuver
C. The satellite is in a Low Earth Orbit
  D. The satellite uses Light Emitting Optics

## Slide 54: T8B11 What is a commonly used method of sending signals to and from a digital satellite?
  A. USB AFSK
  B. PSK31
  C. FM Packet
  D. WSJT

## Slide 55: T8B11 What is a commonly used method of sending signals to and from a digital satellite?
  A. USB AFSK
  B. PSK31
C. FM Packet
  D. WSJT

## Slide 56: T8C01 Which of the following methods is used to locate sources of noise interference or jamming?
  A. Echolocation
  B. Doppler radar
  C. Radio direction finding
  D. Phase locking

## Slide 57: T8C01 Which of the following methods is used to locate sources of noise interference or jamming?
  A. Echolocation
  B. Doppler radar
C. Radio direction finding
  D. Phase locking

## Slide 58: T8C02 Which of these items would be useful for a hidden transmitter hunt?
  A. Calibrated SWR meter
  B. A directional antenna
  C. A calibrated noise bridge
  D. All of these choices are correct

## Slide 59: T8C02 Which of these items would be useful for a hidden transmitter hunt?
  A. Calibrated SWR meter
B. A directional antenna
  C. A calibrated noise bridge
  D. All of these choices are correct

## Slide 60: T8C03 What popular operating activity involves contacting as many stations as possible during a specified period of time?
  A. Contesting
  B. Net operations
  C. Public service events
  D. Simulated emergency exercises

## Slide 61: T8C03 What popular operating activity involves contacting as many stations as possible during a specified period of time?
A. Contesting
  B. Net operations
  C. Public service events
  D. Simulated emergency exercises

## Slide 62: T8C04 Which of the following is good procedure when contacting another station in a radio contest?
  A. Be sure to sign only the last two letters of your call if there is a pileup calling the station
  B. Work the station twice to be sure that you are in his log
  C. Send only the minimum information needed for proper identification and the contest exchange
  D. All of these choices are correct

## Slide 63: T8C04 Which of the following is good procedure when contacting another station in a radio contest?
  A. Be sure to sign only the last two letters of your call if there is a pileup calling the station
  B. Work the station twice to be sure that you are in his log
C. Send only the minimum information needed for proper identification and the contest exchange
  D. All of these choices are correct

## Slide 64: Maindenhead Grids
Special Operation
<number>
Two letters and two numbers define an area 1° latitude x 2° longitude anywhere in the world. Seattle is CN87, Portland CN85.
Notes: <number>
This grid map is courtesy Icom America and is downloadable from their web site at http://www.icomamerica.com.
Two letter designator followed by a number ranging from 1 to 100 representing 1° latitude x 2° longitude square area of the earth.
  The earth is divided into 20° Latitude x 10° Longitude squares starting on the date line at the south pole and going North and East.
  Each square is given a two letter designator labeled East and North starting with AA and Ending with RR
  An – In are West of GMT, Jn – Rn are east of GMT
  nA – n I are South of the equator, nJ – nR are North of the equator
  Each square is further divided into 100 1°x2° squares and given a number starting in the lower left corner of the square and are labeled up and right
  Seattle is in CN-87, Los Angles DM-04
  Spokane is in DN-17

## Slide 65: T8C05 What is a grid locator?
  A. A letter-number designator assigned to a geographic location
  B. A letter-number designator assigned to an azimuth and elevation
  C. An instrument for neutralizing a final amplifier
  D. An instrument for radio direction finding

## Slide 66: T8C05 What is a grid locator?
A. A letter-number designator assigned to a geographic location
  B. A letter-number designator assigned to an azimuth and elevation
  C. An instrument for neutralizing a final amplifier
  D. An instrument for radio direction finding

## Slide 67: T8C06 For what purpose is a temporary "1 by 1" format (letter-number-letter) call sign assigned?
  A. To designate an experimental station
  B. To honor a deceased relative who was a radio amateur
  C. For operations in conjunction with an activity of special significance to the amateur community
  D. All of these choices are correct

## Slide 68: T8C06 For what purpose is a temporary "1 by 1" format (letter-number-letter) call sign assigned?
  A. To designate an experimental station
  B. To honor a deceased relative who was a radio amateur
C. For operations in conjunction with an activity of special significance to the amateur community
  D. All of these choices are correct

## Slide 69: T8C07 What is the maximum power allowed when transmitting telecommand signals to radio controlled models?
  A. 500 milliwatts
  B. 1 watt
  C. 25 watts
  D. 1500 watts

## Slide 70: T8C07 What is the maximum power allowed when transmitting telecommand signals to radio controlled models?
  A. 500 milliwatts
B. 1 watt
  C. 25 watts
  D. 1500 watts

## Slide 71: T8C08 What is required in place of on-air station identification when sending signals to a radio control model using amateur frequencies?
  A. Voice identification must be transmitted every 10 minutes
  B. Morse code ID must be sent once per hour
  C. A label indicating the licensee's name, call sign and address must be affixed to the transmitter
  D. A flag must be affixed to the transmitter antenna with the station call sign in 1 inch high letters or larger

## Slide 72: T8C08 What is required in place of on-air station identification when sending signals to a radio control model using amateur frequencies?
  A. Voice identification must be transmitted every 10 minutes
  B. Morse code ID must be sent once per hour
C. A label indicating the licensee's name, call sign and address must be affixed to the transmitter
  D. A flag must be affixed to the transmitter antenna with the station call sign in 1 inch high letters or larger

## Slide 73: EchoLink® and IRLP
Communications Modes and Methods
<number>
EchoLink® software allows licensed Amateur Radio stations to communicate with one another over the Internet, using voice-over-IP (VoIP) technology.

## Slide 74: T8C09 How might you obtain a list of active nodes that use VoIP?
  A. From the FCC Rulebook
  B. From your local emergency coordinator
  C. From a repeater directory
  D. From the local repeater frequency coordinator

## Slide 75: T8C09 How might you obtain a list of active nodes that use VoIP?
  A. From the FCC Rulebook
  B. From your local emergency coordinator
C. From a repeater directory
  D. From the local repeater frequency coordinator

## Slide 76: T8C10 How do you select a specific IRLP node when using a portable transceiver?
  A. Choose a specific CTCSS tone
  B. Choose the correct DSC tone
  C. Access the repeater autopatch
  D. Use the keypad to transmit the IRLP node ID

## Slide 77: T8C10 How do you select a specific IRLP node when using a portable transceiver?
  A. Choose a specific CTCSS tone
  B. Choose the correct DSC tone
  C. Access the repeater autopatch
D. Use the keypad to transmit the IRLP node ID

## Slide 78: T8C11 What name is given to an amateur radio station that is used to connect other amateur stations to the Internet?
  A. A gateway
  B. A repeater
  C. A digipeater
  D. A beacon

## Slide 79: T8C11 What name is given to an amateur radio station that is used to connect other amateur stations to the Internet?
A. A gateway
  B. A repeater
  C. A digipeater
  D. A beacon

## Slide 80: T8D01 Which of the following is an example of a digital communications method?
  A. Packet
  B. PSK31
  C. MFSK
  D. All of these choices are correct

## Slide 81: T8D01 Which of the following is an example of a digital communications method?
  A. Packet
  B. PSK31
  C. MFSK
D. All of these choices are correct

## Slide 82: APRS – Automatic Position Reporting System
Communications Modes and Methods
<number>
Real-time
location
mapping

## Slide 83: T8D02 What does the term APRS mean?
  A. Automatic Position Reporting System
  B. Associated Public Radio Station
  C. Auto Planning Radio Set-up
  D. Advanced Polar Radio System

## Slide 84: T8D02 What does the term APRS mean?
A. Automatic Position Reporting System
  B. Associated Public Radio Station
  C. Auto Planning Radio Set-up
  D. Advanced Polar Radio System

## Slide 85: T8D03 Which of the following is normally used when sending automatic location reports via amateur radio?
  A. A connection to the vehicle speedometer
  B. A WWV receiver
  C. A connection to a broadcast FM sub-carrier receiver
  D. A Global Positioning System receiver

## Slide 86: T8D03 Which of the following is normally used when sending automatic location reports via amateur radio?
  A. A connection to the vehicle speedometer
  B. A WWV receiver
  C. A connection to a broadcast FM sub-carrier receiver
D. A Global Positioning System receiver

## Slide 87: National Television Systems Committee (NTSC)
Communications Modes and Methods
<number>
Television Standards
  NTSC – Canada, US, Japan, South Korea
  PAL
  SECAM

## Slide 88: T8D04 What type of transmission is indicated by the term NTSC?
  A. A Normal Transmission mode in Static Circuit
  B. A special mode for earth satellite uplink
  C. An analog fast scan color TV signal
  D. A frame compression scheme for TV signals

## Slide 89: T8D04 What type of transmission is indicated by the term NTSC?
  A. A Normal Transmission mode in Static Circuit
  B. A special mode for earth satellite uplink
C. An analog fast scan color TV signal
  D. A frame compression scheme for TV signals

## Slide 90: T8D05 Which of the following emission modes may be used by a Technician Class operator between 219 and 220 MHz?
  A. Spread spectrum
  B. Data
  C. SSB voice
  D. Fast-scan television

## Slide 91: T8D05 Which of the following emission modes may be used by a Technician Class operator between 219 and 220 MHz?
  A. Spread spectrum
B. Data
  C. SSB voice
  D. Fast-scan television

## Slide 92: PSK31 Digital Mode
Communications Modes and Methods
<number>
Provides VERY EFFICIENT keyboard to keyboard chat capability. PSK31 is not error-corrected.

## Slide 93: T8D06 What does the abbreviation PSK mean?
  A. Pulse Shift Keying
  B. Phase Shift Keying
  C. Packet Short Keying
  D. Phased Slide Keying

## Slide 94: T8D06 What does the abbreviation PSK mean?
  A. Pulse Shift Keying
B. Phase Shift Keying
  C. Packet Short Keying
  D. Phased Slide Keying

## Slide 95: T8D07 What is PSK31?
  A. A high-rate data transmission mode
  B. A method of reducing noise interference to FM signals
  C. A method of compressing digital television signal
  D. A low-rate data transmission mode

## Slide 96: T8D07 What is PSK31?
  A. A high-rate data transmission mode
  B. A method of reducing noise interference to FM signals
  C. A method of compressing digital television signal
D. A low-rate data transmission mode

## Slide 97: T8D08 Which of the following may be included in packet transmissions?
  A. A check sum which permits error detection
  B. A header which contains the call sign of the station to which the information is being sent
  C. Automatic repeat request in case of error
  D. All of these choices are correct

## Slide 98: T8D08 Which of the following may be included in packet transmissions?
  A. A check sum which permits error detection
  B. A header which contains the call sign of the station to which the information is being sent
  C. Automatic repeat request in case of error
D. All of these choices are correct

## Slide 99: T8D09 What code is used when sending CW in the amateur bands?
  A. Baudot
  B. Hamming
  C. International Morse
  D. Gray

## Slide 100: T8D09 What code is used when sending CW in the amateur bands?
  A. Baudot
  B. Hamming
C. International Morse
  D. Gray

## Slide 101: T8D10 Which of the following can be used to transmit CW in the amateur bands?
  A. Straight Key
  B. Electronic Keyer
  C. Computer Keyboard
  D. All of these choices are correct

## Slide 102: T8D10 Which of the following can be used to transmit CW in the amateur bands?
  A. Straight Key
  B. Electronic Keyer
  C. Computer Keyboard
D. All of these choices are correct

## Slide 103: T8D11 What is a "parity" bit?
  A. A control code required for automatic position reporting
  B. A timing bit used to ensure equal sharing of a frequency
  C. An extra code element used to detect errors in received data
  D. A "triple width" bit used to signal the end of a character

## Slide 104: T8D11 What is a "parity" bit?
  A. A control code required for automatic position reporting
  B. A timing bit used to ensure equal sharing of a frequency
C. An extra code element used to detect errors in received data
  D. A "triple width" bit used to signal the end of a character

## Slide 105: SUBELEMENT T8 [4 exam questions – 4 groups]
<number>
Microhams 2010 Technician
Notes: <number>
http://www.microhams.com
Created by Scott N7SS