## Slide 1: SUBELEMENT T3 [3 Exam Questions - 3 Groups]
Radio wave characteristics, radio and electromagnetic properties, propagation modes
Notes: <number>
2010 Technician Class (Element 2) Master syllabus
Released 1 February, 2010
396 questions in 35 sections
These slides are free to use and are available from http://www.microhams.com. Changes are allowed if Microhams branding is left in place (feel free to ad your own). Any content additions should be forwarded to the author, Scott N7SS at N7SS@arrl.net so they can be rolled into future versions and available for everyone.

## Slide 2: T3 – Radio Waves
<number>
Microhams 2010 Technician
T3A - Radio wave characteristics; how a radio signal travels; distinctions of HF, VHF and UHF; fading, multipath; wavelength vs. penetration; antenna orientation
T3B - Radio and electromagnetic wave properties; the electromagnetic spectrum, wavelength vs. frequency, velocity of electromagnetic waves
T3C - Propagation modes; line of sight, sporadic E, meteor, aurora scatter, tropospheric ducting, F layer skip, radio horizon

## Slide 3: T3A01 What should you do if another operator reports that your station's 2 meter signals were strong just a moment ago, but now they are weak or distorted?
<number>
Microhams 2010 Technician
  A. Change the batteries in your radio to a different type
  B. Turn on the CTCSS tone
  C. Ask the other operator to adjust his squelch control
  D. Try moving a few feet, as random reflections may be causing multi-path distortion

## Slide 4: T3A01 What should you do if another operator reports that your station's 2 meter signals were strong just a moment ago, but now they are weak or distorted?
<number>
Microhams 2010 Technician
  A. Change the batteries in your radio to a different type
  B. Turn on the CTCSS tone
  C. Ask the other operator to adjust his squelch control
D. Try moving a few feet, as random reflections may be causing multi-path distortion

## Slide 5: T3A02 Why are UHF signals often more effective from inside buildings than VHF signals?
<number>
Microhams 2010 Technician
  A. VHF signals lose power faster over distance
  B. The shorter wavelength allows them to more easily penetrate the structure of buildings
  C. This is incorrect; VHF works better than UHF inside buildings
  D. UHF antennas are more efficient than VHF antennas

## Slide 6: T3A02 Why are UHF signals often more effective from inside buildings than VHF signals?
<number>
Microhams 2010 Technician
  A. VHF signals lose power faster over distance
B. The shorter wavelength allows them to more easily penetrate the structure of buildings
  C. This is incorrect; VHF works better than UHF inside buildings
  D. UHF antennas are more efficient than VHF antennas

## Slide 7: T3A03 What antenna polarization is normally used for long-distance weak-signal CW and SSB contacts using the VHF and UHF bands?
<number>
Microhams 2010 Technician
  A. Right-hand circular
  B. Left-hand circular
  C. Horizontal
  D. Vertical

## Slide 8: T3A03 What antenna polarization is normally used for long-distance weak-signal CW and SSB contacts using the VHF and UHF bands?
<number>
Microhams 2010 Technician
  A. Right-hand circular
  B. Left-hand circular
C. Horizontal
  D. Vertical

## Slide 9: T3A04 What can happen if the antennas at opposite ends of a VHF or UHF line of sight radio link are not using the same polarization?
<number>
Microhams 2010 Technician
  A. The modulation sidebands might become inverted
  B. Signals could be significantly weaker
  C. Signals have an echo effect on voices
  D. Nothing significant will happen

## Slide 10: T3A04 What can happen if the antennas at opposite ends of a VHF or UHF line of sight radio link are not using the same polarization?
<number>
Microhams 2010 Technician
  A. The modulation sidebands might become inverted
B. Signals could be significantly weaker
  C. Signals have an echo effect on voices
  D. Nothing significant will happen

## Slide 11: T3A05 When using a directional antenna, how might your station be able to access a distant repeater if buildings or obstructions are blocking the direct line of sight path?
<number>
Microhams 2010 Technician
  A. Change from vertical to horizontal polarization
  B. Try to find a path that reflects signals to the repeater
  C. Try the long path
  D. Increase the antenna SWR

## Slide 12: T3A05 When using a directional antenna, how might your station be able to access a distant repeater if buildings or obstructions are blocking the direct line of sight path?
<number>
Microhams 2010 Technician
  A. Change from vertical to horizontal polarization
B. Try to find a path that reflects signals to the repeater
  C. Try the long path
  D. Increase the antenna SWR

## Slide 13: T3A06 What term is commonly used to describe the rapid fluttering sound sometimes heard from mobile stations that are moving while transmitting?
<number>
Microhams 2010 Technician
  A. Flip-flopping
  B. Picket fencing
  C. Frequency shifting
  D. Pulsing

## Slide 14: T3A06 What term is commonly used to describe the rapid fluttering sound sometimes heard from mobile stations that are moving while transmitting?
<number>
Microhams 2010 Technician
  A. Flip-flopping
B. Picket fencing
  C. Frequency shifting
  D. Pulsing

## Slide 15: T3A07 What type of wave carries radio signals between transmitting and receiving stations?
<number>
Microhams 2010 Technician
  A. Electromagnetic
  B. Electrostatic
  C. Surface acoustic
  D. Magnetostrictive

## Slide 16: T3A07 What type of wave carries radio signals between transmitting and receiving stations?
<number>
Microhams 2010 Technician
A. Electromagnetic
  B. Electrostatic
  C. Surface acoustic
  D. Magnetostrictive

## Slide 17: T3A08 What is the cause of irregular fading of signals from distant stations during times of generally good reception?
<number>
Microhams 2010 Technician
  A. Absorption of signals by the "D" layer of the ionosphere
  B. Absorption of signals by the "E" layer of the ionosphere
  C. Random combining of signals arriving via different path lengths
  D. Intermodulation distortion in the local receiver

## Slide 18: T3A08 What is the cause of irregular fading of signals from distant stations during times of generally good reception?
<number>
Microhams 2010 Technician
  A. Absorption of signals by the "D" layer of the ionosphere
  B. Absorption of signals by the "E" layer of the ionosphere
C. Random combining of signals arriving via different path lengths
  D. Intermodulation distortion in the local receiver

## Slide 19: T3A09 Which of the following is a common effect of "skip" reflections between the Earth and the ionosphere?
<number>
Microhams 2010 Technician
  A. The sidebands become reversed at each reflection
  B. The polarization of the original signal is randomized
  C. The apparent frequency of the received signal is shifted by a random amount
  D. Signals at frequencies above 30 MHz become stronger with each reflection

## Slide 20: T3A09 Which of the following is a common effect of "skip" reflections between the Earth and the ionosphere?
<number>
Microhams 2010 Technician
  A. The sidebands become reversed at each reflection
B. The polarization of the original signal is randomized
  C. The apparent frequency of the received signal is shifted by a random amount
  D. Signals at frequencies above 30 MHz become stronger with each reflection

## Slide 21: T3A10 What may occur if VHF or UHF data signals propagate over multiple paths?
<number>
Microhams 2010 Technician
  A. Transmission rates can be increased by a factor equal to the number of separate paths observed
  B. Transmission rates must be decreased by a factor equal to the number of separate paths observed
  C. No significant changes will occur if the signals are transmitting using FM
  D. Error rates are likely to increase

## Slide 22: T3A10 What may occur if VHF or UHF data signals propagate over multiple paths?
<number>
Microhams 2010 Technician
  A. Transmission rates can be increased by a factor equal to the number of separate paths observed
  B. Transmission rates must be decreased by a factor equal to the number of separate paths observed
  C. No significant changes will occur if the signals are transmitting using FM
D. Error rates are likely to increase

## Slide 23: T3A11 Which part of the atmosphere enables the propagation of radio signals around the world?
<number>
Microhams 2010 Technician
  A. The stratosphere
  B. The troposphere
  C. The ionosphere
  D. The magnetosphere

## Slide 24: Ionospheric Layers
Radio Wave Propagation
<number>
Notes: <number>
The key points are the D, E and F layers. The F layer splits and becomes F1 and F2 with the additional energy from the daytime sun. The D and E layers disappear at night without the sun’s energy. The D layer absorbs most RF power, particularly at low frequencies. The other layers will reflect RF energy. The higher the layer, the further the contact possible.
Propagation conditions are a balance between the D layer absorption of lower frequencies and the reflection of the higher frequencies by the upper layers. As more of the sun’s energy (primarily electromagnetic and particle emissions) strikes the ionosphere, all the layers grown in size and density. The D layer will absorb more low frequency RF and the upper layers will reflect more high frequency RF. This creates a window of frequencies above the Lowest Usable Frequency (LUF) and Maximum Usable Frequency (MUF) that will work for long distance communications.
Sunspots provide huge amounts of energy to reflect radio waves in the ionosphere and are especially important in the upper bands. The sun rotates (solar day) every 28 days. This means if conditions are good on one day, they are likely to repeat 28 days later when the earth is in the same position.
Because the sun is so critical for communications, measurements are constantly being made of the “Solar Flux” (RF energy emitted by the sun). In the US, WWV broadcasts reports with the “Solar Flux Index” (a measure of solar activity that is taken at a specific frequency) every hour.

## Slide 25: T3A11 Which part of the atmosphere enables the propagation of radio signals around the world?
<number>
Microhams 2010 Technician
  A. The stratosphere
  B. The troposphere
C. The ionosphere
  D. The magnetosphere

## Slide 26: Wavelength vs Frequency
Radio and Electronic Fundamentals
<number>
The distance a radio wave travels in one cycle is called wavelength
The number of cycles per second is frequency
The maximum displacement of wave from reference value is amplitude
One Wavelength
Time
V+
V-
0V
One Cycle
Amplitude

## Slide 27: T3B01 What is the name for the distance a radio wave travels during one complete cycle?
<number>
Microhams 2010 Technician
  A. Wave speed
  B. Waveform
  C. Wavelength
  D. Wave spread

## Slide 28: T3B01 What is the name for the distance a radio wave travels during one complete cycle?
<number>
Microhams 2010 Technician
  A. Wave speed
  B. Waveform
C. Wavelength
  D. Wave spread

## Slide 29: T3B02 What term describes the number of times per second that an alternating current reverses direction?
<number>
Microhams 2010 Technician
  A. Pulse rate
  B. Speed
  C. Wavelength
  D. Frequency

## Slide 30: T3B02 What term describes the number of times per second that an alternating current reverses direction?
<number>
Microhams 2010 Technician
  A. Pulse rate
  B. Speed
  C. Wavelength
D. Frequency

## Slide 31: T3B03 What are the two components of a radio wave?
<number>
Microhams 2010 Technician
  A. AC and DC
  B. Voltage and current
  C. Electric and magnetic fields
  D. Ionizing and non-ionizing radiation

## Slide 32: T3B03 What are the two components of a radio wave?
<number>
Microhams 2010 Technician
  A. AC and DC
  B. Voltage and current
C. Electric and magnetic fields
  D. Ionizing and non-ionizing radiation

## Slide 33: T3B04 How fast does a radio wave travel through free space?
<number>
Microhams 2010 Technician
  A. At the speed of light
  B. At the speed of sound
  C. Its speed is inversely proportional to its wavelength
  D. Its speed increases as the frequency increases

## Slide 34: T3B04 How fast does a radio wave travel through free space?
<number>
Microhams 2010 Technician
A. At the speed of light
  B. At the speed of sound
  C. Its speed is inversely proportional to its wavelength
  D. Its speed increases as the frequency increases

## Slide 35: Frequency to Wavelength Conversion
Radio and Electronic Fundamentals
<number>
300
Freq (MHz)
Wavelength =
To convert from frequency to wavelength in meters:
Frequency and wavelength are inversely proportional – as one increases, the other decreases
Longer (wavelength) – Lower (frequency)

## Slide 36: T3B05 How does the wavelength of a radio wave relate to its frequency?
<number>
Microhams 2010 Technician
  A. The wavelength gets longer as the frequency increases
  B. The wavelength gets shorter as the frequency increases
  C. There is no relationship between wavelength and frequency
  D. The wavelength depends on the bandwidth of the signal

## Slide 37: T3B05 How does the wavelength of a radio wave relate to its frequency?
<number>
Microhams 2010 Technician
  A. The wavelength gets longer as the frequency increases
B. The wavelength gets shorter as the frequency increases
  C. There is no relationship between wavelength and frequency
  D. The wavelength depends on the bandwidth of the signal

## Slide 38: T3B06 What is the formula for converting frequency to wavelength in meters?
<number>
Microhams 2010 Technician
  A. Wavelength in meters equals frequency in hertz multiplied by 300
  B. Wavelength in meters equals frequency in hertz divided by 300
  C. Wavelength in meters equals frequency in megahertz divided by 300
  D. Wavelength in meters equals 300 divided by frequency in megahertz

## Slide 39: T3B06 What is the formula for converting frequency to wavelength in meters?
<number>
Microhams 2010 Technician
  A. Wavelength in meters equals frequency in hertz multiplied by 300
  B. Wavelength in meters equals frequency in hertz divided by 300
  C. Wavelength in meters equals frequency in megahertz divided by 300
D. Wavelength in meters equals 300 divided by frequency in megahertz

## Slide 40: T3B07 What property of radio waves is often used to identify the different frequency bands?
<number>
Microhams 2010 Technician
  A. The approximate wavelength
  B. The magnetic intensity of waves
  C. The time it takes for waves to travel one mile
  D. The voltage standing wave ratio of waves

## Slide 41: T3B07 What property of radio waves is often used to identify the different frequency bands?
<number>
Microhams 2010 Technician
A. The approximate wavelength
  B. The magnetic intensity of waves
  C. The time it takes for waves to travel one mile
  D. The voltage standing wave ratio of waves

## Slide 42: Radio Spectrum
Radio and Electronic Fundamentals
<number>
Medium Wave (MF) | Short Wave (HF) | Very High Frequency (VHF) | Ultra High Frequency (UHF)
AM Broadcast
540
1630
TV 2-6
54
88
FM Broadcast
108
TV 7-13
174
216
TV 14-69
470
806
300 kHz
3 MHz
30 MHz
300 MHz
3 GHz
Frequency
1 Km
100 m
10 m
1 m
10 cm
Wavelength
Major Amateur Bands in Amber

## Slide 43: T3B08 What are the frequency limits of the VHF spectrum?
<number>
Microhams 2010 Technician
  A. 30 to 300 kHz
  B. 30 to 300 MHz
  C. 300 to 3000 kHz
  D. 300 to 3000 MHz

## Slide 44: T3B08 What are the frequency limits of the VHF spectrum?
<number>
Microhams 2010 Technician
  A. 30 to 300 kHz
B. 30 to 300 MHz
  C. 300 to 3000 kHz
  D. 300 to 3000 MHz

## Slide 45: T3B09 What are the frequency limits of the UHF spectrum?
<number>
Microhams 2010 Technician
  A. 30 to 300 kHz
  B. 30 to 300 MHz
  C. 300 to 3000 kHz
  D. 300 to 3000 MHz

## Slide 46: T3B09 What are the frequency limits of the UHF spectrum?
<number>
Microhams 2010 Technician
  A. 30 to 300 kHz
  B. 30 to 300 MHz
  C. 300 to 3000 kHz
D. 300 to 3000 MHz

## Slide 47: T3B10 What frequency range is referred to as HF?
<number>
Microhams 2010 Technician
  A. 300 to 3000 MHz
  B. 30 to 300 MHz
  C. 3 to 30 MHz
  D. 300 to 3000 kHz

## Slide 48: T3B10 What frequency range is referred to as HF?
<number>
Microhams 2010 Technician
  A. 300 to 3000 MHz
  B. 30 to 300 MHz
C. 3 to 30 MHz
  D. 300 to 3000 kHz

## Slide 49: T3B11 What is the approximate velocity of a radio wave as it travels through free space?
<number>
Microhams 2010 Technician
  A. 3000 kilometers per second
  B. 300,000,000 meters per second
  C. 300,000 miles per hour
  D. 186,000 miles per hour

## Slide 50: T3B11 What is the approximate velocity of a radio wave as it travels through free space?
<number>
Microhams 2010 Technician
  A. 3000 kilometers per second
B. 300,000,000 meters per second
  C. 300,000 miles per hour
  D. 186,000 miles per hour

## Slide 51: T3C01 Why are "direct" (not via a repeater) UHF signals rarely heard from stations outside your local coverage area?
<number>
Microhams 2010 Technician
  A. They are too weak to go very far
  B. FCC regulations prohibit them from going more than 50 miles
  C. UHF signals are usually not reflected by the ionosphere
  D. They collide with trees and shrubbery and fade out

## Slide 52: T3C01 Why are "direct" (not via a repeater) UHF signals rarely heard from stations outside your local coverage area?
<number>
Microhams 2010 Technician
  A. They are too weak to go very far
  B. FCC regulations prohibit them from going more than 50 miles
C. UHF signals are usually not reflected by the ionosphere
  D. They collide with trees and shrubbery and fade out

## Slide 53: T3C02 Which of the following might be happening when VHF signals are being received from long distances?
<number>
Microhams 2010 Technician
  A. Signals are being reflected from outer space
  B. Signals are arriving by sub-surface ducting
  C. Signals are being reflected by lightning storms in your area
  D. Signals are being refracted from a sporadic E layer

## Slide 54: T3C02 Which of the following might be happening when VHF signals are being received from long distances?
<number>
Microhams 2010 Technician
  A. Signals are being reflected from outer space
  B. Signals are arriving by sub-surface ducting
  C. Signals are being reflected by lightning storms in your area
D. Signals are being refracted from a sporadic E layer

## Slide 55: T3C03 What is a characteristic of VHF signals received via auroral reflection?
<number>
Microhams 2010 Technician
  A. Signals from distances of 10,000 or more miles are common
  B. The signals exhibit rapid fluctuations of strength and often sound distorted
  C. These types of signals occur only during winter nighttime hours
  D. These types of signals are generally strongest when your antenna is aimed to the south (for stations in the Northern Hemisphere)

## Slide 56: T3C03 What is a characteristic of VHF signals received via auroral reflection?
<number>
Microhams 2010 Technician
  A. Signals from distances of 10,000 or more miles are common
B. The signals exhibit rapid fluctuations of strength and often sound distorted
  C. These types of signals occur only during winter nighttime hours
  D. These types of signals are generally strongest when your antenna is aimed to the south (for stations in the Northern Hemisphere)

## Slide 57: T3C04 Which of the following propagation types is most commonly associated with occasional strong over-the-horizon signals on the 10, 6, and 2 meter bands?
<number>
Microhams 2010 Technician
  A. Backscatter
  B. Sporadic E
  C. D layer absorption
  D. Gray-line propagation

## Slide 58: T3C04 Which of the following propagation types is most commonly associated with occasional strong over-the-horizon signals on the 10, 6, and 2 meter bands?
<number>
Microhams 2010 Technician
  A. Backscatter
B. Sporadic E
  C. D layer absorption
  D. Gray-line propagation

## Slide 59: T3C05 What is meant by the term "knife-edge" propagation?
<number>
Microhams 2010 Technician
  A. Signals are reflected back toward the originating station at acute angles
  B. Signals are sliced into several discrete beams and arrive via different paths
  C. Signals are partially refracted around solid objects exhibiting sharp edges
  D. Signals propagated close to the band edge exhibiting a sharp cutoff

## Slide 60: T3C05 What is meant by the term "knife-edge" propagation?
<number>
Microhams 2010 Technician
  A. Signals are reflected back toward the originating station at acute angles
  B. Signals are sliced into several discrete beams and arrive via different paths
C. Signals are partially refracted around solid objects exhibiting sharp edges
  D. Signals propagated close to the band edge exhibiting a sharp cutoff

## Slide 61: T3C06 What mode is responsible for allowing over-the-horizon VHF and UHF communications to ranges of approximately 300 miles on a regular basis?
<number>
Microhams 2010 Technician
  A. Tropospheric scatter
  B. D layer refraction
  C. F2 layer refraction
  D. Faraday rotation

## Slide 62: T3C06 What mode is responsible for allowing over-the-horizon VHF and UHF communications to ranges of approximately 300 miles on a regular basis?
<number>
Microhams 2010 Technician
A. Tropospheric scatter
  B. D layer refraction
  C. F2 layer refraction
  D. Faraday rotation

## Slide 63: T3C07 What band is best suited to communicating via meteor scatter?
<number>
Microhams 2010 Technician
  A. 10 meters
  B. 6 meters
  C. 2 meters
  D. 70 cm

## Slide 64: T3C07 What band is best suited to communicating via meteor scatter?
<number>
Microhams 2010 Technician
  A. 10 meters
B. 6 meters
  C. 2 meters
  D. 70 cm

## Slide 65: T3C08 What causes "tropospheric ducting"?
<number>
Microhams 2010 Technician
  A. Discharges of lightning during electrical storms
  B. Sunspots and solar flares
  C. Updrafts from hurricanes and tornadoes
  D. Temperature inversions in the atmosphere

## Slide 66: T3C08 What causes "tropospheric ducting"?
<number>
Microhams 2010 Technician
  A. Discharges of lightning during electrical storms
  B. Sunspots and solar flares
  C. Updrafts from hurricanes and tornadoes
D. Temperature inversions in the atmosphere

## Slide 67: T3C09 What is generally the best time for long-distance 10 meter band propagation?
<number>
Microhams 2010 Technician
  A. During daylight hours
  B. During nighttime hours
  C. When there are coronal mass ejections
  D. Whenever the solar flux is low

## Slide 68: T3C09 What is generally the best time for long-distance 10 meter band propagation?
<number>
Microhams 2010 Technician
A. During daylight hours
  B. During nighttime hours
  C. When there are coronal mass ejections
  D. Whenever the solar flux is low

## Slide 69: T3C10 What is the radio horizon?
<number>
Microhams 2010 Technician
  A. The distance at which radio signals between two points are effectively blocked by the curvature of the Earth
  B. The distance from the ground to a horizontally mounted antenna
  C. The farthest point you can see when standing at the base of your antenna tower
  D. The shortest distance between two points on the Earth's surface

## Slide 70: T3C10 What is the radio horizon?
<number>
Microhams 2010 Technician
A. The distance at which radio signals between two points are effectively blocked by the curvature of the Earth
  B. The distance from the ground to a horizontally mounted antenna
  C. The farthest point you can see when standing at the base of your antenna tower
  D. The shortest distance between two points on the Earth's surface

## Slide 71: T3C11 Why do VHF and UHF radio signals usually travel somewhat farther than the visual line of sight distance between two stations?
<number>
Microhams 2010 Technician
  A. Radio signals move somewhat faster than the speed of light
  B. Radio waves are not blocked by dust particles
  C. The Earth seems less curved to radio waves than to light
  D. Radio waves are blocked by dust particles

## Slide 72: T3C11 Why do VHF and UHF radio signals usually travel somewhat farther than the visual line of sight distance between two stations?
<number>
Microhams 2010 Technician
  A. Radio signals move somewhat faster than the speed of light
  B. Radio waves are not blocked by dust particles
C. The Earth seems less curved to radio waves than to light
  D. Radio waves are blocked by dust particles

## Slide 73: SUBELEMENT T3 [3 exam questions – 3 groups]
<number>
Microhams 2010 Technician
Notes: <number>
http://www.microhams.com
Created by Scott N7SS