## Slide 1: SUBELEMENT T1 [6 Exam Questions - 6 Groups]
FCC Rules, descriptions and definitions for the amateur radio service, operator and station license responsibilities
Notes: <number>
2010 Technician Class (Element 2) Master syllabus
Released 1 February, 2010
396 questions in 35 sections
These slides are free to use and are available from http://www.microhams.com. Changes are allowed if Microhams branding is left in place (feel free to ad your own). Any content additions should be forwarded to the author, Scott N7SS at N7SS@arrl.net so they can be rolled into future versions and available for everyone.

## Slide 2: T1 – FCC Rules
<number>
Microhams 2010 Technician
T1A - Amateur Radio services; purpose of the amateur service, amateur-satellite service, operator/primary station license grant, where FCC rules are codified, basis and purpose of FCC rules, meanings of basic terms used in FCC rules
T1B - Authorized frequencies; frequency allocations, ITU regions, emission type, restricted sub-bands, spectrum sharing, transmissions near band edges
T1C - Operator classes and station call signs; operator classes, sequential, special event, and vanity call sign systems, international communications, reciprocal operation, station license licensee, places where the amateur service is regulated by the FCC, name and address on ULS, license term, renewal, grace period
T1D - Authorized and prohibited transmissions
T1E - Control operator and control types; control operator required, eligibility, designation of control operator, privileges and duties, control point, local, automatic and remote control, location of control operator
T1F - Station identification and operation standards; special operations for repeaters and auxiliary stations, third party communications, club stations, station security, FCC inspection

## Slide 3: Certificate of Successful Completion (CSCE) Valid for 365 Days
FCC Rules
<number>
Notes: <number>
The three current license classes that can be earned are visible in the middle. If you pass element 1, this is upgrade credit for 365 days but offers operating privileges forever. The three VE signature lines are visible on the bottom as is the issuing VEC organization (W5YI) across the top.

## Slide 4: FCC Part 97
FCC Rules
<number>
  Title 47 governs all Telecommunicatons in the US
    There are 301 parts (Part 0-300)
  Part 97 applies to Amateur Radio
  Copies available at: http://www.arrl.org/FandES/field/regulations/rules-reg.html http://www.fcc.gov

## Slide 5: FCC Universal License System
FCC Rules
<number>
  Online License Service http://wireless.fcc.gov/uls/
  Tracks all FCC License Applications and Licensees
  When your license shows up here, you’re legal

## Slide 6: Definitions
FCC Rules
<number>
Regulatory Body – FCC rules are defined in Part 97
Amateur Service – A radio communication service, carried out by authorized individuals without pecuniary interest
Amateur Operator – A person granted a license for amateur service
Amateur Station – A station licensed for Amateur Service
Amateur Space Station – An amateur station over 50KM high
Unidentified Communications – Communications from an unidentified source
Interference – Unwanted signals that disrupt other communications
Notes: <number>
Amateur License is two license: operator license and a station license

## Slide 7: Five Fundamental Purposes of Ham Radio
FCC Rules
<number>
  1. Recognition and enhancement of the value of the amateur service to the public as a voluntary noncommercial communication service, particularly with respect to providing emergency communications.
  2. Continuation and extension of the amateur’s proven ability to contribute to the advancement of the radio art.
  3. Encouragement and improvement of the amateur service through rules which provide for advancing skills in both the communications and technical phases of the art.
  4. Expansion of the existing reservoir within the amateur radio service of trained operators, technicians, and electronics experts.
  5. Continuation and extension of the amateur’s unique ability to enhance international goodwill.

## Slide 8: T1A01 For whom is the Amateur Radio Service intended?
<number>
Microhams 2010 Technician
  A. Persons who have messages to broadcast to the public
  B. Persons who need communications for the activities of their immediate family members, relatives and friends
  C. Persons who need two-way communications for personal reasons
  D. Persons who are interested in radio technique solely with a personal aim and without pecuniary interest

## Slide 9: T1A01 For whom is the Amateur Radio Service intended?
<number>
Microhams 2010 Technician
  A. Persons who have messages to broadcast to the public
  B. Persons who need communications for the activities of their immediate family members, relatives and friends
  C. Persons who need two-way communications for personal reasons
D. Persons who are interested in radio technique solely with a personal aim and without pecuniary interest

## Slide 10: T1A02 What agency regulates and enforces the rules for the Amateur Radio Service in the United States?
<number>
Microhams 2010 Technician
  A. FEMA
  B. The ITU
  C. The FCC
  D. Homeland Security

## Slide 11: T1A02 What agency regulates and enforces the rules for the Amateur Radio Service in the United States?
<number>
Microhams 2010 Technician
  A. FEMA
  B. The ITU
C. The FCC
  D. Homeland Security

## Slide 12: T1A03 Which part of the FCC rules contains the rules and regulations governing the Amateur Radio Service?
<number>
Microhams 2010 Technician
  A. Part 73
  B. Part 95
  C. Part 90
  D. Part 97

## Slide 13: T1A03 Which part of the FCC rules contains the rules and regulations governing the Amateur Radio Service?
<number>
Microhams 2010 Technician
  A. Part 73
  B. Part 95
  C. Part 90
D. Part 97

## Slide 14: T1A04 Which of the following meets the FCC definition of harmful interference?
<number>
Microhams 2010 Technician
  A. Radio transmissions that annoy users of a repeater
  B. Unwanted radio transmissions that cause costly harm to radio station apparatus
  C. That which seriously degrades, obstructs, or repeatedly interrupts a radio communication service operating in accordance with the Radio Regulations
  D. Static from lightning storms

## Slide 15: T1A04 Which of the following meets the FCC definition of harmful interference?
<number>
Microhams 2010 Technician
  A. Radio transmissions that annoy users of a repeater
  B. Unwanted radio transmissions that cause costly harm to radio station apparatus
C. That which seriously degrades, obstructs, or repeatedly interrupts a radio communication service operating in accordance with the Radio Regulations
  D. Static from lightning storms

## Slide 16: T1A05 What is the FCC Part 97 definition of a space station?
<number>
Microhams 2010 Technician
  A. Any multi-stage satellite
  B. An Earth satellite that carries one of more amateur operators
  C. An amateur station located less than 25 km above the Earth's surface
  D. An amateur station located more than 50 km above the Earth's surface

## Slide 17: T1A05 What is the FCC Part 97 definition of a space station?
<number>
Microhams 2010 Technician
  A. Any multi-stage satellite
  B. An Earth satellite that carries one of more amateur operators
  C. An amateur station located less than 25 km above the Earth's surface
D. An amateur station located more than 50 km above the Earth's surface

## Slide 18: T1A06 What is the FCC Part 97 definition of telecommand?
<number>
Microhams 2010 Technician
  A. An instruction bulletin issued by the FCC
  B. A one-way radio transmission of measurements at a distance from the measuring instrument
  C. A one-way transmission to initiate, modify or terminate functions of a device at a distance
  D. An instruction from a VEC

## Slide 19: T1A06 What is the FCC Part 97 definition of telecommand?
<number>
Microhams 2010 Technician
  A. An instruction bulletin issued by the FCC
  B. A one-way radio transmission of measurements at a distance from the measuring instrument
C. A one-way transmission to initiate, modify or terminate functions of a device at a distance
  D. An instruction from a VEC

## Slide 20: T1A07 What is the FCC Part 97 definition of telemetry?
<number>
Microhams 2010 Technician
  A. An information bulletin issued by the FCC
  B. A one-way transmission to initiate, modify or terminate functions of a device at a distance
  C. A one-way transmission of measurements at a distance from the measuring instrument
  D. An information bulletin from a VEC

## Slide 21: T1A07 What is the FCC Part 97 definition of telemetry?
<number>
Microhams 2010 Technician
  A. An information bulletin issued by the FCC
  B. A one-way transmission to initiate, modify or terminate functions of a device at a distance
C. A one-way transmission of measurements at a distance from the measuring instrument
  D. An information bulletin from a VEC

## Slide 22: T1A08 Which of the following entities recommends transmit/receive channels and other parameters for auxiliary and repeater stations?
<number>
Microhams 2010 Technician
  A. Frequency Spectrum Manager
  B. Frequency Coordinator
  C. FCC Regional Field Office
  D. International Telecommunications Union

## Slide 23: T1A08 Which of the following entities recommends transmit/receive channels and other parameters for auxiliary and repeater stations?
<number>
Microhams 2010 Technician
  A. Frequency Spectrum Manager
B. Frequency Coordinator
  C. FCC Regional Field Office
  D. International Telecommunications Union

## Slide 24: T1A09 Who selects a Frequency Coordinator?
<number>
Microhams 2010 Technician
  A. The FCC Office of Spectrum Management and Coordination Policy
  B. The local chapter of the Office of National Council of Independent Frequency Coordinators
  C. Amateur operators in a local or regional area whose stations are eligible to be auxiliary or repeater stations
  D. FCC Regional Field Office

## Slide 25: T1A09 Who selects a Frequency Coordinator?
<number>
Microhams 2010 Technician
  A. The FCC Office of Spectrum Management and Coordination Policy
  B. The local chapter of the Office of National Council of Independent Frequency Coordinators
C. Amateur operators in a local or regional area whose stations are eligible to be auxiliary or repeater stations
  D. FCC Regional Field Office

## Slide 26: T1A10 What is the FCC Part 97 definition of an amateur station?
<number>
Microhams 2010 Technician
  A. A station in an Amateur Radio Service consisting of the apparatus necessary for carrying on radio communications
  B. A building where Amateur Radio receivers, transmitters, and RF power amplifiers are installed
  C. Any radio station operated by a non-professional
  D. Any radio station for hobby use

## Slide 27: T1A10 What is the FCC Part 97 definition of an amateur station?
<number>
Microhams 2010 Technician
A. A station in an Amateur Radio Service consisting of the apparatus necessary for carrying on radio communications
  B. A building where Amateur Radio receivers, transmitters, and RF power amplifiers are installed
  C. Any radio station operated by a non-professional
  D. Any radio station for hobby use

## Slide 28: T1A11 Which of the following stations transmits signals over the air from a remote receive site to a repeater for retransmission?
<number>
Microhams 2010 Technician
  A. Beacon station
  B. Relay station
  C. Auxiliary station
  D. Message forwarding station

## Slide 29: T1A11 Which of the following stations transmits signals over the air from a remote receive site to a repeater for retransmission?
<number>
Microhams 2010 Technician
  A. Beacon station
  B. Relay station
C. Auxiliary station
  D. Message forwarding station

## Slide 30: T1B01 What is the ITU?
<number>
Microhams 2010 Technician
  A. An agency of the United States Department of Telecommunications Management
  B. A United Nations agency for information and communication technology issues
  C. An independent frequency coordination agency
  D. A department of the FCC

## Slide 31: T1B01 What is the ITU?
<number>
Microhams 2010 Technician
  A. An agency of the United States Department of Telecommunications Management
B. A United Nations agency for information and communication technology issues
  C. An independent frequency coordination agency
  D. A department of the FCC

## Slide 32: International Telegraph Union (ITU) Regions
FCC Rules
<number>
Notes: <number>
The airwaves are a shared resource that must be coordinated worldwide. The ITU is the body that does this. It’s important to recognize that the Americas are in Region 2. Europe including Russia and Africa are Region 1 and the rest of Asia is Region 3.

## Slide 33: T1B02 North American amateur stations are located in which ITU region?
<number>
Microhams 2010 Technician
  A. Region 1
  B. Region 2
  C. Region 3
  D. Region 4

## Slide 34: T1B02 North American amateur stations are located in which ITU region?
<number>
Microhams 2010 Technician
  A. Region 1
B. Region 2
  C. Region 3
  D. Region 4

## Slide 35: Wavelength vs Frequency
FCC Rules
<number>
The distance a radio wave travels in one cycle is called wavelength
The number of cycles per second is frequency
The maximum displacement of wave from reference value is amplitude
One Wavelength
Time
V+
V-
0V
One Cycle
Amplitude

## Slide 36: Frequency to Wavelength Conversion
FCC Rules
<number>
300
Freq (MHz)
Wavelength =
To convert from frequency to wavelength in meters:
Frequency and wavelength are inversely proportional – as one increases, the other decreases
Longer (wavelength) – Lower (frequency)

## Slide 37
FCC Rules
<number>
23cm
33cm
70cm
1.25m
2m
6m
2300 2310 2390 2450
1240 1300
902 928
420 430 435 438 450
Not Available North of Line A |  | Satellite | 
219 220 222 225
144 144.1 148
CW | 
50 50.1 54
 No Code Technicians Have All Privileges On The Above Bands 
13cm
Point to Point Digital Links |  | 
CW | 
70cm - 5 MHz repeater frequency separation (Split)
2m - 600 kHz repeater frequency separation (Split)
Notes: <number>
The FCC has mandated the areas colored (other than blue) to specific purposes. The remaining areas are divided by the amateur community into a band plan to insure most effective use of the spectrum and minimize interference. This band plan is not law but voluntary. If the FCC does get involved in a dispute, they will use the local band plan as a means to resolve the dispute.

## Slide 38: FCC Line A
FCC Rules
<number>
Notes: <number>
This information is not on the test. It is only provided because it’s relevant to Seattle amateurs

## Slide 39
FCC Rules
<number>
10m
15m
40m
80m
28 28.100 28.300 28.500 29.0 29.7
 | CW & Data | CW & SSB | 
21 21.100 21.200 21.450
 | CW Only | 
7 7.100 7.150 7.300
 | CW Only | 
3.5 3.675 3.725 4.0
 | CW Only | 
Legend | Technician + HF CW | 
 | Technician + HF Voice (SSB) | 
Notes
This information does not appear in the Technician exam
Technician Licensees may use up to 1500 watts PEP
Technician + HF Licensees may use up to 1500 watts PEP and 200 watts PEP on the HF bands
Technician with Morse Code Privileges
Notes: <number>
This information is not on the Technician exam

## Slide 40: T1B03 Which frequency is within the 6 meter band?
<number>
Microhams 2010 Technician
  A. 49.00 MHz
  B. 52.525 MHz
  C. 28.50 MHz
  D. 222.15 MHz

## Slide 41: T1B03 Which frequency is within the 6 meter band?
<number>
Microhams 2010 Technician
  A. 49.00 MHz
B. 52.525 MHz
  C. 28.50 MHz
  D. 222.15 MHz

## Slide 42: T1B04 Which amateur band are you using when your station is transmitting on 146.52 MHz?
<number>
Microhams 2010 Technician
  A. 2 meter band
  B. 20 meter band
  C. 14 meter band
  D. 6 meter band

## Slide 43: T1B04 Which amateur band are you using when your station is transmitting on 146.52 MHz?
<number>
Microhams 2010 Technician
A. 2 meter band
  B. 20 meter band
  C. 14 meter band
  D. 6 meter band

## Slide 44: T1B05 Which 70 cm frequency is authorized to a Technician Class license holder operating in ITU Region 2?
<number>
Microhams 2010 Technician
  A. 53.350 MHz
  B. 146.520 MHz
  C. 443.350 MHz
  D. 222.520 MHz

## Slide 45: T1B05 Which 70 cm frequency is authorized to a Technician Class license holder operating in ITU Region 2?
<number>
Microhams 2010 Technician
  A. 53.350 MHz
  B. 146.520 MHz
C. 443.350 MHz
  D. 222.520 MHz

## Slide 46: T1B06 Which 23 cm frequency is authorized to a Technician Class operator license?
<number>
Microhams 2010 Technician
  A. 2315 MHz
  B. 1296 MHz
  C. 3390 MHz
  D. 146.52 MHz

## Slide 47: T1B06 Which 23 cm frequency is authorized to a Technician Class operator license?
<number>
Microhams 2010 Technician
  A. 2315 MHz
B. 1296 MHz
  C. 3390 MHz
  D. 146.52 MHz

## Slide 48: T1B07 What amateur band are you using if you are transmitting on 223.50 MHz?
<number>
Microhams 2010 Technician
  A. 15 meter band
  B. 10 meter band
  C. 2 meter band
  D. 1.25 meter band

## Slide 49: T1B07 What amateur band are you using if you are transmitting on 223.50 MHz?
<number>
Microhams 2010 Technician
  A. 15 meter band
  B. 10 meter band
  C. 2 meter band
D. 1.25 meter band

## Slide 50: T1B08 What do the FCC rules mean when an amateur frequency band is said to be available on a secondary basis?
<number>
Microhams 2010 Technician
  A. Secondary users of a frequency have equal rights to operate
  B. Amateurs are only allowed to use the frequency at night
  C. Amateurs may not cause harmful interference to primary users
  D. Secondary users are not allowed on amateur bands

## Slide 51: T1B08 What do the FCC rules mean when an amateur frequency band is said to be available on a secondary basis?
<number>
Microhams 2010 Technician
  A. Secondary users of a frequency have equal rights to operate
  B. Amateurs are only allowed to use the frequency at night
C. Amateurs may not cause harmful interference to primary users
  D. Secondary users are not allowed on amateur bands

## Slide 52: T1B09 Why should you not set your transmit frequency to be exactly at the edge of an amateur band or sub-band?
<number>
Microhams 2010 Technician
  A. To allow for calibration error in the transmitter frequency display
  B. So that modulation sidebands do not extend beyond the band edge
  C. To allow for transmitter frequency drift
  D. All of these choices are correct

## Slide 53: T1B09 Why should you not set your transmit frequency to be exactly at the edge of an amateur band or sub-band?
<number>
Microhams 2010 Technician
  A. To allow for calibration error in the transmitter frequency display
  B. So that modulation sidebands do not extend beyond the band edge
  C. To allow for transmitter frequency drift
D. All of these choices are correct

## Slide 54: T1B10 Which of the bands available to Technician Class operators have mode-restricted sub-bands?
<number>
Microhams 2010 Technician
  A. The 6 meter, 2 meter, and 70 cm bands
  B. The 2 meter and 13 cm bands
  C. The 6 meter, 2 meter, and 1.25 meter bands
  D. The 2 meter and 70 cm bands

## Slide 55: T1B10 Which of the bands available to Technician Class operators have mode-restricted sub-bands?
<number>
Microhams 2010 Technician
  A. The 6 meter, 2 meter, and 70 cm bands
  B. The 2 meter and 13 cm bands
C. The 6 meter, 2 meter, and 1.25 meter bands
  D. The 2 meter and 70 cm bands

## Slide 56: T1B11 What emission modes are permitted in the mode-restricted sub-bands at 50.0 to 50.1 MHz and 144.0 to 144.1 MHz?
<number>
Microhams 2010 Technician
  A. CW only
  B. CW and RTTY
  C. SSB only
  D. CW and SSB

## Slide 57: T1B11 What emission modes are permitted in the mode-restricted sub-bands at 50.0 to 50.1 MHz and 144.0 to 144.1 MHz?
<number>
Microhams 2010 Technician
A. CW only
  B. CW and RTTY
  C. SSB only
  D. CW and SSB

## Slide 58: Callsign Groups
FCC Rules
<number>
Group A | 1x2, 2x1 W1AW, KU7M
Group B | 2x2 KK7LK
Group C | 1x3 N7WSU
Group D | 2x3 KB7PJM
All valid US Callsigns start with A, K, N or W and contain a digit 0-9
Notes: <number>
There are no more Group A or B callsigns issued automatically in any call district. All new licenses are either class C or D. In the 7 call district, the new callsigns will be class D.

## Slide 59: US Call Districts
FCC Rules
<number>

## Slide 60: Other Call Sign Categories
FCC Rules
<number>
Vanity Call Sign
  Custom call sign chosen by you
  Can be any valid callsign available to your license class
Club Call Sign
  Call sign for your club
  Can be any valid callsign available to the trustee
Special Event Call Sign
  1x1 – N8D
  Valid only for the duration of the event
  Available to any amateur licensee

## Slide 61: FCC Amateur License
FCC Rules
<number>
N7OS is a Club Vanity License

## Slide 62: T1C01 Which type of call sign has a single letter in both the prefix and suffix?
<number>
Microhams 2010 Technician
  A. Vanity
  B. Sequential
  C. Special event
  D. In-memoriam

## Slide 63: T1C01 Which type of call sign has a single letter in both the prefix and suffix?
<number>
Microhams 2010 Technician
  A. Vanity
  B. Sequential
C. Special event
  D. In-memoriam

## Slide 64: T1C02 Which of the following is a valid US amateur radio station call sign?
<number>
Microhams 2010 Technician
  A. KMA3505
  B. W3ABC
  C. KDKA
  D. 11Q1176

## Slide 65: T1C02 Which of the following is a valid US amateur radio station call sign?
<number>
Microhams 2010 Technician
  A. KMA3505
B. W3ABC
  C. KDKA
  D. 11Q1176

## Slide 66: T1C03 What types of international communications are permitted by an FCC-licensed amateur station?
<number>
Microhams 2010 Technician
  A. Communications incidental to the purposes of the amateur service and remarks of a personal character
  B. Communications incidental to conducting business or remarks of a personal nature
  C. Only communications incidental to contest exchanges, all other communications are prohibited
  D. Any communications that would be permitted on an international broadcast station

## Slide 67: T1C03 What types of international communications are permitted by an FCC-licensed amateur station?
<number>
Microhams 2010 Technician
A. Communications incidental to the purposes of the amateur service and remarks of a personal character
  B. Communications incidental to conducting business or remarks of a personal nature
  C. Only communications incidental to contest exchanges, all other communications are prohibited
  D. Any communications that would be permitted on an international broadcast station

## Slide 68: T1C04 When are you allowed to operate your amateur station in a foreign country?
<number>
Microhams 2010 Technician
  A. When the foreign country authorizes it
  B. When there is a mutual agreement allowing third party communications
  C. When authorization permits amateur communications in a foreign language
  D. When you are communicating with non-licensed individuals in another country

## Slide 69: T1C04 When are you allowed to operate your amateur station in a foreign country?
<number>
Microhams 2010 Technician
A. When the foreign country authorizes it
  B. When there is a mutual agreement allowing third party communications
  C. When authorization permits amateur communications in a foreign language
  D. When you are communicating with non-licensed individuals in another country

## Slide 70: T1C05 What must you do if you are operating on the 23 cm band and learn that you are interfering with a radiolocation station outside the United States?
<number>
Microhams 2010 Technician
  A. Stop operating or take steps to eliminate the harmful interference
  B. Nothing, because this band is allocated exclusively to the amateur service
  C. Establish contact with the radiolocation station and ask them to change frequency
  D. Change to CW mode, because this would not likely cause interference

## Slide 71: T1C05 What must you do if you are operating on the 23 cm band and learn that you are interfering with a radiolocation station outside the United States?
<number>
Microhams 2010 Technician
A. Stop operating or take steps to eliminate the harmful interference
  B. Nothing, because this band is allocated exclusively to the amateur service
  C. Establish contact with the radiolocation station and ask them to change frequency
  D. Change to CW mode, because this would not likely cause interference

## Slide 72: T1C06 From which of the following may an FCC-licensed amateur station transmit, in addition to places where the FCC regulates communications?
<number>
Microhams 2010 Technician
  A. From within any country that belongs to the International Telecommunications Union
  B. From within any country that is a member of the United Nations
  C. From anywhere within in ITU Regions 2 and 3
  D. From any vessel or craft located in international waters and documented or registered in the United States

## Slide 73: T1C06 From which of the following may an FCC-licensed amateur station transmit, in addition to places where the FCC regulates communications?
<number>
Microhams 2010 Technician
  A. From within any country that belongs to the International Telecommunications Union
  B. From within any country that is a member of the United Nations
  C. From anywhere within in ITU Regions 2 and 3
D. From any vessel or craft located in international waters and documented or registered in the United States

## Slide 74: T1C07 What may result when correspondence from the FCC is returned as undeliverable because the grantee failed to provide the correct mailing address?
<number>
Microhams 2010 Technician
  A. Fine or imprisonment
  B. Revocation of the station license or suspension of the operator license
  C. Require the licensee to be re-examined
  D. A reduction of one rank in operator class

## Slide 75: T1C07 What may result when correspondence from the FCC is returned as undeliverable because the grantee failed to provide the correct mailing address?
<number>
Microhams 2010 Technician
  A. Fine or imprisonment
B. Revocation of the station license or suspension of the operator license
  C. Require the licensee to be re-examined
  D. A reduction of one rank in operator class

## Slide 76: T1C08 What is the normal term for an FCC-issued primary station/operator license grant?
<number>
Microhams 2010 Technician
  A. Five years
  B. Life
  C. Ten years
  D. Twenty years

## Slide 77: T1C08 What is the normal term for an FCC-issued primary station/operator license grant?
<number>
Microhams 2010 Technician
  A. Five years
  B. Life
C. Ten years
  D. Twenty years

## Slide 78: T1C09 What is the grace period following the expiration of an amateur license within which the license may be renewed?
<number>
Microhams 2010 Technician
  A. Two years
  B. Three years
  C. Five years
  D. Ten years

## Slide 79: T1C09 What is the grace period following the expiration of an amateur license within which the license may be renewed?
<number>
Microhams 2010 Technician
A. Two years
  B. Three years
  C. Five years
  D. Ten years

## Slide 80: T1C10 How soon may you operate a transmitter on an amateur service frequency after you pass the examination required for your first amateur radio license?
<number>
Microhams 2010 Technician
  A. Immediately
  B. 30 days after the test date
  C. As soon as your name and call sign appear in the FCC's ULS database
  D. You must wait until you receive your license in the mail from the FCC

## Slide 81: T1C10 How soon may you operate a transmitter on an amateur service frequency after you pass the examination required for your first amateur radio license?
<number>
Microhams 2010 Technician
  A. Immediately
  B. 30 days after the test date
C. As soon as your name and call sign appear in the FCC's ULS database
  D. You must wait until you receive your license in the mail from the FCC

## Slide 82: T1C11 If your license has expired and is still within the allowable grace period, may you continue to operate a transmitter on amateur service frequencies?
<number>
Microhams 2010 Technician
  A. No, transmitting is not allowed until the ULS database shows that the license has been renewed
  B. Yes, but only if you identify using the suffix "GP"
  C. Yes, but only during authorized nets
  D. Yes, for up to two years

## Slide 83: T1C11 If your license has expired and is still within the allowable grace period, may you continue to operate a transmitter on amateur service frequencies?
<number>
Microhams 2010 Technician
A. No, transmitting is not allowed until the ULS database shows that the license has been renewed
  B. Yes, but only if you identify using the suffix "GP"
  C. Yes, but only during authorized nets
  D. Yes, for up to two years

## Slide 84: T1D01 With which countries are FCC-licensed amateur stations prohibited from exchanging communications?
<number>
Microhams 2010 Technician
  A. Any country whose administration has notified the ITU that it objects to such communications
  B. Any country whose administration has notified the United Nations that it objects to such communications
  C. Any country engaged in hostilities with another country
  D. Any country in violation of the War Powers Act of 1934

## Slide 85: T1D01 With which countries are FCC-licensed amateur stations prohibited from exchanging communications?
<number>
Microhams 2010 Technician
A. Any country whose administration has notified the ITU that it objects to such communications
  B. Any country whose administration has notified the United Nations that it objects to such communications
  C. Any country engaged in hostilities with another country
  D. Any country in violation of the War Powers Act of 1934

## Slide 86: T1D02 On which of the following occasions may an FCC-licensed amateur station exchange messages with a U.S. military station?
<number>
Microhams 2010 Technician
  A. During an Armed Forces Day Communications Test
  B. During a Memorial Day Celebration
  C. During an Independence Day celebration
  D. During a propagation test

## Slide 87: T1D02 On which of the following occasions may an FCC-licensed amateur station exchange messages with a U.S. military station?
<number>
Microhams 2010 Technician
A. During an Armed Forces Day Communications Test
  B. During a Memorial Day Celebration
  C. During an Independence Day celebration
  D. During a propagation test

## Slide 88: T1D03 When is the transmission of codes or ciphers allowed to hide the meaning of a message transmitted by an amateur station?
<number>
Microhams 2010 Technician
  A. Only during contests
  B. Only when operating mobile
  C. Only when transmitting control commands to space stations or radio control craft
  D. Only when frequencies above 1280 MHz are used

## Slide 89: T1D03 When is the transmission of codes or ciphers allowed to hide the meaning of a message transmitted by an amateur station?
<number>
Microhams 2010 Technician
  A. Only during contests
  B. Only when operating mobile
C. Only when transmitting control commands to space stations or radio control craft
  D. Only when frequencies above 1280 MHz are used

## Slide 90: T1D04 What is the only time an amateur station is authorized to transmit music?
<number>
Microhams 2010 Technician
  A. When incidental to an authorized retransmission of manned spacecraft communications
  B. When the music produces no spurious emissions
  C. When the purpose is to interfere with an illegal transmission
  D. When the music is transmitted above 1280 MHz

## Slide 91: T1D04 What is the only time an amateur station is authorized to transmit music?
<number>
Microhams 2010 Technician
A. When incidental to an authorized retransmission of manned spacecraft communications
  B. When the music produces no spurious emissions
  C. When the purpose is to interfere with an illegal transmission
  D. When the music is transmitted above 1280 MHz

## Slide 92: T1D05 When may amateur radio operators use their stations to notify other amateurs of the availability of equipment for sale or trade?
<number>
Microhams 2010 Technician
  A. When the equipment is normally used in an amateur station and such activity is not conducted on a regular basis
  B. When the asking price is $100.00 or less
  C. When the asking price is less than its appraised value
  D. When the equipment is not the personal property of either the station licensee or the control operator or their close relatives

## Slide 93: T1D05 When may amateur radio operators use their stations to notify other amateurs of the availability of equipment for sale or trade?
<number>
Microhams 2010 Technician
A. When the equipment is normally used in an amateur station and such activity is not conducted on a regular basis
  B. When the asking price is $100.00 or less
  C. When the asking price is less than its appraised value
  D. When the equipment is not the personal property of either the station licensee or the control operator or their close relatives

## Slide 94: T1D06 Which of the following types of transmissions are prohibited?
<number>
Microhams 2010 Technician
  A. Transmissions that contain obscene or indecent words or language
  B. Transmissions to establish one-way communications
  C. Transmissions to establish model aircraft control
  D. Transmissions for third party communications

## Slide 95: T1D06 Which of the following types of transmissions are prohibited?
<number>
Microhams 2010 Technician
A. Transmissions that contain obscene or indecent words or language
  B. Transmissions to establish one-way communications
  C. Transmissions to establish model aircraft control
  D. Transmissions for third party communications

## Slide 96: Station Control
Control Operator
Licensed amateur responsible for proper station operation
Control Point
The point at which the Control Operator function is performed
Local, Remote, Automatic Control
<number>
Microhams 2010 Technician

## Slide 97: T1D07 When is an amateur station authorized to automatically retransmit the radio signals of other amateur stations?
<number>
Microhams 2010 Technician
  A. When the signals are from an auxiliary, beacon, or Earth station
  B. When the signals are from an auxiliary, repeater, or space station
  C. When the signals are from a beacon, repeater, or space station
  D. When the signals are from an Earth, repeater, or space station

## Slide 98: T1D07 When is an amateur station authorized to automatically retransmit the radio signals of other amateur stations?
<number>
Microhams 2010 Technician
  A. When the signals are from an auxiliary, beacon, or Earth station
B. When the signals are from an auxiliary, repeater, or space station
  C. When the signals are from a beacon, repeater, or space station
  D. When the signals are from an Earth, repeater, or space station

## Slide 99: T1D08 When may the control operator of an amateur station receive compensation for operating the station?
<number>
Microhams 2010 Technician
  A. When engaging in communications on behalf of their employer
  B. When the communication is incidental to classroom instruction at an educational institution
  C. When re-broadcasting weather alerts during a RACES net
  D. When notifying other amateur operators of the availability for sale or trade of apparatus

## Slide 100: T1D08 When may the control operator of an amateur station receive compensation for operating the station?
<number>
Microhams 2010 Technician
  A. When engaging in communications on behalf of their employer
B. When the communication is incidental to classroom instruction at an educational institution
  C. When re-broadcasting weather alerts during a RACES net
  D. When notifying other amateur operators of the availability for sale or trade of apparatus

## Slide 101: T1D09 Under which of the following circumstances are amateur stations authorized to transmit signals related to broadcasting, program production, or news gathering, assuming no other means is available?
<number>
Microhams 2010 Technician
  A. Only where such communications directly relate to the immediate safety of human life or protection of property
  B. Only when broadcasting communications to or from the space shuttle.
  C. Only where noncommercial programming is gathered and supplied exclusively to the National Public Radio network
  D. Only when using amateur repeaters linked to the Internet

## Slide 102: T1D09 Under which of the following circumstances are amateur stations authorized to transmit signals related to broadcasting, program production, or news gathering, assuming no other means is available?
<number>
Microhams 2010 Technician
A. Only where such communications directly relate to the immediate safety of human life or protection of property
  B. Only when broadcasting communications to or from the space shuttle.
  C. Only where noncommercial programming is gathered and supplied exclusively to the National Public Radio network
  D. Only when using amateur repeaters linked to the Internet

## Slide 103: T1D10 What is the meaning of the term broadcasting in the FCC rules for the amateur services?
<number>
Microhams 2010 Technician
  A. Two-way transmissions by amateur stations
  B. Transmission of music
  C. Transmission of messages directed only to amateur operators
  D. Transmissions intended for reception by the general public

## Slide 104: T1D10 What is the meaning of the term broadcasting in the FCC rules for the amateur services?
<number>
Microhams 2010 Technician
  A. Two-way transmissions by amateur stations
  B. Transmission of music
  C. Transmission of messages directed only to amateur operators
D. Transmissions intended for reception by the general public

## Slide 105: T1D11 Which of the following types of communications are permitted in the Amateur Radio Service?
<number>
Microhams 2010 Technician
  A. Brief transmissions to make station adjustments
  B. Retransmission of entertainment programming from a commercial radio or TV station
  C. Retransmission of entertainment material from a public radio or TV station
  D. Communications on a regular basis that could reasonably be furnished alternatively through other radio services

## Slide 106: T1D11 Which of the following types of communications are permitted in the Amateur Radio Service?
<number>
Microhams 2010 Technician
A. Brief transmissions to make station adjustments
  B. Retransmission of entertainment programming from a commercial radio or TV station
  C. Retransmission of entertainment material from a public radio or TV station
  D. Communications on a regular basis that could reasonably be furnished alternatively through other radio services

## Slide 107: T1E01 When must an amateur station have a control operator?
<number>
Microhams 2010 Technician
  A. Only when the station is transmitting
  B. Only when the station is being locally controlled
  C. Only when the station is being remotely controlled
  D. Only when the station is being automatically controlled

## Slide 108: T1E01 When must an amateur station have a control operator?
<number>
Microhams 2010 Technician
A. Only when the station is transmitting
  B. Only when the station is being locally controlled
  C. Only when the station is being remotely controlled
  D. Only when the station is being automatically controlled

## Slide 109: T1E02 Who is eligible to be the control operator of an amateur station?
<number>
Microhams 2010 Technician
  A. Only a person holding an amateur service license from any country that belongs to the United Nations
  B. Only a citizen of the United States
  C. Only a person over the age of 18
  D. Only a person for whom an amateur operator/primary station license grant appears in the FCC database or who is authorized for alien reciprocal operation

## Slide 110: T1E02 Who is eligible to be the control operator of an amateur station?
<number>
Microhams 2010 Technician
  A. Only a person holding an amateur service license from any country that belongs to the United Nations
  B. Only a citizen of the United States
  C. Only a person over the age of 18
D. Only a person for whom an amateur operator/primary station license grant appears in the FCC database or who is authorized for alien reciprocal operation

## Slide 111: T1E03 Who must designate the station control operator?
<number>
Microhams 2010 Technician
  A. The station licensee
  B. The FCC
  C. The frequency coordinator
  D. The ITU

## Slide 112: T1E03 Who must designate the station control operator?
<number>
Microhams 2010 Technician
A. The station licensee
  B. The FCC
  C. The frequency coordinator
  D. The ITU

## Slide 113: T1E04 What determines the transmitting privileges of an amateur station?
<number>
Microhams 2010 Technician
  A. The frequency authorized by the frequency coordinator
  B. The class of operator license held by the station licensee
  C. The highest class of operator license held by anyone on the premises
  D. The class of operator license held by the control operator

## Slide 114: T1E04 What determines the transmitting privileges of an amateur station?
<number>
Microhams 2010 Technician
  A. The frequency authorized by the frequency coordinator
  B. The class of operator license held by the station licensee
  C. The highest class of operator license held by anyone on the premises
D. The class of operator license held by the control operator

## Slide 115: T1E05 What is an amateur station control point?
<number>
Microhams 2010 Technician
  A. The location of the station's transmitting antenna
  B. The location of the station transmitting apparatus
  C. The location at which the control operator function is performed
  D. The mailing address of the station licensee

## Slide 116: T1E05 What is an amateur station control point?
<number>
Microhams 2010 Technician
  A. The location of the station's transmitting antenna
  B. The location of the station transmitting apparatus
C. The location at which the control operator function is performed
  D. The mailing address of the station licensee

## Slide 117: T1E06 Under which of the following types of control is it permissible for the control operator to be at a location other than the control point?
<number>
Microhams 2010 Technician
  A. Local control
  B. Automatic control
  C. Remote control
  D. Indirect control

## Slide 118: T1E06 Under which of the following types of control is it permissible for the control operator to be at a location other than the control point?
<number>
Microhams 2010 Technician
  A. Local control
B. Automatic control
  C. Remote control
  D. Indirect control

## Slide 119: T1E07 When the control operator is not the station licensee, who is responsible for the proper operation of the station?
<number>
Microhams 2010 Technician
  A. All licensed amateurs who are present at the operation
  B. Only the station licensee
  C. Only the control operator
  D. The control operator and the station licensee are equally responsible

## Slide 120: T1E07 When the control operator is not the station licensee, who is responsible for the proper operation of the station?
<number>
Microhams 2010 Technician
  A. All licensed amateurs who are present at the operation
  B. Only the station licensee
  C. Only the control operator
D. The control operator and the station licensee are equally responsible

## Slide 121: T1E08 What type of control is being used for a repeater when the control operator is not present at a control point?
<number>
Microhams 2010 Technician
  A. Local control
  B. Remote control
  C. Automatic control
  D. Unattended

## Slide 122: T1E08 What type of control is being used for a repeater when the control operator is not present at a control point?
<number>
Microhams 2010 Technician
  A. Local control
  B. Remote control
C. Automatic control
  D. Unattended

## Slide 123: T1E09 What type of control is being used when transmitting using a handheld radio?
<number>
Microhams 2010 Technician
  A. Radio control
  B. Unattended control
  C. Automatic control
  D. Local control

## Slide 124: T1E09 What type of control is being used when transmitting using a handheld radio?
<number>
Microhams 2010 Technician
  A. Radio control
  B. Unattended control
  C. Automatic control
D. Local control

## Slide 125: T1E10 What type of control is used when the control operator is not at the station location but can indirectly manipulate the operating adjustments of a station?
<number>
Microhams 2010 Technician
  A. Local
  B. Remote
  C. Automatic
  D. Unattended

## Slide 126: T1E10 What type of control is used when the control operator is not at the station location but can indirectly manipulate the operating adjustments of a station?
<number>
Microhams 2010 Technician
  A. Local
B. Remote
  C. Automatic
  D. Unattended

## Slide 127: T1E11 Who does the FCC presume to be the control operator of an amateur station, unless documentation to the contrary is in the station records?
<number>
Microhams 2010 Technician
  A. The station custodian
  B. The third party participant
  C. The person operating the station equipment
  D. The station licensee

## Slide 128: T1E11 Who does the FCC presume to be the control operator of an amateur station, unless documentation to the contrary is in the station records?
<number>
Microhams 2010 Technician
  A. The station custodian
  B. The third party participant
  C. The person operating the station equipment
D. The station licensee

## Slide 129: T1F01 What type of identification is being used when identifying a station on the air as "Race Headquarters"?
<number>
Microhams 2010 Technician
  A. Tactical call
  B. Self-assigned designator
  C. SSID
  D. Broadcast station

## Slide 130: T1F01 What type of identification is being used when identifying a station on the air as "Race Headquarters"?
<number>
Microhams 2010 Technician
A. Tactical call
  B. Self-assigned designator
  C. SSID
  D. Broadcast station

## Slide 131: T1F02 When using tactical identifiers, how often must your station transmit the station's FCC-assigned call sign?
<number>
Microhams 2010 Technician
  A. Never, the tactical call is sufficient
  B. Once during every hour
  C. Every ten minutes
  D. At the end of every communication

## Slide 132: T1F02 When using tactical identifiers, how often must your station transmit the station's FCC-assigned call sign?
<number>
Microhams 2010 Technician
  A. Never, the tactical call is sufficient
  B. Once during every hour
C. Every ten minutes
  D. At the end of every communication

## Slide 133: T1F03 When is an amateur station required to transmit its assigned call sign?
<number>
Microhams 2010 Technician
  A. At the beginning of each contact, and every 10 minutes thereafter
  B. At least once during each transmission
  C. At least every 15 minutes during and at the end of a contact
  D. At least every 10 minutes during and at the end of a contact

## Slide 134: T1F03 When is an amateur station required to transmit its assigned call sign?
<number>
Microhams 2010 Technician
  A. At the beginning of each contact, and every 10 minutes thereafter
  B. At least once during each transmission
  C. At least every 15 minutes during and at the end of a contact
D. At least every 10 minutes during and at the end of a contact

## Slide 135: T1F04 Which of the following is an acceptable language for use for station identification when operating in a phone sub-band?
<number>
Microhams 2010 Technician
  A. Any language recognized by the United Nations
  B. Any language recognized by the ITU
  C. The English language
  D. English, French, or Spanish

## Slide 136: T1F04 Which of the following is an acceptable language for use for station identification when operating in a phone sub-band?
<number>
Microhams 2010 Technician
  A. Any language recognized by the United Nations
  B. Any language recognized by the ITU
C. The English language
  D. English, French, or Spanish

## Slide 137: T1F05 What method of call sign identification is required for a station transmitting phone signals?
<number>
Microhams 2010 Technician
  A. Send the call sign followed by the indicator RPT
  B. Send the call sign using CW or phone emission
  C. Send the call sign followed by the indicator R
  D. Send the call sign using only phone emission

## Slide 138: T1F05 What method of call sign identification is required for a station transmitting phone signals?
<number>
Microhams 2010 Technician
  A. Send the call sign followed by the indicator RPT
B. Send the call sign using CW or phone emission
  C. Send the call sign followed by the indicator R
  D. Send the call sign using only phone emission

## Slide 139: T1F06 Which of the following formats of a self-assigned indicator is acceptable when identifying using a phone transmission?
<number>
Microhams 2010 Technician
  A. KL7CC stroke W3
  B. KL7CC slant W3
  C. KL7CC slash W3
  D. All of these choices are correct

## Slide 140: T1F06 Which of the following formats of a self-assigned indicator is acceptable when identifying using a phone transmission?
<number>
Microhams 2010 Technician
  A. KL7CC stroke W3
  B. KL7CC slant W3
  C. KL7CC slash W3
D. All of these choices are correct

## Slide 141: T1F07 Which of the following restrictions apply when appending a self-assigned call sign indicator?
<number>
Microhams 2010 Technician
  A. It must be more than three letters and less than five letters
  B. It must be less than five letters
  C. It must start with the letters AA through AL, K, N, or W and be not less than two characters or more than five characters in length
  D. It must not conflict with any other indicator specified by the FCC rules or with any call sign prefix assigned to another country

## Slide 142: T1F07 Which of the following restrictions apply when appending a self-assigned call sign indicator?
<number>
Microhams 2010 Technician
  A. It must be more than three letters and less than five letters
  B. It must be less than five letters
  C. It must start with the letters AA through AL, K, N, or W and be not less than two characters or more than five characters in length
D. It must not conflict with any other indicator specified by the FCC rules or with any call sign prefix assigned to another country

## Slide 143: T1F08 When may a Technician Class licensee be the control operator of a station operating in an exclusive Extra Class operator segment of the amateur bands?
<number>
Microhams 2010 Technician
  A. Never
  B. On Armed Forces Day
  C. As part of a multi-operator contest team
  D. When using a club station whose trustee is an Extra Class operator licensee

## Slide 144: T1F08 When may a Technician Class licensee be the control operator of a station operating in an exclusive Extra Class operator segment of the amateur bands?
<number>
Microhams 2010 Technician
A. Never
  B. On Armed Forces Day
  C. As part of a multi-operator contest team
  D. When using a club station whose trustee is an Extra Class operator licensee

## Slide 145: T1F09 What type of amateur station simultaneously retransmits the signal of another amateur station on a different channel or channels?
<number>
Microhams 2010 Technician
  A. Beacon station
  B. Earth station
  C. Repeater station
  D. Message forwarding station

## Slide 146: T1F09 What type of amateur station simultaneously retransmits the signal of another amateur station on a different channel or channels?
<number>
Microhams 2010 Technician
  A. Beacon station
  B. Earth station
C. Repeater station
  D. Message forwarding station

## Slide 147: T1F10 Who is accountable should a repeater inadvertently retransmit communications that violate the FCC rules?
<number>
Microhams 2010 Technician
  A. The control operator of the originating station
  B. The control operator of the repeater
  C. The owner of the repeater
  D. Both the originating station and the repeater owner

## Slide 148: T1F10 Who is accountable should a repeater inadvertently retransmit communications that violate the FCC rules?
<number>
Microhams 2010 Technician
A. The control operator of the originating station
  B. The control operator of the repeater
  C. The owner of the repeater
  D. Both the originating station and the repeater owner

## Slide 149: T1F11 To which foreign stations do the FCC rules authorize the transmission of non-emergency third party communications?
<number>
Microhams 2010 Technician
  A. Any station whose government permits such communications
  B. Those in ITU Region 2 only
  C. Those in ITU Regions 2 and 3 only
  D. Those in ITU Region 3 only

## Slide 150: T1F11 To which foreign stations do the FCC rules authorize the transmission of non-emergency third party communications?
<number>
Microhams 2010 Technician
A. Any station whose government permits such communications
  B. Those in ITU Region 2 only
  C. Those in ITU Regions 2 and 3 only
  D. Those in ITU Region 3 only

## Slide 151: T1F12 How many persons are required to be members of a club for a club station license to be issued by the FCC?
<number>
Microhams 2010 Technician
  A. At least 5
  B. At least 4
  C. A trustee and 2 officers
  D. At least 2

## Slide 152: T1F12 How many persons are required to be members of a club for a club station license to be issued by the FCC?
<number>
Microhams 2010 Technician
  A. At least 5
B. At least 4
  C. A trustee and 2 officers
  D. At least 2

## Slide 153: T1F13 When must the station licensee make the station and its records available for FCC inspection?
<number>
Microhams 2010 Technician
  A. Any time upon request by an official observer
  B. Any time upon request by an FCC representative
  C. 30 days prior to renewal of the station license
  D. 10 days before the first transmission

## Slide 154: T1F13 When must the station licensee make the station and its records available for FCC inspection?
<number>
Microhams 2010 Technician
  A. Any time upon request by an official observer
B. Any time upon request by an FCC representative
  C. 30 days prior to renewal of the station license
  D. 10 days before the first transmission

## Slide 155: SUBELEMENT T1 [6 exam questions – 6 groups]
<number>
Microhams 2010 Technician
Notes: <number>
http://www.microhams.com
Created by Scott N7SS