## Slide 1: Math for the General Class Ham Radio Operator
A prerequisite math refresher for the math phobic ham
Notes: <number>

## Slide 2: Why is This Lesson for You?
The General Class license requires the study and understanding of:
  The science and art of radio and electronics.
  The math needed to deal with the scientific concepts.
  The technology (calculator) to do the math.
For some, these three challenges are frustrating to deal with all at the same time.
The result … “memorize the answers.”
Notes: <number>
The study and enjoyment of ham radio requires the mastery at some level of three areas: the science and art of radio and electronics, the math needed to fully understand and use the science of radio and electronics, and the technology to do the math. For many, math classes are a pleasant (and for some not so pleasant) memory for their formal schooling days. Admittedly, the math required to fully understand the science and art of radio is not the kind of math that most people use every day. The level of math required for the Technician and General Class license is Algebra 1, the level required for Extra Class is Algebra 2 and some Trigonometry . Though this level of math may sound intimidating, it really isn’t that difficult, and there are only a very few specific formulas that the ham needs to be able to solve and understand. Modern calculator technology certainly takes the drudgery out of solving the math problems.
The frustration comes from all three content areas coming at you all at the same time. While the licensee is trying the study the material and understand the fundamental concepts, they are at the same time slapped with the math formulas that are used to explain the concepts … and then faced with a calculator that has a gazillion buttons. The result is “memorize the answers” and hope for the best.
If you do not want to just settle for “memorizing the answers”, then this course is for you.

## Slide 3: Math Vocabulary
What are equations and formulas?
What do variables mean?
What does solving an equation mean?
Getting the final answer!
Notes: <number>
We now will being to look at a little math refresher and will start with understanding some common terms. It is necessary to establish a common set of words so that we can communicate in the language of math. Some of the vocabulary words and the definitions will make the pure mathematician cringe, but we are going to take a practical approach, one that will allow you to accomplish the job and communicate with math. This will take a little instructor poetic license to help get the points across without getting bogged down in the pure technicalities of mathematics.
So we will begin by defining what we mean by equations and formulas (those terms will be interchangeable in this course), what they represent, and what they are used for.
Then we will discuss how letters (variables) are used to represent something in an equation that will be later replaced by an actual number for final computation of the answer.
Next we will discuss the mechanics of moving the variables around in the equation to focus (solve) on the particular variable of interest that we are looking form.
And finally, we will plug some numbers first into the variables, and then into the calculator to get the answer we are looking for.

## Slide 4: Math Vocabulary What are equations and formulas?
Equations are relationships between things that are exactly equivalent (have the same overall value).
Two equivalent sets of things are shown equal by using the equal sign (=).
The left side of the = has the same value as the right side.
Notes: <number>
It is bad form to use the word to define the word, in this case using equivalent to define equation. But it is the easiest way to define equations. When you compare two things whether it is numbers or anything else, if those two things are equivalent or have the same value, then they are equal. In mathematics, equations are used to show the relationship between two sets of numbers or values. If those two sets of numbers or values have exactly the value, then they are equal, and that relationship is shown with the equal sign.
In math, an equation is also called a formula which is a way to mathematically show the relationship between things. During this course you will hear equation and formula used interchangeably. They mean the same thing…they are equal.
So in an equation, the collection of things or numbers on one side of the equal sign has the exact same value as the collection of the things or numbers on the other side.

## Slide 5: Math Vocabulary What do variables mean?
Many times relationships between things are not specific to just one case.
To accommodate many different cases, substitute symbols are used to take the place of specific, discrete numbers in an equation or formula.
  These symbols are called variables and usually are letters.
  The variables are place holders that represent actual numbers that are as yet to be determined.
  Variables are treated just like the numbers they represent.
Later on, specific numbers can be put in the place of the variables and the equation can be solved.
  (solved means to come up with the final answer)
Notes: <number>
The real value of using equations to show relationships in math, is that the equation can show the relationship in all cases, not just a very specific case. For instance, an equation that shows the relationship between a radio wave frequency and the length of an antenna to use on that frequency is more useful that having to have an arithmetic problem for each and every frequency. One equation can be used for all frequencies, you just have to plug different numbers into the equation when to want to find the final answer.
So, variables are used in math equations to represent specific numbers…they act as place holders for the numbers. Later the numbers and substituted back into the equation to calculate the final answer. Generally, letters are used as variables and most times the letters are chosen in such a way that give an indication what is represented. For instance, a common variable for radius is r, for frequency is f, etc.
Here is a good place to put up before the class some common formulas they will see in their ham studies. Simply point of the variables, but don’t spend a lot of time on the particulars of what the variables represent…that is for the other course.

## Slide 6: Math Vocabulary What does solving an equation mean?
Now we are getting to the meat of the math review, solving equations.
Solving an equation means to manipulate (move around the equation) the variables (the place holders that represent actual numbers) to find the answer we are looking for.

## Slide 7: Math Vocabulary What does solving an equation mean?
When we solve an equation, we move what we are looking for to one side of the equal sign, and move everything else to the other side.
There are short cuts to this process, but we are going to stress doing it one-step-at-a-time to reinforce learning the concepts.
  It may seem tedious at first, but well worth the effort for later.

## Slide 8: Math Vocabulary What does solving an equation mean?
Every variable in an equation is “participating” or interacting with other variables through some mathematic operation.
Math operations:
  Add: +
  Subtract: -
  Multiply: X or *
  Divide: / or
  Roots: or
  Etc.

## Slide 9: Math Vocabulary What does solving an equation mean?
When you move variables from one side of the equation to the other, it takes a little “math sense” to know which one to move first.
Be patient, it takes time and practice to develop “math sense.”

## Slide 10: Math Vocabulary What does solving an equation mean?
If you do something to one side of the equation, you must do exactly the same thing to the other side of the equation to keep everything equal…this is important.
When you move a variable, apply the opposite math operation the variable is doing to both sides of the equation.

## Slide 11: Math Vocabulary What does solving an equation mean?
Opposite math operations:
  Addition/subtraction
  Multiplication/division
  Roots and squares (or roots and powers)

## Slide 12: Math Vocabulary What does solving an equation mean?
Here is our first example to illustrate solving an equation.
The equation for Ohm’s Law is:
E = I*R
The variables mean:
  E represents voltage
  I represents current
  R represents resistance
The math operator is multiplication.

## Slide 13: Math Vocabulary What does solving an equation mean?
If we know the current and the resistance, we can easily calculate the voltage by replacing the variables with the actual numbers:
  Current is 10 (we will disregard units for now)
  Resistance is 50
Therefore: E = 10*50
E = 500 (in this case volts)

## Slide 14: Math Vocabulary What does solving an equation mean?
What if we know the voltage and the current and want to find the resistance?
Here is where we need to solve the equation for resistance, then do the arithmetic.
To do this, we need to move the “I” from the right side to the left side so that the “R” is all by itself on the right side of the equation.
  E = I*R
  to
  2. E/I = R

## Slide 15: Math Vocabulary What does solving an equation mean?
To move a variable from one side to the other side of an equation, apply the variable to BOTH sides using the opposite math operation.
In this case the operation in the equation is multiplication, the opposite operation is division.
The variable to be moved is “I.”

## Slide 16: Ohms Law & Power
Ohms Law E=IR
Power P=EI
Combining these You can Get
P=I2 R or P=E2 R

## Slide 17: Decibels
The standard way used to describe Power or Voltage ratios
dB = 10log10 (Pm/Pref)
dB = 20log10 (Vm/Vref)
3dB is a factor of 2 in power
10dB is a factor of 10 in power

## Slide 18: AC RMS
The RMS value of an AC voltage will dissipate the same power as the same value DC voltage into a Resistive Load
For a sine wave
Vrms=.707Vpk = .707Vp-p/2
Vpk =1.414Vrms

## Slide 19: Peak Envelope Power
Peak Envelope Power (PEP) is how the FCC specifies your transmitter power.
For an unmodulated carrier PEP =Average Power also true for FM, FSK, PSK. Do not confuse with peak voltage PEP is calculated using RMS voltage.
PEP = (Vrms)2 /R

## Slide 20: Quiz Time
Section 4.1
G5B01 – A B C D
G5B03 – A B C D
G5B04 – A B C D
G5B05 – A B C D
G5B10 – A B C D
Section 4.2
G5B06 – A B C D
G5B07 – A B C D
G5B08 – A B C D
G5B09 – A B C D
G5B11 – A B C D
G5B12 – A B C D
G5B13 – A B C D
G5B14 – A B C D