## Slide 1
Technician License Course Chapter 5 Operating Station Equipment
Lesson Plan Module 11:
Transmitters, Receivers and Transceivers

## Slide 2
Generalized Transceiver Categories
Single Band VHF or UHF FM
Dual Band VHF/UHF FM
Multimode VHF/UHF
Multiband HF and VHF/UHF
Handheld (HT)
Notes: In this lesson you will be comparing and contrasting the different kinds of equipment available. You can adjust these categories to meet your personal preferences and experiences. It would be a good idea to have examples of the different kinds of equipment. Catalogs from the major equipment retailers would be helpful to give an idea of the level of costs. Go ahead and deviate from any kind of lesson script during this lesson but keep in mind the time and keep from spending too much time on this topic.

## Slide 3
Single Band Transceiver
Probably the most common starter rig.
Operates from 12 volts dc, requires external power supply.
Requires an external antenna.
Can be operated mobile or as a base station.
Limited to frequency modulation (FM) and usually either 2 meters or 70 cm bands.
Up to approximately 50 watts output.
Notes: Let students know that the term rig refers to the equipment being used. The specific equipment referenced comes from the context in which the word is used.

## Slide 4
Dual Band Transceiver
Same as the single band transceiver but includes additional band(s).
Most common are 2 meter and 70 cm bands.
Could add 6 meters, 222 MHz or 1.2 GHz.
Depending on antenna connectors, might require separate coax for each band or a duplexer for single coax.
Notes: You will have to explain how a single coax can be used for two bands in this rig and the possible complication of dealing with single antennas, dual band antennas, how duplexers are used etc.

## Slide 5
Multimode Transceiver
Can be single or multiband.
Main difference is that these rigs can operate on all major modes SSB/AM/FM, CW, Data, RTTY etc.
More features add complexity and cost.
Most flexible of the rigs that will allow you to explore new modes as you gain experience.

## Slide 6
Multiband Transceiver
Covers many bands – can be limited to HF or can be HF/VHF/UHF.
Also covers all modes.
Frequently 100 watts on HF, some power limitations on high bands (50 watts).
Larger units have internal power supplies, smaller units need external power (13.8 V).

## Slide 7
Handheld (HT) Transceiver
Small handheld FM units.
Can be single band or dual band.
Limited power (usually 5 watts or less).
Includes power (battery) and antenna in one package.
An attractive first starter rig – but make sure it is what you want.
Notes: The HT is probably the most attractive starter rig for new hams. Spend some time discussing the advantages and limitations of the HT, particularly for your area of operation. I emphasize caution in having the HT as the starter rig because of the sometimes disappointing performance in remote or sparsely repeater populated areas. I encourage hams to consider the HT as the secondary radio and steer them toward the single band transceiver as their first rig.

## Slide 8
Side-by-Side
 | Single Band | Dual Band | Multimode | Multiband | Handheld
Freq Agility | Limited | Medium | Medium | Full | Limited
Functionality | Limited | Limited | Full | Full | Limited
Ease of Use | Easy | Medium | Medium | Difficult | Easy
Programming | Easy | Easy | Medium | Challenging | Easy/Medium
Power | Low | Low | Medium | High | Low
Cost | Low | Modest | High | High | Low
Notes: This how I would assess the various rigs side-by-side, you may want to adjust this based on your assessment. Power levels are all green because it all depends on the area and what the ham wants to accomplish. This slide could generate a lot of good discussion questions, so let it.

## Slide 9
Rig Vocabulary
We will now go through some jargon and vocabulary specific to the functions and controls of a transmitter and receiver.
  This is a way to discuss how to operate a transceiver.
These controls, though separate, are combined in a transceiver.
Notes: The following presentation serves a dual purpose. It will allow you to focus on vocabulary that might show up in the examination and also allow you to discuss with the students how you operate a transmitter and a receiver.

## Slide 10
Transmitter Controls and Functions
Band selection
Memories
Main tuning dial (both TX and RX):
  Controls the frequency selection via the variable frequency oscillator (VFO).
  Could be an actual dial or key pad or programmed channels.
  Variable frequency step size (tuning rate, resolution).
  Could have more than one VFO (control more that one frequency at a time).

## Slide 11
Transmitter Controls and Functions
Mode selector (both TX and RX for multimode rigs).
  AM/FM/SSB (LSB or USB)
  CW
  Data (RTTY)
Could be automatic based on recognized band plan.

## Slide 12
Transmitter Controls and Functions
Microphone controls
  Gain
    How loudly you need to talk to be heard.
  Speech Compressor or Speech Processor
    Compacting your speech into a narrow frequency range to enhance “punch.”
    Use Compression sparingly.
  Too much gain or compression can cause problems.
    Splatter
    Over-deviation
    Over-modulation

## Slide 13
Transmitter Controls and Functions
Power output level
Automatic Level Control (ALC).
  Automatically limits transmitter drive (output level) to prevent problems associated with too much gain or compression.
Also can control external power amplifier operation.

## Slide 14
Transmitter Controls and Functions
Transmitter on/off
  Push-to-Talk (PTT)
  Voice-Operated Transmission (VOX)
    VOX Gain
    VOX Delay
    Anti-VOX
  Key jack
Notes: Spend some time here explaining the various VOX controls and how they affect the control of the transceiver.

## Slide 15
Transmitter Controls and Functions
Microphones (Mic)
  Hand mics
  Desk mics
    Preamplified desk mikes
  Speaker-mics
  Headsets or boom-sets
  Internal mikes
  Microphone connectors are not standardized even those of the same type may have different connections and may contain voltages to power active microphones
Speak across the mic, not into the mic.
Notes: As you talk about microphones, give the students some techniques on how close to hold the mic to their mouth, how to speak into the mic (clearly and distinctly), and speak across the mic not directly into the mic (to prevent lip smacking and spitting sounds).

## Slide 16
Transmitter Controls and Functions
Morse Keys
  Straight key
  Electronic keyer and paddle
  Semi-automatic (Bug)

## Slide 17
Receiver Controls and Functions
AF Gain or Volume
  Controls the audio level to the speaker or headphones.
RF Gain
  Controls the strength of radio signal entering the receiver.
  Used to limit (attenuate) very strong local signals.
  Usually operated in the full-open position.

## Slide 18
Receiver Controls and Functions
Automatic Gain Control (AGC)
  Automatically limits the incoming signals during signal (voice) peaks.
    Prevents peaks from capturing the receiver and limiting reception of lower level portions of the incoming signal.
  Fast setting for CW.
  Slow settings for SSB and AM.
  Not used in FM because of the type of signal used in FM.
Receiver Incremental Tuning (RIT)
  Adjusts the Receiver Frequency offset from transmiter

## Slide 19
Receiver Controls and Functions
Carrier Squelch
  Turns off audio to speaker when signal is not present.
Tone (or Code) Squelch
    Turns off audio to speaker when tone or digital code.
Used in FM primarily
  Open – allows very weak signals to pass through (along with noise).
  Tight – allows only the strongest signals to pass through.
Advance the squelch control until the noise just disappears.

## Slide 20
Receiver Controls and Functions
Filters
  Bandwidth filter
    SSB – 2400 Hz, CW – 500 Hz
    Used to narrow the width of signal that is passed.
    Can attenuate adjacent interference.
  Notch filter
    Very narrow filter that can be moved over an interfering signal to attenuate it.
  Noise blanker or limiter
    Limits signal spikes that are frequently associated with random naturally generated noise.

## Slide 21
Receiver Controls and Functions
Reception and Transmission Meter.
  In transmit, indicates output power or ALC or other functions as selected by switch setting.
In receive - indicates signal strength.
  In “S” units S1 through S9 – S9 is strongest.
  Also have dB over S9 to cover very strong signals.

## Slide 22
Receiver Controls and Functions
Receivers can be limited to ham bands or can cover other parts of the spectrum.
General coverage receivers cover a wide area of the spectrum and can be used for shortwave listening (SWL).

## Slide 23
Handheld Transceivers
Single, dual and multiband versions (with increasing cost and complexity).
  Some have expanded receiver coverage (wide-band receive).
Very portable and self-contained.
  Internal microphone and speaker.
  Rubber duck antenna.
  Battery powered.
Notes: Spend some time discussing how to get the most performance out of the HT (hold the HT vertical, speak across the mic, not into the mic, etc.)
Also make sure that you cover that the rubber duck antenna actually has negative gain when compared to other antennas, that the trade-off for the convenience of a small, flexible antenna is reduced performance.

## Slide 24
Nice to have handheld accessories
Extra battery packs.
Drop-in, fast charger.
Extended antenna.
External microphone and speaker.
Headset.

## Slide 25: Quiz Time
Chapter 5.1

## Slide 26: Chapter 5.1 Key
T2B03 A B C D
T4A01 A B C D
T4B01 A B C D
T4B02 A B C D
T4B03 A B C D
T4B04 A B C D
T4B05 A B C D
T4B06 A B C D
T4B07 A B C D
T4B08 A B C D
T4B09 A B C D
T4B10 A B C D
T7A10 A B C D
T7B01 A B C D
T7C01 A B C D
T8D10 A B C D

## Slide 27
Data Modes
Connecting computers via ham radio.
  Some systems use radio to connect to Internet gateways.
The bulk of the work is done by specialized modems or computer software/sound card.
  Terminal Node Controller (TNC).
  Multiple Protocol Controller (MPC).

## Slide 28: Popular Digital Modes
Radioteletype (RTTY)(FSK)
MFSK Multipule Frequency Shift Keying
  2,3,4 bits at a time
PSK31 or PSK63
  Phase Shift Keying
Packet Radio usually VHF
  AX.25 with header, checksum, automatic repeat
Automatic Packet Reporting System (APRS)
Winlink

## Slide 29: Errors & Codes
BER – bit error rate
  Noise interference or multipath can cause errors
  Adding a parity bit can detect errors.
  Some modes (ie AMTOR & Packet) are error correcting.
Codes used
  CW – International Morse Code
  RTTY – Baudot (5 bit)
  Packet – ASCII
  PSK31 - varicode

## Slide 30: Automatic Position Reporting System (APRS)

## Slide 31
Data Station Setup

## Slide 32: Internet Gateway

## Slide 33
Power Supplies
Most modern radio equipment runs from 12 volts dc.
Household current is 120 volts ac.
Power supplies convert 120 volts ac to 12 volts dc.
  13.8 volts dc is the common voltage you will see.
  This is the charging voltage for motorized vehicles.

## Slide 34
Types of Power Supplies
Linear:
  Transformers
  Heavy (physically)
  Heavy duty current
  Expensive
Switching:
  Electronics instead of transformers
  Light weight and small
  Not as robust
  Less expensive
Notes: Examples of the different kinds of supplies would be helpful to illustrate the differences.

## Slide 35
Power Supply Ratings Voltage and Current
Continuous duty – how much current can be supplied over the long term.
Intermittent duty – how much surge current can be supplied over the short term.
Regulation – how well the power supply can handle rapid current changes.

## Slide 36
Mobile Power Wiring Safety
Car batteries hold lots of energy – shorting a battery could cause a fire.
If power is not well filtered a high pitched wine from the alternator can be heard in the audio.
Special requirements for safe car wiring:
  Fuse both positive and negative leads.
  Connect radio’s negative lead to where the battery ground connection is made.
  Use grommets or protective sleeves to prevent wire chafing.
  Don’t assume all metal in the car is grounded; modern cars are as much plastic as metal.
Notes: The concept of fusing both the negative and positive leads of the equipment in a car installation might take some explanation.

## Slide 37
Batteries
Create current through a chemical reaction.
  Made up of individual cells connected in series or parallel.
  Ni-cad 1.2 V/cell
  Alkaline 1.5 V/cell
  Lead Acid 2 V/Cell
  Lithium Ion .2 V/cell
Battery types.
  Disposable Carbon –Zinc, Alkaline
  Rechargeable. Ni-Cd, Lead-Acid, Lithium Ion
Power capabilities rated in Ampere-hours.
  Amps X time.
Notes: Examples of the different kinds of batteries will help illustrate this point. Discuss how the different kinds of batteries are used.

## Slide 38
Battery Charging
Some batteries can be recharged, some cannot.
Use the proper charger for the battery being charged.
Batteries will wear out over time.
Best if batteries are maintained fully charged.
  Over-charging will cause heating and could damage the battery.
Some batteries (lead-acid) will release toxic fumes during charging so require ventilation.

## Slide 39
Handheld Transceivers
Battery packs – packages of several individual rechargeable batteries connected together.
  NiCd (nickel-cadmium)
  NiMH (nickel-metal hydride)
  Li-ion (lithium-ion)
For emergencies, have a battery pack that can use disposable batteries (AA size)
Notes: Spend some time discussing how to get the most performance out of the HT (hold the HT vertical, speak across the mic, not into the mic, etc.)
Also make sure that you cover that the rubber duck antenna actually has negative gain when compared to other antennas, that the trade-off for the convenience of a small, flexible antenna is reduced performance.

## Slide 40: QuizTime
Chapter 5.2 & 5.3

## Slide 41: Chapter 5.2 Key
T4A06 A B C D
T4A07 A B C D
T7B12 A B C D
T8C11 A B C D
T8D01 A B C D
T8D02 A B C D
T8D03 A B C D
T8D06 A B C D
T8D07 A B C D
T8D08 A B C D
T8D09 A B C D
T8D11 A B C D

## Slide 42: Chapter 5.3 Key
T4A03 A B C D
T4A10 A B C D
T4A11 A B C D
T5A06 A B C D
T6A10 A B C D
T6A11 A B C D
T6D05 A B C D
T7B09 A B C D
T0A08 A B C D
T0A09 A B C D
T0A10 A B C D

## Slide 43
Radio Frequency Interference (RFI)
Unwanted, unintentional signals from some electronic device that interferes with radio wave reception.
You can prevent creating RFI by operating your transmitting equipment properly.
Notes: Point out that RFI can come from virtually any electronic device from overhead power lines, to electric can openers, to computers and TV sets.

## Slide 44
Types of RFI
Direct detection – offending signals get into the electronics circuits to cause interference.
Overload – strong signal that overwhelms the weaker, wanted signal.
Harmonics – even multiples of the offending signal that coincide with the wanted signal.
Notes: Discuss briefly with the students these basic types of RFI, and how they might be able to distinguish between them. At the same time, discuss some techniques they might use to mitigate the effects of the interference.
Direct detection usually affects consumer electronic devices (telephones and audio equipment). Can be mitigated by proper manufacture, installation, shielding, filters, ferrite bead chokes, etc. Actually very hard to deal with and generally not the fault of the ham radio operator, but try to convince your neighbor of that who just spent hundreds of dollars on their new equipment.
Overload – generally is a problem in fringe reception areas of TV signals. Not as much a problem now days with satellite and cable TV. Usually the problem can be mitigated by reducing transmitter power or filtering.
Harmonics – generally are a symptom of poor transmitter design or operation.

## Slide 45
RFI Mitigation
Filters attenuate (reduce) interfering signals – but do not totally eliminate them.
  High-pass – generally on the receive side to eliminate overload.
  Low-pass – generally on the transmit side to eliminate harmonics.
  Band-pass – used within most radio equipment.
  Band Reject – Could be used to prevent a 2-Meter transmitter from interfering with a television
Notes: Emphasize that filters can only attenuate the offending signal, they can not eliminate the signals. Discuss briefly the different kinds of filters and how they might be used. Have a high pass filter on hand that might be inserted into the feed line of a TV set to mitigate interfering signals and discuss how it might be installed.

## Slide 46
Cable TV Interference
Usually the result of broken shielding somewhere in the cable.
  Loose connections.
  Broken connections.
  Corroded connections.
Usually solved by proper cable maintenance by cable supplier.
  If the subscriber is a legitimate subscriber.

## Slide 47
Noise Sources
Electrical arcs (motors, thermostats, electric fences, neon signs).
Power lines.
Motor vehicle ignitions or alternators.
Switching power supplies.
Computers, networks, and TV sets.
Notes: Discuss with the students other sources of interfering noise and give them techniques on how to seek out the source of the noise. In many cases of the fixed noise, simply turning off the potentially offending appliance will help identify the source. Power line noise mitigation is the responsibility of the power company. Motor vehicle noise is generally short lived unless it is coming from the hams vehicle. Grounding and filtering in many of these cases will mitigate the noise.

## Slide 48
Dealing with RFI
Make sure you operate your equipment properly.
Eliminate interference in your own home first.

## Slide 49
Dealing with RFI
Take interference complaints seriously.
Make sure that you’re really not the cause (demonstrate that you don’t interfere within your own home).
Offer to help eliminate the RFI, even if you are not at fault.
Consult ARRL RFI Resources for help and assistance.

## Slide 50
What the Rules Say
RFI from and to unlicensed devices is the responsibility of the users of such devices
Bottom line – If your station is operating properly, you are protected against interference complaints
BUT – Be a good neighbor because they may (probably) not be familiar with Part 15 rules and regulations
Notes: Discuss with the students that though the law is probably on their side, their neighbors will not understand that and they will hold the ham responsible for the interference. It takes diplomacy to deal with RFI complaints!!!!!

## Slide 51: RF Grounding
The safety ground in house wiring is a poor RF ground
  The long run of wire has high RF impedance.
Use a short (if possible) run of flat Strap or copper braid to a dedicated ground rod or rods.
Tie all equipment to common ground bus
RF feedback in your transmitter can cause garbled transmission.

## Slide 52: Quiz Time
Chapter 5.4 & 5.5

## Slide 53: Chapter 5.4 &5.5 Key
Chapter 5.4
T4A04 A B C D
T4A05 A B C D
T4A09 A B C D
T7B02 A B C D
T7B03 A B C D
T7B04 A B C D
T7B05 A B C D
T7B06 A B C D
T7B07 A B C D
T7B08 A B C D
Chapter 5.5
T4A08 A B C D
T7B11 A B C D