## Slide 1: Technician License Course Chapter 8 Operating Regulations: Control Operators; Station Identification; Third-Party Communications Interference; Remote & Automatic Operation; Prohibited Transmissions

## Slide 2
Control Operator
An Amateur Station must have a control operator only when the station is transmitting.
Must have a valid Amateur Radio License that appears in the FCC database, or an alien authorized for reciprocal operation.
Station must operate within the authorization of the control operator’s license.
Control operator must be present at the control point of the station (the on-off switch) or remotely connected by a control link.
Notes: The control operator must have a license. This does not mean the highest class license of the group. For kids, if they are licensed and their parents are not, the kids are the control operators not their parents.
If an Extra Class and a Tech Class ham are operating a station and the Tech is the control operator, then the station is restricted to Tech privileges. If the hams want to use the Extra privileges, than the Extra Class ham is the control operator. The control operator doesn’t necessarily mean that they are the owners of the station.
The control operator must be in a position to stop improper operation of the station. In other words, they must be in a position to turn the transmitter off to prevent improper transmissions…this is the on-off switch in its simplest terms. The control operator of a repeater must be able to turn off the repeater if there are improper transmissions being made, this is usually done by remote control.

## Slide 3
More Important Information
Control operator responsibilities.
  The FCC’s primary concern is that transmissions are made only under the control of a licensed operator.
Control operator – the licensed amateur responsible for making sure transmissions comply with FCC rules.
Control operator designated by the station licensee
If the control operator is not the station licensee the responsibility for proper operation is shared.
The FCC assumes that the station licensee is the control operator unless there is documentation to the contrary.

## Slide 4
Station Identification (ID)
Normal ID.
  Say your call sign every ten minutes during and at the end of the contact (QSO).
Use of Tactical Call Signs.
  Does not substitute for proper station ID.
Ham Guests.
For FCC licensed Stations operating Phone Identification must be in English. (may be in CW)
You may Append a self assigned indicator
  For example K6PJ/K7 or K6PJ/mobile
  Must not conflict with any FCC assigned indicator or ITU Prefix assigned to another country
Notes: You are only required to say your call sign at 10 minute intervals and at the very end of a contact. Give some examples of proper identification. Also mention that regardless of the language being used for the contact, the station identification must be made in English. It is good practice to say both call signs so that others know who is on the air…maybe they will want to join in the conversation.
During EMCOMM and public service operations it is often very convenient to expedite communications that Tactical Call Signs are used. Go over the concept of Tactical Call Signs and how they might be used. Also stress that the 10 minute ID rule still applies and give an example of how to properly use the Tactical and personal call signs to satisfy this requirement.
Finally go over a situation where a guest operator who has a higher class license than the owner of the station, and the guest wants to use their high class privileges on the station using the lower class call sign. They would append their call with the station owners call.

## Slide 5
ID Rules Apply
Repeaters must also ID using the same 10 minute rule.
  Can be voice or CW (at 20 WPM or less).
Satellites and ISS have special rules.
Space Station – located more than 50 km above the earths surface
Special event calls.
  Normal club call or control operator call given once per hour.
Notes: There are many special circumstances. The important thing here is for the students to recognize that the rules are not always hard and fast and that there are exceptions that need to be understood if they will be involved in these kinds of operations.

## Slide 6
Third-Party Communications
Third-party means that a non-ham is involved in communication via ham radio.
  Could be actually speaking on the air.
  Could be passing a message on behalf of the non-ham.
Two situations – different rules.
  Within the US.
  Communication that crosses international borders.
Notes: Define third-party communications and give some examples.

## Slide 7
Third-Party within US
No special rules.
Just make sure the message is non-commercial in nature.

## Slide 8
Third-Party Across Borders
Make sure that third-party agreement exists.
  Check for current third-party agreements from ARRL Web site or FCC sources if in doubt.
  You might be surprised at the countries that we do not have third-party agreements with.
During station identification say both stations’ call signs.
Notes: Point out the table in the text that lists the countries we have third-party agreements with.

## Slide 9
Interference
QRN
  Natural interference (thunderstorms).
  Man-made (appliances and power lines).
QRM
  Interference from nearby signals.
  Other hams or other users of the frequencies.
Operators should avoid interfering with other users of the frequencies.
Notes: Review these “Q” signals.

## Slide 10
Interference
Harmful
  Interference that is disruptive but not intentional.
  Deal with it as best you can and help others avoid harmful interference.
Willful
  Intentionally causing interference.
  This becomes a legal and law enforcement issue.
  This is rare and there are procedures to deal with this (ARRL Official Observers can help).
Notes: Give the students some techniques on how to identify the type of interference and how to deal with it. Most of the interference will be unintentional. Everyone makes a mistake and in fact most hams will cause unintentional interference at some time during their operating careers. This type of interference should be discussed with some consideration because the student may be on the receiving end of a complaint themselves sometime.
Willful interference is another matter. Give the students some strategies on how to deal with this kind of interference. Basically document the interference and give the information to their local Official Observer. Also avoid giving the perpetrator an audience. In most cases the person doing the interfering will give up and go somewhere else if they do not get the response and attention they are looking for.
In all cases, if the students receive and interference complaint, they need to take that complaint seriously and deal with it as best they can.

## Slide 11
Preventing Interference
Use common sense and courtesy.
Keep equipment in proper operating order.
No one owns a frequency; be a good neighbor and share.
Yield to special operations and special circumstances.
Notes: It is hard to teach common sense, but try to give the students some sense of how they can avoid interference problems and how they can mitigate interference should it occur (and it will). It is important to stress that getting into an on-the-air argument about interference is counterproductive and should be avoided.

## Slide 12
Remote and Automatic Control
Some stations, repeaters and beacons operate without the control operator physically present at the control point.
If a repeater retransmits communications that violate the FCC rules the originating station is responsible
These stations must still comply with control operator stipulations.
  Local.
  Remote.
  Automatic.
Notes: Simply stress that regardless of the technical situation, the control operator must still be able to turn off the station to prevent improper transmissions. Remote control means that there is some sort of control link that allows the control operator to take action. These links can be independent radio links, telephone or Internet lines. Automatic controls are usually computers that have safeguards programmed into the controller to prevent improper operation. You could mention the time-out timer on a repeater as an example.

## Slide 13
Prohibited Transmissions
Unidentified transmissions .
  (not giving your call sign)
False or deceptive signals.
  (using someone else’s call sign)
False distress or emergency signals.
  (fake calls for help)
Obscene or indecent speech.
  (up to interpretation)
Music.
Notes: Most of these prohibited transmissions should be easy to identify. Obscene or indecent language is up to some interpretation. Give the students some examples of things to avoid discussing on the radio.

## Slide 14
No Business Communications
You cannot make a profit through the use of transmissions made via ham radio.
Advertising ham radio gear is okay as long as it’s not your regular business
Exception: teachers may use ham radio in their classrooms.
Notes: This is also another area where it can get a little gray. Give some examples of acceptable and unacceptable business related communications. It boils down to if the operator is going to profit in some way by the transmission, then they should not do it. If in doubt, don’t use ham radio for the transmission.
This can really get sticky in the scenario of professionals using ham radio during an emergency situation.

## Slide 15
No Encrypted Transmissions
Encryption involves encoding information for transmission that must be decoded upon reception to interpret the information.
This is okay if:
  Coding is open source.
  Intention is not to hide the message or deceive.
Notes: Most students will not get involved in this situation. They should not try to hide or deceive anyone listening in on the transmission through the use of codes. The use of codes does not necessarily have to be technical in nature.

## Slide 16
No Broadcasting
Broadcasting is sending one-way transmissions with no expectation of getting a response.
  News
  Music
Exceptions:
  Code practice.
  Ham radio related bulletins.
  Re-transmission of shuttle communications.

## Slide 17
Special Circumstances
Ham communication is generally intended for hams.
Emergencies and critical situations create special circumstances.
Special commemorative events may qualify as special circumstances.
  Armed Forces Day Communication Test
Normal rules return when the situation returns to normal.
Notes: Though ham communication is generally intended for hams, there are special circumstances where the rules are set aside to support the community at large during the emergency or critical situation. Give the students some specific examples that they might come across in their communities or regions.

## Slide 18: Quiz Time
Chapter 8

## Slide 19: Chapter 8 key
Section 8.1
T1E01 A B C D
T1E02 A B C D
T1E03 A B C D
T1E04 A B C D
T1E05 A B C D
T1E07 A B C D
T1E11 A B C D
T1F08 A B C D
Section 8.2
T1A05 A B C D
T1D11 A B C D
T1F01 A B C D
T1F02 A B C D
T1F03 A B C D
T1F04 A B C D
T1F05 A B C D
T1F06 A B C D
T1F07 A B C D
T2A06 A B C D
T2A07 A B C D
T2B09 A B C D

## Slide 20: Chapter 8 key
Section 8.3
T1A04 A B C D
T2B07 A B C D
T2B08 A B C D
Section 8.4
T1F11 A B C D
Section 8.5
T1E06 A B C D
T1E08 A B C D
T1E09 A B C D
T1E10 A B C D
T1F10 A B C D
Section 8.6
T1D02 A B C D
T1D03 A B C D
T1D04 A B C D
T1D05 A B C D
T1D06 A B C D
T1D07 A B C D
T1D08 A B C D
T1D09 A B C D
T1D10 A B C D