## Slide 1
Technician License Course Chapter 3 Electricity Components & Circuits

## Slide 2
Fundamentals of Electricity
When dealing with electricity, what we are referring to is the flow of electrons through a conductor.
  Electrons are negatively charged atomic particles.
    The opposite charge is the positive charge
  A conductor is a material that allows electrons to move with relative freedom within the material.
    Copper, Aluminum, Silver
  An insulator is a material does not allow electrons to move easily.
    Glass, wood rubber
Notes: You need to take some time to make sure all the students are on the same page when dealing with electronics fundamentals. You will probably find a wide range of knowledge from those who have no clue what you’re talking about to those who know far more about the topic than you do. Acknowledge this right up front, but tell the students you are going to lay the vocabulary foundation for material that follows. For those with little knowledge, tell them to hang on because it will become clear as the lesson proceeds. For those more knowledgeable, tell them to be patient and allow for a little instructor license to over simplify so that all can understand.

## Slide 3
Fundamentals of Electricity
In electronics and radio, we control the flow of electrons to make things happen.
You need to have a basic understanding of how and why we control the flow of electrons so that you can better operate your radio.
Notes: Use this time to provide some motivation of “why do I need to know this stuff.”

## Slide 4
Basic Characteristics of Electricity
There are three characteristics of electricity:
  Voltage, AKA EMF, E in formulas
    Measured in Volts (V)
  Current, I in formulas
    Measured in Amperes, Amps (A)
  Resistance, R in formulas
    Measured in Ohms (Ω)
All three must be present for electrons to flow.

## Slide 5
Basic Characteristics of Electricity
The flow of water through a hose is a good analogy to understand the three characteristics of electricity and how they are related.
Notes: Take some time to talk the students through the water analogy. Pressure that pushes water through a hose, in electricity it is voltage (or Electromotive force). The water in the hose, in electricity it is the electrons (current) that will move. The friction that prevents the water from just freely moving through the hose, in electricity it is resistance. Resistance comes from the electrons running into obstacles within the conductor (and other electrons) as they pass through. Have the students rub their hands together and observe what happens (heat). When resistance impedes the flow of electronics (slows the flow down), the change in kinetic energy (energy of movement) must be turned into some form of energy (remember energy is neither created or destroyed), it is just turned into something else) in this case heat.

## Slide 6
Characteristics of Electricity are
Inter-related
Voltage, current and resistance must be present to have current flow.
Just like water flowing through a hose, changes in voltage, current and resistance affect each other.
That effect is mathematically expressed in Ohm’s Law.
Notes: If there is no push (voltage) there is no current (current by definition is flowing electrons), if there is no movement, there can be no resistance.
If there is nothing to push, there will be no pressure, no movement - no resistance.
There is always going to be some form of impediment to movement.
What you are describing here is that inter-relationship which is Ohm’s law

## Slide 7
Ohm’s Law
E is voltage
  Units - volts
I is current
  Units - amperes
R is resistance
  Units - ohms
R = E/I
I = E/R
E = I x R
Notes: Go over the simple Ohm’s Law math and provide a few examples of how to solve problems. Give some homework problems that are the same as test questions (without telling them that they are test questions). Have the students solve these problems so they are confident that they can do the math.

## Slide 8: Meter Basics
Voltmeter (Measure Voltage or EMF)
  Connect in parallel with circuit where you wish to measure voltage
Ammeter (Measure Current or Amperage)
  Must be inserted in the circuit where the current is to be measured
Ohmmeter (Measure Resistance or Ohms)
  Circuit must be unpowered.
  Really an ammeter in series with a known voltage
Multimeter can do all of the above
  Can be damaged if not set correctly

## Slide 9
The Electric Circuit: An Electronic Roadmap
For current to flow, there must be a path from one side of the source of the current to the other side of the source – this path is called a circuit.
  There must be a hose (conductive path) through which the water (current) can flow.
The following are some vocabulary words that help describe an electronic circuit.
Notes: This would be a good time to illustrate a simple circuit diagram.

## Slide 10
Series Circuits
Series circuits provide one and only one path for current flow.
Notes: Trace the flow of current through the circuit and show there is only one way for current to flow.

## Slide 11
Parallel Circuits
Parallel circuits provide alternative paths for current flow.
Notes: Trace the current flow through the circuit and show that there are multiple paths for current flow.

## Slide 12
Moving Electrons Doing Something Useful
Any time energy is expended to do something, work is performed.
When moving electrons do some work, power is consumed.
Power is measured in the units of Watts (W).
Notes: Discuss the concept of power in electronics. Student will probably be familiar with this concept because of their electric bill.

## Slide 13
Power Formula
Power is defined as the amount of current that is being pushed through a conductor or device to do work.
  P = E x I
  E = P/I
  I = P/E
P
I
E
Notes: Go through some simple problems using the power formula. Again use test question examples for homework.

## Slide 14: Combining Ohms Law & Power
If you have Voltage & Resistance Use the Power formula and Ohms law
  P=E*I and I=E/R
  P =E2/R
If you have Current & Resistance
  P=E*I and E =I*R
  P= I2*R

## Slide 15
Two Basic Kinds of Current
When current flows in only one direction, it is called direct current (dc).
  Batteries are a common source of dc.
  Most electronic devices are powered by dc.
When current flows alternatively in one direction then in the opposite direction, it is called alternating current (ac).
  Frequency is how often it reverses direction / 2
  Your household current is ac.
    US 60Hz, Europe 50Hz
  RF is AC
Notes: Discuss the two different kinds of current and what they might be used for. Point out to the students that their household ac current is frequently converted into dc to run many household appliances. That conversion is done inside the appliance or inside an external converter like a wall transformer.
Explain why house current is ac (easier to transmit the electricity from the power plant to the home).

## Slide 16: Quiz Time
Chapter 3.1

## Slide 17: Chapter 3.1 Key - A
T3B02 A B C D
T5A01 A B C D
T5A02 A B C D
T5A03 A B C D
T5A04 A B C D
T5A05 A B C D
T5A07 A B C D
T5A08 A B C D
T5A09 A B C D
T5A10 A B C D
T5A11 A B C D
T5C08 A B C D
T5C09 A B C D
T5C10 A B C D
T5C11 A B C D
T5D01 A B C D
T5D02 A B C D
T5D03 A B C D
T5D04 A B C D
T5D05 A B C D

## Slide 18: Chapter 3.1 Key - B
T5D06 A B C D
T5D07 A B C D
T5D08 A B C D
T5D09 A B C D
T5D10 A B C D
T5D11 A B C D
T5D12 A B C D
T7D01 A B C D
T7D02 A B C D
T7D03 A B C D
T7D04 A B C D
T7D05 A B C D
T7D06 A B C D
T7D07 A B C D
T7D10 A B C D
T7D11 A B C D

## Slide 19
Electronics – Controlling the Flow of Current
To make an electronic device (like a radio) do something useful (like a receiver), we need to control and manipulate the flow of current.
There are a number of different electronic components that we use to do this.
Notes: You are now going to shift into some specifics of how electron flow is controlled. Don’t go into a lot of detail that will bury the students and overwhelm them with advanced information that will just scare them. But using their basic understanding of current flow, give them the basics of what the major component do. Have physical examples of the basic components on hand for show and tell.

## Slide 20
The Resistor
The function of the resistor is to restrict (limit) the flow of current through it.
  Resistance in Ohms
A variable resistor is usually called a potentiometer
  Often used as a volume control
Circuit Symbol
Notes: Describe what is inside the resistor.

## Slide 21
The Capacitor
The function of the capacitor is to temporarily store electric current.
  Like a very temporary storage battery.
  Stores energy in an electrostatic field.
  Capacitance in Farads
    Usually microfarads or picofarads
Circuit Symbol
Notes: Describe the internal architecture of the capacitor.

## Slide 22
The Inductor
The function of the inductor is to temporarily store electric current.
  Is basically a coil of wire.
  Stores energy in a magnetic field.
  Inductance in Henrys
    Usually millihenries or microhenries
Circuit Symbol

## Slide 23
Resonance
Because capacitors and inductors store energy in different ways, the stored energy can actually cancel each other under the right conditions.
  Capacitors – electric field
  Inductors – magnetic field
Cancelled current = no reactance, just leaving resistance.

## Slide 24
Resonant Antenna
If an antenna is designed correctly, the capacitive reactance cancels the inductive reactance.
Theoretically, the resulting reactance is zero.
  Leaving only resistance – meaning minimum impediment to the radio frequency currents flowing in the antenna and sending the radio wave into space.
Notes: Talk here about the design of the basic dipole antenna. Use the wavelength formula to calculate the length of a ¼ wave vertical for two meters and then compare that calculation to a commercially produced antenna.

## Slide 25
Antennas are Part Capacitor – Part Inductor – Part Resistor
Antennas actually have characteristics of capacitor, inductor and resistor electronic components.
Capacitors and inductors, because they store energy in fields, react differently to ac than dc.
  Special kind of resistance to the flow of ac – called reactance.
Notes: This is going to be a big jump for some students. The concepts of reactance and resonance is difficult for even the most experienced hams let alone the new ham. If your students appear to be struggling during the discussion, point out that your main goal is for them to have just a fundamental understanding of the concepts and the vocabulary involved here.

## Slide 26: The Diode
PN junction allows current to flow in one direction
  Cathode (P-type) often marked with stripe
  Anode (N-type)
  Current flows easily from cathode to anode
Symbol
Zener Diode
Light Emitting Diode (LED)

## Slide 27
The Bipolar Transistor (BJT)
The function of the transistor is to variably control the flow of current.
Three layers NPN, PNP
  Much like an electronically controlled valve.
  An analogy, the faucet in your sink.
  C - Collector
  B – Base
  E- Emitter
Circuit Symbol
C
E
B
B
C
E
Notes: The water faucet analogy is a good one to explain the function of a transistor.

## Slide 28: Field Effect Transistor (FET)
Gate Voltage controls Drain to Source Current
  G – Gate
  D – Drain
  S – Source
Gain measures the ability to amplify a signal
P Channel FET
N Channel FET
MOSFET
D
S
G
D
S
G
D
S
G

## Slide 29
The Integrated Circuit
The integrated circuit is a collection of components contained in one device that accomplishes a specific task.
  Acts like a “black-box”
Circuit Symbol
Notes: Give some examples of the specific kind of task that might be performed by an IC.

## Slide 30
Protective Components – Intentional Open Circuits
Fuses and circuit breakers are designed to interrupt the flow of current if the current becomes uncontrolled.
  Fuses blow – one time protection.
  Circuit breakers trip – can be reset and reused.
Circuit Symbol
Notes: Spend some time on the safety aspects of dealing with fuses and circuit breakers.

## Slide 31: Switches & Relays
Switch manually operated
Relay - A switch controlled by an Electromagnet
Single Pole Single Throw
Single Pole Double Throw
Double Pole Double Throw

## Slide 32
Other Circuit Symbols

## Slide 33
Putting It All Together in a Circuit Diagram or Schematic
Notes: Have other examples of circuit diagrams to share with the students, ask them to point out some of the components that they have learned. It is also a good idea to have a simple circuit board with the associated circuit diagram so that students can see a practical application and the connection between the circuit diagram and an operative circuit. A code practice oscillator would be a good example -- simple but does something.

## Slide 34: Quiz Time
Chapter 3.2

## Slide 35: Chapter 3.2 Key A
T5C01 A B C D
T5C02 A B C D
T5C03 A B C D
T5C04 A B C D
T6A01 A B C D
T6A02 A B C D
T6A03 A B C D
T6A04 A B C D
T6A05 A B C D
T6A06 A B C D
T6A07 A B C D
T6A08 A B C D
T6A09 A B C D
T5C01 A B C D
T5C02 A B C D
T5C03 A B C D
T5C04 A B C D
T6A01 A B C D
T6A02 A B C D
T6A03 A B C D
T6A04 A B C D
T6A05 A B C D
T6A06 A B C D
T6A07 A B C D
T6A08 A B C D
T6A09 A B C D

## Slide 36: Chapter 3.2 Key B
T6C01 A B C D
T6C02 A B C D
T6C03 A B C D
T6C04 A B C D
T6C05 A B C D
T6C06 A B C D
T6C07 A B C D
T6C08 A B C D
T6C09 A B C D
T6C10 A B C D
T6C11 A B C D
T6C12 A B C D
T6C13 A B C D
T6D01 A B C D
T6D02 A B C D
T6D03 A B C D
T6D04 A B C D
T6D06 A B C D
T6D07 A B C D
T6D08 A B C D
T6D09 A B C D
T6D10 A B C D
T0A04 A B C D
T0A05 A B C D

## Slide 37
The Basic Radio Station

## Slide 38
Basic Station Organization
Station Equipment
  Receiver
  Transmitter
  Antenna
  Power Supply
Accessory Station Equipment
Repeaters
Notes: Go over with the students the basic outline of the material to be presented during this lesson. This lesson is deceptively simple because there is a lot of preparation required to make this lesson effective. You should try to set up an operative station to give some demonstration contact. Use some care that you don’t set up a station that will intimidate the students on the first day, try to set up a station that would be typical of the type of station that they might set up in the beginning of their ham radio careers. Don’t spend a lot of time at this point demonstrating all the exotic modes available to the students, there will be plenty of time to do that later in the course. I would suggest a basic two meter set up and give demonstration contacts on repeaters and simplex. Then have a simple HF station and make one or two phone and one CW contact. Some advice on contact…don’t depend on a CQ being answered, it may or may not happen. I would suggest you have a few “planted” contacts from your club. These planted contacts are standing by on the frequency ready to step in and make a contact just in case your CQ goes unanswered. Try to get planted contact operators who are good at drawing out conversations on the radio. New operators are intimidated by radio and sometimes need to be prodded to say more than yes or no answers to questions.

## Slide 39
Transmit/Receive (TR) Switch
If the station antenna is shared between the transmitter and receiver, the TR switch allows the antenna to be switched to the transmitter when sending and to the receiver when receiving.
  In a transceiver, this TR switch is inside the unit and requires no attention by the operator.

## Slide 40
What Happens During Radio Communication?
Transmitting (sending a signal):
  Information (voice, data, video, commands, etc.) is converted to electronic form.
  The information in electronic form is attached or embedded on a radio wave (a carrier).
  The radio wave is sent out from the station antenna into space.

## Slide 41
What Happens During Radio Communication?
Receiving end:
  The radio wave (carrier) with the information is intercepted by the receiving station antenna.
  The receiver extracts the information from the carrier wave.
  The information is then presented to the user in a format that can be understood (sound, picture, words on a computer screen, response to a command).

## Slide 42
What Happens During Radio Communication?
This sounds pretty simple, but it in reality is pretty complex.
This complexity is one thing that makes ham radio fun…learning all about how radios work.
Don’t be intimidated. You will be required to only know the basics, but you can learn as much about the “art and science” of radio as you want.

## Slide 43
Simple CW Transmitter Block Diagram

## Slide 44: The Superheterodyne Receiver Block Diagram

## Slide 45: Filters

## Slide 46: Types of Circuits
Modulator – combines information with a carrier
Demodulator – Extracts information from a modulated carrier
  Product Detector for SSB or CW
  Discriminator for FM

## Slide 47: FM Superheterodyne

## Slide 48: Receiver Performance
Sensitivity (microvolts)
  The strength of the weakest signal that can be detected.
  Can be improved by connecting an RF preamplifier between the receiver and antenna.
Selectivity (Hertz)
  The ability to separate signals on near by frequencies

## Slide 49: Transverter
Transmit / Receive Converter
A device that changes the transmit out and receive in of a transceiver from one band to another
For Example if you have 10 meter (28 MHz) transceiver you could use a transverter to operate on 222 MHz

## Slide 50: Quiz Time
Chapter 3.3

## Slide 51: Chapter 3.3 Key
T7A01 A B C D
T7A02 A B C D
T7A03 A B C D
T7A04 A B C D
T7A05 A B C D
T7A06 A B C D
T7A08 A B C D
T7A11 A B C D
T7A12 A B C D
T7A13 A B C D