## Slide 1
Technician License Course Chapter 6 Communicating with other hams

## Slide 2
The Typical Telephone Conversation
Greeting.
Identify who is participating.
Exchange information, generally taking turns.
Salutations.
End the conversation.
Notes: Communication is something that we do every day, but rarely to we think about communication in detail. Simply go through a short telephone conversation that the students might have and point out the parts.
Greeting: Hello
Identify: Mom? This is Ron.
Exchange information: I am having a really great time on my vacation….we have done….
Salutations: Well I better get going, I’ll call you tomorrow.
End the conversation: Bye

## Slide 3
The Typical Ham Contact (QSO)
Greeting.
Identify who is participating.
Exchange information, generally taking turns.
Salutations.
End the conversation.
Notes: Take a moment to mention “Q” signals and what QSO means.
Now go over a fictitious ham contact and point out that it is the same as a telephone conversation except that there are a few procedural differences and some special vocabulary.
Greeting: CQ CQ CQ this is WA8SME.
Identify who is participating: WA8SME this is W6WBT Phil in Coleville calling.
Exchange information: Hi Phil, you have a good signal today from Coleville, you’re running 59 here in Bridgeport….
Salutations: Well Phil, I better get to some chores before it rains. Thanks for the contact and I hope to hear you again. 73 for now.
End the conversation: W6WBT this is WA8SME, clear.

## Slide 4
Radio Manners
Speak clearly and distinctly
Giant party line – choose topics accordingly
Shared use of frequencies
Use of phonetics.
Station identification (FCC 10 minute rule)
Schedules with other stations
Notes: Just like using the phone, when you talk on the radio you are communicating only with verbal information, there is no non-verbal feedback or communication. (The majority of communication while face-to-face is in non-verbal form) Therefore you need to make sure you choose your words wisely and speak clearly (you won’t see the raised eyebrows that indicate that you are not being understood). Additionally there will be static and interfering signals that will possibly corrupt the information, and also language barriers and accents.
There could be hundreds of people listening in, and the person you are talking to could be in another country with different values, therefore, choose your conversation topics wisely. Avoid controversial and or offensive topics. Avoid talking about religion, politics, off color content, dirty jokes and swearing. Some is just not acceptable, others are flat illegal.
You will share the frequencies with other hams, and because of propagation, you may not hear both sides of a conversation going on. It is a good habit to get into to ask if the frequency is in use before you use it. Simply say, “Is this frequency in use?” and wait for a reply. If not reply then go ahead.

## Slide 5: Phonetics
Use the ITU Phonetics Alphabet (page 6-2)
It is slightly different that that used by US Military
My Call – Kilo Six Papa Juliet

## Slide 6
Radio Manners
Signal Reports
Location
Name
Power level
Antenna
RST
  Readability (1-5)
  Strength (1-9)
  Tone (CW only 1-9)
  “Your signal is 58”
Notes: Go over the meaning of RST. Talk with your students about adjusting the content and pace of the QSO according to the RST. If signals are strong and perfectly readable, “arm chair copy”, then carry on at a normal pace. If signals a weak and barely readable, give lost of repeats of important information, keep transmissions short and the content light. If the other station can’t hear you well, then there is no need to talk about the meaning of life.
Give the location of your station is one of the fundamental components of a QSO. Your location is usually referred to as your QTH. You can give your QTH as city and state, simply your state, major geographic landmarks and street intersections, or by grid square…depending of the context of the conversation.

## Slide 7: Some Terms
CQ – General call looking for contact. Could be modified to say what kind of contact
  CQ DX - looking outside of own country
  CQ Europe – looking for contact in Europe
  CQ Contest – looking for contest contact.
73 – Best wishes
Grid Locator (aka Maiden head square)
  1° latitude x 2° Longitude; Bozeman DN45
Clear – I am done with the frequency

## Slide 8: Q Signals
Can be a statement or a question.
QRM – Interferance
QSY – Change Frequency
  QRN – Noise
  QSO – Contact
  QSL – Confirmation
  QTH – Location
  QRT –Stop Sending

## Slide 9
Radio Manners
Ham radio is self-regulated.
  ARRL Official Observers.
Logging contacts – on paper or computer
QSLs
  Awards Programs
Notes: Spend some time discussing with the students about how hams deal with unacceptable on-the-air behavior. Stress the importance of not confronting the violation on-the-air. One of the best strategies is to note the violation, but do not indicate to the offender that their behavior is being noticed…that gives them the audience that they are seeking and actually reinforces the bad behavior. Discuss the role of the OO program.
Though logging is no longer required, it is a good idea to keep records of your on-the-air activity even if just as an archive of those you have talked to or perhaps as a record of when your station was in use in case of an interference concern. Logging is a good habit. During contests logs are generally required to compete.
QSLs- the final courtesy. Bring in some QSL cards and show them to the class. Also bring in some of the operating awards that you have and explain some of the award programs.

## Slide 10
Band Plans
A band plan is a way of organizing the use of radio frequencies.
  Formal and legal plan.
  Informal – gentleman's agreement.
HF Band Plans are fairly simple
VHF/UHF plans are more complex to cover repeaters satellites and other uses
Notes: Discuss with the students the need for band plans, to bring organization and prevent potential chaos, but also a band plan allows us to find other hams to contact.
Pass out the band plan chart and explain how to extract information from the chart.
There are actually two kinds of band plans.
The formal or legal plan is the regulated authorization and regulated use of specific frequency ranges (bands) for licensed use. These plans are established by governmental regulatory agencies (like the FCC). Violating the formal band plan could result in legal sanctions. Give examples of the legal band plan.
The informal band plan is an organization of operating activities based on accepted practice. These plans are not legally binding but good operator practice and radio manners encourage hams to follow the informal band plans. These informal band plans are established by precedence and accepted practice and also by major organizations like the ARRL. Informal band plans are voluntary, but the FCC expects that good amateur practice means we follow those band plans.

## Slide 11: Band Plan Terms
Weak Signal – for CW SSB long range digital modes to separate it from FM & Repeaters
Satellite Uplinks & downlinks
Simplex - Talking and listening on the same frequency
Simplex Calling Frequency for initiating contact
Repeater inputs & outputs

## Slide 12
Making Contacts
On repeaters: Simply say your call to establish contact
On HF, call CQ – I am calling any station or answer a CQ Give the other stations call then your call.
Practice using your radio
Off frequency, low batteries or a bad location can cause problems
Notes: This is a good time to discuss some of the dos and don’ts of operating a radio. Set up situations that the students could find themselves facing and discuss proper operating techniques for those situations. Mention some specifics such as pausing between transmissions on a repeater to allow for a breaking station, saying your call sign every ten minutes minimum, use standard phonetics to help facilitate communication during poor signal conditions, local repeater accepted practices, the difference between starting a contact using CQ or monitoring, etc.
If the local repeater has a autopatch, go over how to access it and what are the accepted uses of the autopatch.

## Slide 13
Making Contacts
Taking turns and breaking-in.
Nets – groups of operators gathered on a specific frequency for a common interest or purpose.
Using simplex
Calling Frequencies
  SSB 50.125, 144.200, 432.100 MHz
  FM simplex 52.525, 146.52, 446.0 MHz
Notes: This is a good time to discuss some of the do’s and don’ts of operating a radio. Set up situations that the students could find themselves facing and discuss proper operating techniques for those situations. Mention some specifics such as pausing between transmissions on a repeater to allow for a breaking station, saying your call sign every ten minutes minimum, use standard phonetics to help facilitate communication during poor signal conditions, local repeater accepted practices, the difference between starting a contact using CQ or monitoring, etc.
If the local repeater has a autopatch, go over how to access it and what are the accepted uses of the autopatch.

## Slide 14
What is a Repeater?
Specialized transmitter/receiver interconnected by computer controller.
Generally located at a high place.
Receives your signal and simultaneously retransmits your signal on a different frequency.
Dramatically extends line-of-sight range.
  If both users can see the repeater site.

## Slide 16
A Little Vocabulary First
Simplex
  Transmitting and receiving on the same frequency.
  Each user takes turns to transmit.
  Is the preferred method if it works.

## Slide 17
A Little Vocabulary First
Duplex
  Transmitting on one frequency while simultaneously listening on a different frequency.
  Repeaters use duplex.
  Output frequency – the frequency the repeater transmits on and you listen to.
  Input frequency – the frequency the repeater listens to and you transmit on.

## Slide 18
Things to Know to Use a Repeater
Output frequency.
Frequency split.
  and therefore the input frequency.
Repeater access tones (if any).
All information can be found in a repeater directory

## Slide 19
Repeater Output Frequency
Repeaters are frequently identified by their output frequency.
  “Meet you on the 443.50 machine.”
    Here the specific frequency is used.
  “Let’s go to 94.”
    Here an abbreviation for a standard repeater channel is used meaning 146.94 MHz.
  “How about the NARL repeater?”
    Here the repeater is referenced by the sponsoring club name.
Notes: Inform the students of various repeater directory source materials that are available either on-line or in hard copy form.

## Slide 20
Repeater Frequency Split
The split, shifts, or offset frequencies are standardized to help facilitate repeater use.
There are + and – shifts depending on the plan.
Different bands have different standardized amounts of shift.
Notes: The use of different terms for frequency offset might confuse students, let them know that all the terms refer to the same thing. Discuss with the students that most modern radios will automatically set the standardized offset frequency when programmed, that they must specifically program in a non-standard split for those repeaters requiring it. Finally, let them know that the offset plan is not law, just a plan that is used by convention. There are some repeaters that use non standardized splits in order to limit or control use.

## Slide 21
Repeater Access Tones
Sometimes multiple repeaters can be accessed at the same time unintentionally.
To preclude unintentional access, some repeaters require a special subaudible tone to be present before the repeater controller will recognize the signal as a valid signal and turn on the repeater.
These tones are called by various names (depending on equipment manufacturer).
  CTCSS (continuous tone coded squelch system)
  PL (a Motorola trade name for CTCSS)
  Privacy codes or tones
  DCS (digital coded squelch)
Notes: You will have to define what sub-audible means and give some examples of tone frequencies.

## Slide 22
Repeater Access Tones
Access tones are usually published along with repeater frequencies.
Could also be announced when the repeater identifies.
  “PL is 123.0”
Tones are generally programmed into the radio along with frequency and offset.

## Slide 23
Repeater Controller
Computer that controls the repeater operation.
  Station identification (Morse code or synthesized voice).
    Same ID requirements as you have.
  Time-out protection.
    Sometimes called the alligator.
    Protects against continuous transmission in the event of a stuck PTT or long winded hams.
  Courtesy tone – repeater time-out timer reset.
Some Repeaters use auxiliary stations to transmit signals from a remote receiver to the repeater for retransmission
Notes: Here you should cover some of the characteristics of the local repeaters that the students will encounter. Include in the discussion the different IDs used, what a courtesy tone is and what it means, the length of the time-out timers on some machines, and locally accepted uses of repeaters.

## Slide 24: Using a Repeater
To contact someone you heard on a repeater:
  Say his call then your call
To contact anyone on the repeater
  Just give your call
Keep your Transmissions short
  Allow a little time for stations to break in
  To break in give your call between transmissions

## Slide 25: Repeaters & The Internet
Some repeaters may be linked via the internet
Internet Radio Linking Project (IRLP)
  Uses VoIP technology to link repeaters
To use on a repeater so equipped:
  Use Keypad to turn on the IRLP connection
  Use Keypad to enter IRLP node of the remote repeater
  Once Connection is made operate like normal

## Slide 26: Quiz Time
Chapter 6.1 to 6.4

## Slide 27: Chapter 6 Key
Section 6.1
T2B10 A B C D
T2B11 A B C D
T8C05 A B C D
Section 6.2
T2B01 A B C D
Section 6.3
T2A02 A B C D
T2A04 A B C D
T2A05 A B C D
T2A08 A B C D
T2A09 A B C D
T2B10 A B C D
Section 6.4
T1A11 A B C D
T2A01 A B C D
T2A03 A B C D
T2B02 A B C D
T2B04 A B C D
T4B11 A B C D
T8C09 A B C D
T8C10 A B C D

## Slide 28
Nets
Net is short for “Network”
  Evolved over the years to share and exchange information in an organized and efficient way with accuracy
Social nets
Traffic nets
Emergency and public service nets.
Notes: Discuss with the students the purpose of nets and some of the nets that are in your area. Invite the students to listen to the nets during the course of the class.
Discuss here the purpose and theme of some of the social nets in your area.

## Slide 29
Traffic Nets
Traffic refers to formal messages that are relayed via ham radio
Formal structure to ensure accuracy – National Traffic System (NTS)
  Procedures
  Accountability
Notes: Give the students a copy of the radiogram form and go over the various sections of the form, but not in too much detail. The idea here is to give the students the sense that the NTS system and associate procedures are developed to ensure accuracy of the messages being handled within the system.

## Slide 30
Emergency and Public Service Nets
Public service nets – training for emergency nets
  Training for ham operators as well as emergency groups and managers supported by Amateur Radio
Emergency nets
Notes: Discuss some of the public service nets that are common in your area and how they are related to training for emergency communications while providing a valuable public service.
Discuss some of the emergency net operations that are involved in your area. More detail on emergency communications, of which emergency nets are a part, will be discussed a little later.

## Slide 31
Net Structure
Net Control Station (NCS)
  Traffic cop who controls the flow of information
Check-in and check-out procedures
Communications discipline vital
  Learn and follow procedures
  Speak only when directed, and only to whom directed
  Follow through with your commitments
If you have priority or emergency traffic get the attention of the NCS
  Say Priority or Emergency followed by your call
Notes: Discuss with the students the structure and general operating procedures of a net. Emphasize the need for communication discipline, particularly for traffic and emergency nets. (Social nets are a different matter) A little role playing may help to demonstrate the point. You might even consider using HTs on a simplex frequency to demonstrate net check-in/check-out procedures and even run through a short script of passing some traffic during a simulated emergency net.

## Slide 33
Supporting Emergency Operations
One of the pivotal reasons for the existence of Amateur Radio.
You will be licensed communicators.
  Get involved and use what you have learned.
Know where you fit in the overall emergency management team.
Notes: Here is where you can bring some of your own reasons for participating in emergency communications activities. However, stress a realistic role that ham radio plays in emergency management, don’t give false impressions that ham radio is the sole and primary communications method used by emergency managers. Ham radio frequently is used as a back-up system that is employed when the primary systems fail. In reality, if ham radio is never used during an emergency, that is a good thing, because that means the primary systems worked as planned. One way to look at it is that ham radio provides some redundant capability that will allow emergency managers to deploy and employ their professional resources in a more effective manner than if the redundant communications reserves provided by ham radio were not available. In other words, perhaps emergency managers can stretch their professional communications resources a little thin to meet contingency demands because they know they have ham radio as a back-up.

## Slide 34
EMCOMM Organizations
Radio Amateur Civil Emergency Service (RACES).
  Supports civil emergencies.
  National in scope.
Amateur Radio Emergency Service (ARES).
  Local and regional in scope.
  Supports non-governmental agencies.
Notes: Discuss the two organizations and how they are similar and how they are dissimilar (this depends on your local organizations).

## Slide 35
EMCOMM Tips
Don’t become part of the problem.
You are a communicator, not a decision or policy maker.
Don’t give out unauthorized information.
Know your abilities and limitations-keep yourself safe.
Follow radio discipline and net procedures.
Protect personal information-ham radio communications is a ‘party line.”
FCC Rules still apply
Notes: Define the term EMCOMM – emergency communications.
Then discuss these practical tips.

## Slide 36
Emergency Declarations
FCC may declare a Temporary State of Communications Emergency.
  Includes details of conditions and rules to be followed.
  Specifics communicated through web sites and ARRL bulletins, the NTS, and on-the-air.
  Avoid operating on restricted frequencies unless engaged in relief efforts.
Notes: Discuss with the students how this works, hurricane relief operations are the most common communication emergency that they might encounter. Give them the frequencies used and encourage them to listen in on the relief efforts as a learning exercise.

## Slide 37: EMMCOM and your Employer
Beware: “No amateur shall transmit … communications in which the licensee or control operator has a pecuniary interest, including on behalf of an employer
Participating in Training organized by your employer can violate this.
  Exception: Employer is a government agency and a written wavier has been obtained from the FCC.

## Slide 38
Making and Answering Distress Calls
Rule number one – speak in plain language!
Mayday (voice); SOS (Morse code) are flags
Identify
Give location
State the situation
Describe assistance required
Provide other important information
Notes: Again, role playing will help to illustrate the major concepts in making and answering a distress call.

## Slide 39
Tactical Communications
Tactical Call Signs.
  Facilitate communications.
  Location or function specific.
  Transcends operator changes.
FCC ID rules still apply.
Notes: Because students will frequently hear tactical call signs being used, it is a good idea to discuss the proper use of tactical call signs and show them that they are (if used properly) are in compliance with FCC station ID rules and regulations. Role playing here is a good way to illustrate this point and an opportunity for you to model the correct way to use tactical call signs.

## Slide 40
Emergency Equipment
“Go-kits”
  Portable ham radio equipment.
  Emergency power sources.
  Personal survival supplies and equipment.
Notes: Some examples of “go-kits” will help students see what type of equipment is appropriate in your area. Don’t forget to discuss personal survival gear, emphasize that personal survival considerations is part of “Not becoming part of the problem” that was mentioned earlier.

## Slide 41
EMCOMM Training
If you are going to participate in EMCOMM, get training.
Actively participate in EMCOMM activities.
  Nets
  Public service activities
  Attend community meetings and get involved in your community.
Take EMCOMM courses.
  ARRL EMCOMM courses
  NIMS and FEMA courses

## Slide 42: Quiz Time
Chapter 6.5 & 6.6

## Slide 43: Chapter 6.7 Key
T1A06 A B C D
T1A07 A B C D
T1A09 A B C D
T8B01 A B C D
T8B02 A B C D
T8B03 A B C D
T8B04 A B C D
T8B05 A B C D
T8B06 A B C D
T8B07 A B C D
T8B08 A B C D
T8B09 A B C D
T8B10 A B C D
T8B11 A B C D
T8C01 A B C D
T8C02 A B C D
T8C03 A B C D
T8C04 A B C D
T8C07 A B C D
T8C08 A B C D
T8D04 A B C D

## Slide 44
Awards, DXing, Contests
On-air activities provide incentive to get on the radio
Learn about propagation as you search for specific stations on various bands
Improve operating skills
Fun!

## Slide 45
Awards
DXCC
  Contacting 100 different entities (countries)
WAS
  Contacting 50 states
VUCC
  Contacting 100 grid squares on VHF/UHF
Notes: Bring in your awards for show and tell. These are just a few of the major operating awards that are available. Discuss with the students that awards usually require QSL card confirmation of the contact. Also introduce the students to the Logbook of the World as an alternative to QSL cards. Bring in a stack of QSL cards to show the students. Hand out your own QSL card for the students to keep start their collection.
One post class activity that you can do related to QSLing is to make first contacts with the students after they get their licenses. Make it a big deal. Have the class reassemble as a group and pass around an HT for their first contacts. At the end of the class, present QSL cards and First Contact Certificates to each participant as a memento.

## Slide 46
DXing
  Contacting stations far away – a tradition since the first days of radio.
  On HF, usually means contacting stations in other countries
  On VHF/UHF, means contacting stations outside your normal coverage area
    AKA weak signal communications
    Need Multimode Transceiver
    Need Horizontal Antenna (Prefer high Gain)

## Slide 47
Contests
ARRL Sweepstakes
State QSO Parties
VHF/UHF contests
RTTY contests
CQ World Wide DX Contest
Contest calendars
Notes: The object of a radio contest is to contact as many different stations in a defined period of time, using specific frequencies and modes, and exchange some information. Standings are published for the major contests. Contests test operator radio operating skills as well as technical skills.
Point out that there are usually at least one contest opportunity each weekend and how to find out about upcoming contests. ARRL Web contest results would be helpful to illustrate the popularity of contesting in the hobby.

## Slide 48
Field Day
Emergency communications training with a competitive spirit
Set up portable station and antenna (in the field, mobile, anywhere!) and make as many contacts as possible
Get started with your local club or group – great way to get involved
Notes: Yes, Field Day is not technically a contest, but it is treated as such by most ham operators.

## Slide 49
Special Events
Special Event stations are set up to commemorate some significant local event.
Usually stations are demonstration stations set up for public display.
Commemorative certificates are awarded for contacting the stations.
Notes: Bring in some of the special event certificates that you have on hand for show and tell. Bring in the latest QST listing of special event stations to illustrate the variety of special event themes and the number of special events available each weekend.

## Slide 50
Radio Direction Finding
Useful for locating interference or noise sources
Works best with a directional antenna
“Fox hunting” competitions on FM offer a fun opportunity to learn how to do it
Good training for search and rescue

## Slide 51
Amateur Satellites
OSCAR
  Orbiting Satellites Carrying Amateur Radio.
Modes
  FM
  Analog (SSB and CW)
  Digital (FM packet)
You can use if you are licensed for Uplink
  Use Minimum power necessary
International Space Station.
Notes: Satellite operating might interest some hams of the hams. Briefly describe the station equipment required to effectively operate through a satellite and the type of satellite modes available. Discuss some of the technical challenges that have to be considered to operate satellites; finding and tracking the satellite, Doppler compensation, working with transponder equipment, etc.

## Slide 52
Satellite Terms
Uplink – Earth stations transmit to satellite
  Telecommand: One way transmission to initiate functions
Downlink – Satellite transmits to stations on Earth
  Telemetry: One way transmission of measurements
Beacon – signal from satellite with information about satellite operating conditions
Doppler shift – shift in frequency due to relative motion between satellite and Earth station
LEO – Low earth orbit

## Slide 53
Satellite Terms
Spin fading – caused by rotation of satellite
Pacsat – packet radio satellite
Tracking software – gives beam heading and times when satellite is in view
Mode – bands satellite is using for uplink and downlink (eg Mode U/V = 70 cm uplink, 2 meters downlink)

## Slide 54
Other Special Modes
Video
  Slow Scan TV (SSTV)
    Sending snap-shot pictures.
  Amateur TV (ATV)
    70 cm and higher
    Similar to analog commercial TV imagery.
    NTSC Analog fast scan TV

## Slide 55
Other Special Modes
Radio Control (RC).
  Telecommand.
  50 MHz band.
  1 watt maximum power
  Call and address attached to transmitter

## Slide 56: QuizTime
Chapter 6.7