## Slide 1
Technician License Course Chapter 4
Propagation and Antennas
Notes: Make sure you bring in lots of examples of antennas and different kinds of feed lines as examples are you are going through this lesson.

## Slide 2
Radio Wave Propagation: Getting from Point A to Point B
Radio waves propagate by many mechanisms.
  The science of wave propagation has many facets.
We will discuss three basic ways:
  Line of sight
  Ground wave
  Sky wave

## Slide 3
Line-of-Sight
If a source of radio energy can been seen by the receiver, then the radio energy will travel in a straight line from transmitter to receiver.
  There is some attenuation of the signal as the radio wave travels
This is the primary propagation mode for VHF and UHF signals.
Notes: Line-of-sight is probably the easiest propagation mode for students to understand. You can use a laser pointer to demonstrate line-of-sight. You will probably have to refresh the students memory on UHF and VHF definitions and their position on the RF spectrum. Also these bands will be the primary operating bands of the new hams.
The maximum distance for line-of-sight transmissions with two people standing on the surface of the earth is about (roughly) 25 miles, this is due to the curvature of the earth. You can extend this discussion by briefly brining up repeaters and how they extend the line-of-sight range.

## Slide 4
Ground Wave
Some radio frequency ranges (lower HF frequencies) will hug the earth’s surface as they travel
These waves will travel beyond the range of line-of-sight
A few hundred miles
Notes: Point out that this propagation mode is the one used by AM broadcast stations in the day light hours. You can connect with the students experiences with receiving AM broadcast stations using ground waves. What happens at night? Why do they change power levels depending on the time of day? How is the reception at night?

## Slide 5: Radio Wave Diffraction
Radio waves can be diffracted around a discontinuity like light.
  This can allow communication to a station that should be hidden

## Slide 6
VHF and UHF Propagation
VHF & UHF propagation is principally line of sight.
Range is slightly better than visual line of sight.
  because they are refracted along the curvature of the earth making the earth appear less curved to the radio waves.
UHF signals may work better inside buildings because of the shorter wavelength makes it easier for the signal to escape holes like windows
Buildings may block line of sight, but reflections may help get past obstructions.
Reflections from a transmitter that is moving cause multi-path which results in rapid fading of signal – known as picket fencing.
  This multipath can also make your signal much stronger or weaker b moving a few feet.
  Can cause high error rates on digital signals
Notes: Line-of-sight is probably the easiest propagation mode for students to understand. You can use a laser pointer to demonstrate line-of-sight. You will probably have to refresh the students memory on UHF and VHF definitions and their position on the RF spectrum. Also these bands will be the primary operating bands of the new hams.
The maximum distance for line-of-sight transmissions with two people standing on the surface of the earth is about (roughly) 25 miles, this is due to the curvature of the earth. You can extend this discussion by briefly brining up repeaters and how they extend the line-of-sight range.

## Slide 7
Sunspot Cycle
The level of ionization depends on the radiation intensity of the Sun.
Radiation from the Sun is connected to the number of sunspots on the Sun’s surface.
  High number of sunspots, high ionizing radiation emitted from the Sun.
Sunspot activity follows an 11-year cycle.
Notes: Here is a good place to discuss the sun spot cycle, some of the students might make the connection between this practical application of science and the study of the sun and to some things they have heard about sun spots on the evening news programs.

## Slide 8
Ionosphere
Radiation from the Sun momentarily will strip electrons away from the parent atom in the upper reaches of the atmosphere.
  Creates ions
The region where ionization occurs is called the ionosphere.
Notes: Discuss with the students what happens to ionize the upper reaches of the atmosphere. You may have to tap into some old science lessons and vocabulary that the students haven’t thought about in years. Define what an Ion is.
The concept of momentarily stripping away the electrons is important when you get into the details of the layers of the ionosphere and the time it takes for the ionosphere to dissipate during the evening and night time hours.
You can also refer back to the students experience with AM broadcasts and what they observe at night versus what they observe during the day time.

## Slide 9
The Ionosphere – An RF Mirror
The ionized layers of the atmosphere actually act as an RF mirror that reflect certain frequencies back to earth.
Sky-wave propagation is responsible for most long-range, over the horizon communication.
Reflection depends on frequency and angle of incidence.
  Night best for low frequencies (160m – 30m)
  Day best for high frequencies (20m – 10m)
Notes: If the angle is too steep, the waves go right through. If the frequencies are too low or too high, they also are not reflected, and in some cases are absorbed by the layer. Constant monitoring of the ionosphere indicates the maximum and minimum usable frequencies for sky-wave propagation. Hams interested in DX (you might have to explain DX) will adjust their operating bands to take advantage of those frequencies that are reflected off the ionosphere.

## Slide 10
Levels of the Ionosphere
Density of the atmosphere affects:
  The intensity of the radiation that can penetrate to that level.
  The amount of ionization that occurs.
  How quickly the electrons recombine with the nucleus.
F layer is primary means of long range communication ~2500 mile per hop
E layer (sporotic E) useful on VHF about 1200 miles /hop
  Mostly 10m, 6m, 2m
  Often very strong

## Slide 11: Special Propagation Modes
Auroral reflection
  Aim antenna at active aurora
  Reflected signals fluctuate rapidly andare often distorted
Tropospheric Scatter or Ducting
  Often associated with temperature inversion.
  VHF & UHF propagation to about 300 miles
Meteor Scatter
  Reflection off ionization trail of meteor
  Best on 6m useful on 2m & up to 70cm

## Slide 12: Quiz Time
Chapter 4.1

## Slide 13: Chapter 4.2 Key
T3A01 A B C D
T3A02 A B C D
T3A06 A B C D
T3A08 A B C D
T3A10 A B C D
T3A11 A B C D
T3C01 A B C D
T3C02 A B C D
T3C03 A B C D
T3C04 A B C D
T3C05 A B C D
T3C06 A B C D
T3C07 A B C D
T3C08 A B C D
T3C09 A B C D
T3C10 A B C D
T3C11 A B C D

## Slide 14
The Antenna System
Antenna: Facilitates the sending of your signal to some distant station.
  Back to the falling magnet
Feed line: Connects your station to the antenna.
Test and matching equipment: Allows you to monitor antenna performance.
Notes: The transmitter causes electrons to move in the antenna…creating the magnetic field, that changing magnetic field creates an electric field and away we go.

## Slide 15
The Antenna (Some Vocabulary)
Element: The conducting part or parts of an antenna designed to radiate or receive radio waves.
Driven element: The element supplied directly with power from the transmitter
Feed point: Where the transmitted energy enters the antenna.
Notes: The best way to cover this kind of material is to have a few antennas of various types and point out the different parts of the antenna relative to the vocabulary.

## Slide 16
The Antenna (Some Vocabulary)
Polarization: The direction of the electric field relative to the surface of the earth.
Same as the physical direction
    Vertical
    Horizontal
    Circular
Notes: The best way to cover this kind of material is to have a few antennas of various types and point out the different parts of the antenna relative to the vocabulary.

## Slide 17
The Antenna (Some Vocabulary)
Omni-directional – radiates in all directions.
Directional beam – focuses radiation in specific directions.
Gain – apparent increase in power in a particular direction because energy is focused in that direction.
  Measured in decibels (dB)
Notes: Again, manipulatives are the best way to help with this discussion.
The concept of gain is an important concept to make sure the students understand. Gain does not increase the amount of power being transmitted, gain gives the appearance of increased power because the transmitted energy (and received energy) is focused in a specific direction by the antenna elements at the expense of energy that would have been send in other directions. A good way to illustrate this is to blow up a balloon. The inflated balloon represents an omni-directional radiation pattern. Now squeeze the balloon in the middle to create a two lobes (if you do it right, you have one big and one little lobe). This represents the same amount of energy, but now it is focused in specific directions.
The concept of decibels is also a difficult and scary concept for the math phobic of the class. Don’t spend a lot of time on this, just get them used to the use of dB as a way of expressing the gain or apparent power advantage comparisons between one antenna and another. I guess the important specific gain value to remember is 3. For every 3 dB of gain, the apparent power advantage is doubled (5 watts seems like 10 with 3 dB of gain). You also could mention that -3 dB is halving the power…10 watts is like 5 watts when there is a -3 dB of gain (this is significant when students are looking at the performance of the rubber duck antenna versus a ¼ wave whip).

## Slide 18: Polarization Effects
For VHF & UHF signals on direct line of sight polarization must match or the signals will be much weaker.
  FM repeaters use vertical polarization because it is much easier to make vertical mobile antennas.
  Most weak signal work uses horizontal because the horizontal wave tends to travel a bit further over the horizon.
When reflected by the ionosphere the polarization of the wave is randomized.

## Slide 19: Decibels
dB = 10*log(ratio) for Power
  dB = 20*log (ratio) for voltage or current
10 dB is 10 tines the power
3dB is twice the power

## Slide 20
Antenna Radiation Patterns
Radiation patterns are a way of visualizing antenna performance.
The further the line is away from the center of the graph, the stronger the signal at that point.
Notes: This is an opportunity for you to expand on the concept of gain. Walk your students through how to interpret the antenna radio pattern plots. Here is a good time to introduce the concept of front-to-back ratio…another way to describe antenna performance.

## Slide 22
Antenna versus Feed Line
For efficient transfer of energy from the transmitter to the feed line and from the feed line to the antenna, the various impedances need to match.
When there is mismatch of impedances, things may still work, but not as effectively as they could.

## Slide 23
Feed Line types
The purpose of the feed line is to get energy from your station to the antenna.
Basic feed line types.
  Coaxial cable (coax).
  Open-wire or ladder line.
Each has a characteristic impedance, each has its unique application.
Notes: It would be very helpful to have physical examples of the two basic kinds of feed line.

## Slide 24
Coax
Most common feed line.
Easy to use.
Matches impedance of modern radio equipment (50 ohms).
Some loss of signal depending on coax quality (cost).
Notes: Discuss why coax is so common and emphasize how it can be abused and still work well.

## Slide 25
Coax Feed Lines
RG-174
  Small lossy use only for short runs
RG-58
  OK for HF low power(100w) to ~50 feet
RG-8 RG-213
  Good for HF to ~200ft & 1500W
Hardline
  Low loss good for VHF & UHF long Runs
Notes: Go over the different types and grades of coax; examples to show would be helpful. Talk with the students about relative losses and power handling capabilities of each type of coax along with the price.

## Slide 26
Coax Connectors
SO-239/PL-259
  AKA UHF
  Used for HF
N
  Matched Z
  Good for UHF
BNC
SMA

## Slide 27
Open-Wire/Ladder Line
Not common today except in special applications.
Difficult to use.
Need an antenna tuner to make impedance match – but this allows a lot of flexibility.
Theoretically has very low loss.
Notes: Discuss some applications where ladder line is the only way to go. Emphasize that the antenna tuner is required in most cases to transform the feed line impedance to 50 ohms to match the rig.

## Slide 28
Antenna Impedance
Antennas have a characteristic impedance.
Expressed in ohms – common value 50 ohms.
Depends on:
  Antenna design
  Height above the ground
  Distance from surrounding obstacles
  Frequency of operation
  A million other factors
Notes: Give other common values of antenna impedances. As a general rule, anything within 1 wavelength of the antenna will have an impact on the antenna impedance, antenna radiation pattern, and antenna performance.
The complexity of antennas makes a fascinating aspect of the hobby and also makes antenna design an art.

## Slide 29
Impedance – AC Resistance
A quick review of a previous concept: impedance.
  Antennas include characteristics of capacitors, inductors and resistors
The combined response of these component parts to alternating currents (radio waves) is called Impedance.
Notes: You will probably have to spend a little time to re-teach the concept of impedance. It was just touched on previously, now it is time to get a little more serious with the concept because of its importance in the discussion of feed lines and antenna matching.

## Slide 30
Standing Wave Ratio (SWR)
If the antenna and feed line impedances are not perfectly matched, some RF energy is not radiated into space and is returned (reflected) back to the source.
  Something has to happen to this reflected energy – generally converted into heat or unwanted radio energy (bad).

## Slide 31
The Dipole
Most basic antenna.
  Two conductive, equal length parts.
  Feed line connected in the middle.
Total length is ½ wavelength (½ l ).
Length (in feet) = 468 / Frequency (in MHz).

## Slide 32
The Dipole
Notes: Mention that there are variations of the dipole antenna (flat top, inverted V) and that there are advantages and disadvantages of each.

## Slide 33
The Ground-Plane
Simply a dipole that is oriented perpendicular to the Earth’s surface (vertical) .
One half of the dipole is replaced by the ground-plane.
  Earth
  Car roof or trunk lid or other metal surface.
  Radial wires.
Length (in feet) = 234 / Frequency (in MHz).
Notes: Mention here, or better yet have an example to show, that the ground-plane vertical antenna can have a magnetic mount for the car that precludes drilling holes in the car to mount the antenna.

## Slide 34
The Ground-Plane

## Slide 35
Loop Antennas – Variations
Quad
Delta
Horizontal
Notes: These loop antennas are all 1 wavelength in length, and can be horizontal or vertical polarization.

## Slide 36
Directional (Beam) Antennas
Beam antennas focus or direct RF energy in a desired direction.
  Gain
  An apparent increase in power in the desired direction (both transmit and receive).
Yagi (rod-like elements – TV antennas).
Quad (square shape, wire loop elements).
Notes: Go over the concept of gain again with the students and emphasize that there is no increase in power from the transmitter, only an apparent increase in power because the available power is focused or directed in the desired direction at the expense of that power that would have been transmitted in the un-desired directions.
Have on hand photos or examples of the two common beam antennas, Yagi and Quad to illustrate the point here.

## Slide 37
Directional (Beam) Antennas

## Slide 38
Directional (Beam) Antennas
All beam antennas have parts called elements.
  Driven element is connected to the radio by the feed line.
  Reflector element is on the back side.
  Director element is on the front side toward the desired direction.

## Slide 39
Feed Line Devices
Balun
Duplexer
Antenna switch
SWR meter
Antenna analyzer
Antenna tuner
Notes: Briefly discuss the purpose and application of each kind of feed line device that the students may encounter or read about in the literature. Again, physical examples of each device would be helpful during the presentation.
Emphasize that the SWR meter or antenna analyzer is probably one of the first pieces of test equipment they would want to add to their station.

## Slide 40
Nothing is Perfect
Although the goal is to get 100% of your radio energy radiated into space, that is virtually impossible.
What is an acceptable level of reflected power or SWR?
  1:1 SWR is perfect.
  2:1 SWR should be the max you should accept (as a general rule).
    Modern radios will start lowering transmitter output power automatically when SWR is above 2:1.
  3:1 is when you need to do something to reduce SWR.
Notes: You need to give your students the benefit of your experience on how to use the SWR meter, how you might make adjustments in the antennas to improve the SWR, and also give them some guideline as to what is acceptable and what is not. These are some of my guidelines for dealing with SWR, of course there are exceptions to every rule and there certainly are exceptions to these guidelines.

## Slide 41: Care of Feedlines
Water penetration causes coax to get lossy
  Seal Connectors against Moisture.
  Look for cracks in jacket
  Use UV resistant Coax
Air core coax is very low loss but easily contaminated by water.

## Slide 42: Soldering
Antenna construction is often the first Soldering done by hams.
Use ONLY Rosen core solder!
Use enough heat to get good flow of the solder
  The result should have bright shiny surface.
  A dull or grainy surface indicates a cold solder joint.

## Slide 43
Test and Matching Equipment
Proper impedance matching is important enough to deserve some simple test equipment as you develop your station repertoire.
Basic test equipment: SWR meter.
Matching equipment: Antenna tuner.

## Slide 44
Standing Wave Ratio (SWR)
If the antenna and feed line impedances are not perfectly matched, some RF energy is not radiated into space and is returned (reflected) back to the source.
  Something has to happen to this reflected energy – generally converted into heat or unwanted radio energy (bad).

## Slide 45
Antenna Tuner
One way to make antenna matching adjustments is to use an antenna tuner.
Antenna tuners are impedance transformers (they actually do not tune the antenna).
  When used appropriately they are effective.
  When used inappropriately all they do is make a bad antenna look good to the transmitter…the antenna is still bad.
Notes: Spend some time with the students clarifying what actually is happening when they use an antenna tuner. There are many misconceptions about antenna tuners. Basically, the antenna tuner is an impedance transformer that makes the impedance seen by the transmitter look like 50 ohms. An antenna tuner can make a bad antenna look like a good antenna, but the antenna is still bad. Antenna tuners are truly effective when you are truly compensating between impedance miss-matches (an effective antenna at one impedance that needs to transformed to the impedance of the transmitter).

## Slide 46
How to use an Antenna Tuner
Monitor the SWR meter.
Make adjustments on the tuner until the minimum SWR is achieved.
  The impedance of the antenna is transformed to more closely match the impedance of the transmitter.

## Slide 47
SWR Meter
The SWR meter is inserted in the feed line and indicates the mismatch that exists at that point.
You make adjustments to the antenna to minimize the reflected energy (minimum SWR).
Notes: Have an example of an SWR meter on hand to show the students. You can also discuss how SWR meters are now commonly included as a meter function of a transceiver.

## Slide 48
Antenna Supports
Trees.
Towers or masts.
Covenants and antenna restrictions must be considered.
Notes: Bring up any local antenna considerations for your area. Emphasize that you don’t need expensive towers and antennas in order to have fun with ham radio.

## Slide 49: Quiz Time
Chapter 4.2 & 4.3 & 4.4

## Slide 50: Chapter 4.2 Key
T3A04 A B C D
T3A07 A B C D
T3A09 A B C D
T3B03 A B C D
T5B09 A B C D
T5B10 A B C D
T5B11 A B C D
T5C07 A B C D
T9A02 A B C D
T9A11 A B C D

## Slide 51: Chapter 4.3 Key
T6D11 A B C D
T7C03 A B C D
T7C04 A B C D
T7C05 A B C D
T7C06 A B C D
T7C07 A B C D
T9B01 A B C D
T9B02 A B C D
T9B03 A B C D
T9B05 A B C D
T9B09 A B C D
T9B11 A B C D

## Slide 52: Chapter 4.4 Key
T3A03 A B C D
T3A05 A B C D
T7C02 A B C D
T7C08 A B C D
T7C09 A B C D
T7C10 A B C D
T7C11 A B C D
T7D08 A B C D
T7D09 A B C D
T9A01 A B C D
T9A03 A B C D
T9A04 A B C D
T9A05 A B C D
T9A06 A B C D
T9A07 A B C D
T9A08 A B C D
T9A09 A B C D
T9A10 A B C D
T9B04 A B C D
T9B06 A B C D
T9B07 A B C D
T9B08 A B C D
T9B10 A B C D