## Slide 1: Technician License Course Chapter 9 Safety

## Slide 2
Electrical Injuries
Shocks.
  30 V lowest dangerous
Burns.
Even small currents can cause problems.

## Slide 3
Electrical Safety
Avoiding contact is the most effective way of practicing electrical safety.
Most modern radio equipment uses currents that are not as dangerous as older equipment but precautions still must be taken.
Notes: Point out that since most modern equipment runs off of 12 volts, there are still dangerous levels of current, particularly in power supplies that convert 120 volts AC to 12 volt DC. The students still need to be cautious and vigilant around current.

## Slide 4
Mitigating Electrical Hazards
Turn off power when working inside equipment!
Make sure equipment is properly grounded and circuit protected!
Keep one hand in pocket when working around high voltage circuits.
Notes: The bottom line is use some common sense and avoid direct contact with current. Dangling hands, insulating shoes, knowing how components work and store energy are all good things to know and review when working inside equipment that is powered. Not the mention the damage that the operator can cause to equipment by probing around and shorting out parts of the circuit not intended to handle the level of current. Spend some time talking about battery safety. The current capacities of today’s batteries makes even more important to avoid short circuiting batteries.

## Slide 5
Mitigating Electrical Hazards
If power is required:
  Remove jewelry.
  Avoid unintentional touching of circuitry.
  Never bypass safety interlocks.
  Capacitors hold a charge even when power is off.
  Storage batteries are dangerous when shorted.
Notes: The bottom line is use some common sense and avoid direct contact with current. Dangling hands, insulating shoes, knowing how components work and store energy are all good things to know and review when working inside equipment that is powered. Not the mention the damage that the operator can cause to equipment by probing around and shorting out parts of the circuit not intended to handle the level of current. Spend some time talking about battery safety. The current capacities of today’s batteries makes even more important to avoid short circuiting batteries.

## Slide 6
Responding to Electrical Injury
REMOVE POWER!
  Have ON/OFF switches and circuit breakers clearly marked.
Call for help.
Learn CPR and first aid.

## Slide 7
Electrical Grounding and Circuit Protection (in the home)
Make sure your home is “up to code.”
Most ham equipment does not require special wiring or circuits.
  Use 3-wire power cords.
    Green is safety ground
  Use circuit breakers, circuit breaker outlets, or Ground Fault Circuit Interrupter (GFCI) circuit breakers or outlets
  Use proper fuse or circuit breaker size.
  Don’t overload single outlets.
Notes: It would be a good idea to show the students a properly wired 3-prong plug using proper color code wiring.

## Slide 8
Lightning Safety
Antennas are not struck any more frequently than trees or tall structures.
Ground all antennas. (short & direct with no sharp bends)
Use lightning arrestors.
  Ground all protectors to a common plate tied to external ground
Disconnect antenna cables and power cords during storms.
Disconnect telephone lines from computer modems.
Notes: Students should take precautions to mitigate the potential of lightning strikes but they should also be assured that their antennas pose no more of a risk than the trees and other tall structures in the area. Have on hand a lightning arrestor to show the students. Point out that lightning arrestors do not provide absolute protection form a strike. It is a good habit to disconnect antennas when the equipment is not in use. Many people forget that telephone lines and telephone poles are nice lightning rods and can be a source of lightning strikes that can take out equipment. Phone lines connected to computers provide a source for lightning to enter the home and other equipment connected to the household wiring.

## Slide 9
RF Exposure
Exposure to high levels of RF can cause problems.
RF is non-ionizing radiation.
If precautions are taken, RF exposure is minimal and not dangerous.
Problem is RF energy can heat body tissues.
  Heating depends on the RF intensity and frequency.
Notes: Point out to the students that RF exposure can cause harm, particularly heating of body tissues (much like happens in a microwave oven but to a far lesser extent), BUT, with simple precautions, the potential of harm is very small. It sounds stupid, but articulate a simple rule, don’t stand near an antenna, don’t touch an antenna, don’t put an antenna in your mouth when the transmitter is on.

## Slide 10
RF Intensity
Power Density
  Actual transmitter power.
    Higher power, higher risk.
  Antenna gain and proximity.
    Beam antennas focus available energy.
    Being physically close or standing in the beam direction increases risk.
  Mode duty cycle.
    The more time the power output is at high level, the higher the risk.
Notes: Here you will break down and discuss the two components of RF exposure, field intensity and frequency. Try to keep the discussion focused on the big picture, it is easy to get into details, charts and graphs, and using vocabulary of units that are very intimidating. Keep the big picture, know in general terms want influences RF exposure, and how to limit the exposure.
It makes sense that the more power you transmit, the more potential there is for harmful RF exposure. Assure the students that if they operate commercial, off-the-shelf equipment (which they probably will early in their ham radio careers) that the power levels are such that there will be little exposure danger.
Beam antennas focus the RF energy in desired directions, therefore standing close in the favored direction of the beam will increase the hazard.
Finally, spend some time talking about duty cycle…how much time the transmitter is at higher power levels while operating.

## Slide 11
Antenna Proximity
Controlled Environment.
  You know where people are standing in relation to your antenna and you can do something about it.
  More power is allowed because you can make adjustments if needed.
Uncontrolled Environment.
  You have no idea, or have no control of people near your antenna.
  Less power is allowed because you have to assume the worse case scenario.
Notes: Power limits are there to protect against exposure. Therefore if you have control of the antenna environment, you are allowed to run more power because you can take steps to limit exposure if required.
This is the example I use to explain the difference between controlled and uncontrolled environments and associated power restrictions. Consider a 2-meter mobile installation with an external antenna mounted on the trunk lid. RF exposure to the car’s occupant is mitigated by the metal in the car so that is not much of a concern. When the car is traveling down the highway, there is little risk that someone can get near or touch the antenna while transmitting, so it is a controlled environment and higher power can be used. If however, the car is parked in a crowded parking lot with lots of foot traffic, the operator is not assured that a pedestrian might not get close to the antenna, then this would be an uncontrolled environment and therefore allowable power levels is reduced.

## Slide 12
RF Exposure and Frequency
When body parts act like antennas, those parts absorb RF energy at certain frequencies (wavelengths) more efficiently and increase risk.
RF exposure risk varies with frequency.
  More caution is dictated at some frequencies more than other frequencies.
Notes: Basically some body parts act as antennas and when the wavelengths of the frequencies being used approximate the length of the body part exposed, risk increases. Operators need to be aware of this connection and adjust power levels and exposure potential accordingly to mitigate the risk.

## Slide 13
RF Exposure and Frequency

## Slide 14
Mode Duty Cycle
The more time the transmitted power is at high levels, the greater the duty cycle, and the greater the exposure risk.
Notes: Note here, that FM, the mode most used by new hams, is 100% duty cycle.

## Slide 15
RF Exposure Evaluation
All fixed stations must perform an exposure evaluation. Several methods are available to do this.
  Calculation based on FCC OET Bulletin 65
  Computer Simulation
  Measure field strenght
At lower power levels, no evaluation is required. Varies with frequency – example: below 50 W at VHF.
Relocating antennas is one way to reduce RF exposure
Also, regardless of the exposure evaluation results, make sure that people cannot come into contact with your antennas – RF burns are painful

## Slide 16
Physical Safety
Mobile Installations.
  Secure all equipment.
  Place equipment where you can operate it safely while driving
Notes: Make sure that equipment in cars is securely fastened so that it will not move around and create a hazard. Locate the controls of the equipment so that it does not present a hazard and distraction while driving.

## Slide 17
Physical Safety
Antenna installation.
  Clear of trees and power lines.
  If it falls it won’t hit anyone or cross within 10 feet of power lines.
  Towers should use proper grounding techniques.
Notes: Antennas generally need to be clear of obstacles and as high as practical. However, some common sense needs to be exercised to prevent antennas from becoming a safety hazard. Particular attention needs to be given to power lines and structure attachment points.

## Slide 18
Physical Safety
Tower climbing considerations.
  Proper clothing, hard hat and eye protection.
  Climbing harness.
  Gin pole: used for lifting tower sections and antennas.
  Don’t climb a crank-up tower supported by its cable.
  Don’t work alone.
Notes: Finally go over some precautions and safety considerations that must be taken if the students will be doing tower work. Most students will not be installing towers early in their ham careers, but they should be aware that special precautions should be taken and where they can review that information in the future.

## Slide 19: Quiz Time
Chapter 9

## Slide 20: Chapter 9 key
Section 9.1
T0A01 A B C D
T0A02 A B C D
T0A03 A B C D
T0A06 A B C D
T0A07 A B C D
T0A11 A B C D
T0A12 A B C D
T0A13 A B C D
T0B10 A B C D
T0B11 A B C D
Section 9.2
T0C01 A B C D
T0C02 A B C D
T0C03 A B C D
T0C04 A B C D
T0C05 A B C D
T0C06 A B C D
T0C07 A B C D
T0C08 A B C D
T0C09 A B C D
T0C10 A B C D
T0C11 A B C D

## Slide 21: Chapter 9 key
Section 9.3
T0B01 A B C D
T0B02 A B C D
T0B03 A B C D
T0B04 A B C D
T0B05 A B C D
T0B06 A B C D
T0B07 A B C D
T0B08 A B C D
T0B09 A B C D