## Slide 1
Technician License Course Chapter 2
Radio Signals and Waves

## Slide 2
The Basic Radio Station

## Slide 3
What Happens During Radio Communication?
Transmitting (sending a signal):
  Information (voice, data, video, commands, etc.) is converted to electronic form.
  The information in electronic form is attached or embedded on a radio wave (a carrier).
  The radio wave is sent out from the station antenna into space.

## Slide 4
What Happens During Radio Communication?
Receiving end:
  The radio wave (carrier) with the information is intercepted by the receiving station antenna.
  The receiver extracts the information from the carrier wave.
  The information is then presented to the user in a format that can be understood (sound, picture, words on a computer screen, response to a command).

## Slide 5
What Happens During Radio Communication?
This sounds pretty simple, but it in reality is pretty complex.
This complexity is one thing that makes ham radio fun…learning all about how radios work.
Don’t be intimidated. You will be required to only know the basics, but you can learn as much about the “art and science” of radio as you want.

## Slide 6
Radio Waves are AC
Radio waves (electromagnetic radiation) are ac waves.
All electromagnetic radiation travel at the speed of light in free space.
  300,000,000 meters/second
Radio waves are used to carry the information you want to convey to someone else.

## Slide 7
Wave Vocabulary
Before we study radio waves, we need to learn some wave vocabulary.
  Amplitude
  Frequency
  Period
  Wavelength
  Harmonics
Notes: Spend some time with live demonstration to make sure the students are really familiar with the concepts and vocabulary of waves. These demonstrations could include using audio frequency generator connected to a speaker and oscilloscope to allow students to hear a audio sine wave and see the wave. This will allow you to point out the differenced between amplitude and frequency, the relationship between frequency and wavelength, the relationship between frequency and period.

## Slide 8
Metric Units

## Slide 9
Finding Where You are on the Radio Dial
There are two ways to tell someone where to meet you on the radio dial (spectrum).
  Band
    usually approximate wavelength in meters
  Frequency
    Usually megahertz or kilohertz
    1 Hertz = 1 cycle per second

## Slide 10
Wavelength
The distance a radio wave travels during one cycle.
  One complete change between magnetic and electric fields.
Notes: This is the time to talk about the mathematical relationship between frequency and wavelength. Go over a few practice problems using examples of test questions. Give some problems for homework that are the test questions.

## Slide 11
Radio Frequency (RF) Spectrum
The RF spectrum is the range of wave frequencies which will leave an antenna and travel through space.
The RF spectrum is divided into segments of frequencies that basically have unique behavior.
Notes: Each segment division of frequencies will act the same, for instance, short range, reflect off similar surfaces, interact with the ionosphere the same way, etc.

## Slide 12
Radio Frequency (RF) Spectrum
Notes: Point out on the diagram where familiar signals are located like AM/FM commercial radio, police and fire channels, TV, satellite TV. Point out how each segment acts differently from adjacent segments. Don’t be afraid to tell them that it isn’t that simple, that the lines between segments sometimes are a little fuzzy, that is part of the fun of radio.

## Slide 13
So, Where Am I?
Back to how to tell where you are in the spectrum.
Bands identify the segment of the spectrum where you will operate.
  Wavelength is used to identify the band.
Frequencies identify specifically where you are within the band.
Notes: Give some real examples on how to articulate where to meet someone. I.e., I’ll be on 2 meters this evening, on a frequency of 146.52…see you there.
Twenty meters is open to Europe today, listen for the rare station on frequency 14.175 MHz.

## Slide 14
Another Use for Frequency and Wavelength
For the station antenna to efficiently send the radio wave out into space, the antenna must be designed for the specific operating frequency.
  The antenna length needs to closely match the wavelength of the frequency to be used.
  Any mismatch between antenna length and frequency wavelength will result in radio frequency energy being reflected back to the transmitter, not going (being emitted) into space.
Notes: Note that this statement is a generalization and there are a million exceptions. Just go with it for instructional purposes and point out that in the beginning, many over generalizations must be made to facilitate understanding. Once the student understands the basic concepts, then the true complexity of radio and in particular antenna theory can be explored.

## Slide 15
Adding Information - Modulation
When we imprint some information on the radio wave, we modulate the wave.
  Turn the wave on and off
  Voice -- AM and FM
  Data
Different modulation techniques are called modes.
Notes: You now need to make the jump from the discussion of radio spectrum and antenna resonance to the concept of modulation. The important concept here is understanding that modulation is imprinting information on the carrier radio wave. There are different ways to do this imprinting; those different ways are called modes.

## Slide 16
CW - Morse Code – On and Off

## Slide 17
Amplitude Modulation (AM)
In AM, the amplitude of the carrier wave is modified in step with the waveform of the information (voice).
Notes: The ARRL modulation board is an excellent resource that can be used to demonstrate the concept of modulation. This board uses amplitude modulation and demodulation circuits along with an oscilloscope to visually depict what happens during modulation.

## Slide 18
Characteristics of Voice AM
AM signals consist of three components:
  Carrier
  Lower sideband
  Upper sideband
Voice bandwidth is from 300 Hz to 3 kHz.
AM bandwidth is twice the voice bandwidth.

## Slide 19
Characteristics of Voice
Sound waves that make up your voice are a complex mixture of multiple frequencies.
When this complex mixture is embedded on a carrier, two sidebands are created that are mirror images.

## Slide 20
Single Sideband Modulation (SSB)
Since voice is made up of identical mirror image sidebands:
We can improve efficiency of transmission by transmitting only one sideband and then reconstruct the missing sideband at the receiver.

## Slide 21
Frequency Modulation (FM)
Instead of varying amplitude, if we vary the frequency in step with the information waveform – FM is produced.
FM signals are much more resistant to the effects of noise but require more bandwidth.
FM bandwidth (for voice) is between 5 and 15 kHz.
Notes: Discuss the concept of deviation, the amount of frequency change from the center frequency determines the volume of the transmitted information (percent modulation). Discuss what happens if you over deviate. Also discuss that FM can also be produced by varying the phase of the carrier, but this it is hard to distinguish between PM and FM so it isn’t particularly important for the new ham.
Here is a good place to talk about the advantages and disadvantages of the different forms of modulation.

## Slide 22: Modulation Bandwidth
CW < 150Hz
AM ~6 kHz voice ~10 kHz Music Broadcast
SSB ~ 2.6 kHz
FM Communications 5 – 15 kHz
  Also VHF packet
FM Broadcast 150 kHz
Television 6 MHz

## Slide 23: Modulation Selection
FM good for local strong signal communications
  Most VHF/UHF voice work including Reaters
  VHF/UHF Packet Radio
SSB good for long distance weak signal work
  Nearly all HF voice is SSB
  Use for VHF long distance weak signal voice
  Use LSB below 10 MHz USB above 10 MHz
CW will work for much weaker signals than SSB

## Slide 24: Frequency Readouts and Band Edges
The Law requires your entire signal to be within the band.
Therefore be careful when near the edge. Allow for:
  Calibration Error
  Modulation Sidebands
  Frequency drift
Example The top end of the 20 Meter band is 14.350 Mhz.
  A Ham on upper sideband operating on 14.349 MHz is out of band

## Slide 25
The Basic Radio Station

## Slide 26
Basic Station Organization
Station Equipment
  Receiver
  Transmitter
  Antenna
  Power Supply
Accessory Station Equipment
Repeaters
Notes: Go over with the students the basic outline of the material to be presented during this lesson. This lesson is deceptively simple because there is a lot of preparation required to make this lesson effective. You should try to set up an operational station to give some demonstration contact. Use some care that you don’t set up a station that will intimidate the students on the first day. Try to set up a station that would be typical of the type of station that they might set up in the beginning of their ham radio careers. Don’t spend a lot of time at this point demonstrating all the exotic modes available to the students, there will be plenty of time to do that later in the course. I would suggest a basic two meter set up and give demonstration contacts on repeaters and simplex. Then have a simple HF station and make one or two phone and one CW contact. Some advice on contact…don’t depend on a CQ being answered, it may or may not happen. I would suggest you have a few “planted” contacts from your club. These planted contacts are standing by on the frequency ready to step in and make a contact just in case your CQ goes unanswered. Try to get planted contact operators who are good at drawing out conversations on the radio. New operators are intimidated by radio and sometimes need to be prodded to say more than yes or no answers to questions.

## Slide 27
Special Stations You Will Use (Repeaters)
Repeaters are automated stations located at high places that receive and then retransmit your signal – simultaneously.
  Dramatically improves range.
The basic components of a repeater are the same as your station: receiver, transmitter, antenna and power supply.

## Slide 28
Repeaters
But, repeaters are transmitting and receiving at the same time using the same antenna.
This requires a very high quality and specialized filter to prevent the transmitted signal from overpowering the receiver.
This specialized filter is called a duplexer.

## Slide 29
Repeater

## Slide 30
Basic Station Accessories
Human interface accessories:
  Microphones
  Speakers
  Earphones
  Computer
  Morse code key
  TV camera
  Etc.
Station performance accessories:
  Antenna tuner
  SWR meter (antenna match checker)
  Amplifier
  Antenna rotator (turning antenna)
  Filters
  Etc.

## Slide 31
Accessory Equipment

## Slide 32: Quiz Time
Chapter 2

## Slide 33: Chapter 2 Key -1
T3B01 A B C D
T3B04 A B C D
T3B05 A B C D
T3B06 A B C D
T3B07 A B C D
T3B08 A B C D
T3B09 A B C D
T3B10 A B C D
T3B11 A B C D
T5B01 A B C D
T5B02 A B C D
T5B03 A B C D
T5B04 A B C D
T5B05 A B C D
T5B06 A B C D
T5B07 A B C D
T5B08 A B C D
T5C05 A B C D
T5C06 A B C D
T1B09 A B C D
T2B05 A B C D
T2B06 A B C D

## Slide 34: Chapter 2 Key -2
T8A01 A B C D
T8A02 A B C D
T8A03 A B C D
T8A04 A B C D
T8A05 A B C D
T8A06 A B C D
T8A07 A B C D
T8A08 A B C D
T8A09 A B C D
T8A10 A B C D
T8A11 A B C D
T1F09 A B C D
T4A02 A B C D
T4A07 A B C D